## Slide 1
Cambridge
    IGCSE
      Computer Science
      Paper 1
Boolean logic
Unit 3
Hardware
1

## Slide 2
Define the functions of NOT, AND and OR gates
Draw truth tables for each logic gate
Recognise a logic gate from its truth table
Recognise and use standard symbols used to represent logic gates
Objectives

## Slide 3
Binary situations
Binary situations are common in daily life and can refer to things that can be in only one of two states:
  Stop or Go
  Pass or Fail
  On or Off
In computing terms
  A binary 1 can represent TRUE
  A binary 0 can represent FALSE

## Slide 4
Output true or false?
Is the fridge door open?
  IF open then light = TRUE
  IF not open then light = FALSE

## Slide 5
Combining two conditions
Consider a safe with two keys
If both keys are used, the safe will open
  IF Key1 AND Key2 THEN Open = TRUE
  Otherwise, Open = FALSE

## Slide 6
True or false?
Unlocking a smartphone
Using a known fingerprint or
Using a correct PIN code?
  IF fingerprint OR correct PIN THEN unlock = TRUE
  Otherwise, unlock = FALSE

## Slide 7
If it’s not true, it’s false
Did you pass the test?
  IF NOT pass test = TRUE THEN pass test = FALSE
Or conversely,
  IF pass test = TRUE THEN NOT pass test = FALSE

## Slide 8
Boolean functions
AND, OR and NOT are Boolean functions
A computer can calculate the results of A AND B, A OR B, or NOT A depending on whether A and B are TRUE or FALSE
  What do these two circuit diagrams represent?
  How could you represent a Boolean NOT function?
Output
A
B
Input
Output
A
B
Input

## Slide 9
Truth tables
A truth table shows the output from all possible combinations of inputs from a Boolean function
If there are two inputs A and B, there are four possible combinations of TRUE and FALSE
  The truth table representing the AND function is shown below
Input A | Input B | Output P
FALSE | FALSE | FALSE
FALSE | TRUE | FALSE
TRUE | FALSE | FALSE
TRUE | TRUE | TRUE

## Slide 10
Number of inputs
How many possible outputs are there if there is just one input?
  What about if there are three inputs?
  Draw the truth tables representing OR and NOT
Input A | Input B | Output P
FALSE | FALSE | FALSE
FALSE | TRUE | FALSE
TRUE | FALSE | FALSE
TRUE | TRUE | TRUE
Input A | Output P
FALSE | FALSE
TRUE | FALSE

## Slide 11
Boolean function – AND
IF both inputs are TRUE then the output is TRUE
IF a lift is on the correct floor AND the Call button has been pressed THEN open the lift door
Lift on correct floor | Button Pressed | Open Lift Door
FALSE | FALSE | ?
FALSE | TRUE | ?
TRUE | FALSE | ?
TRUE | TRUE | ?
Lift on correct floor | Button Pressed | Open Lift Door
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?

## Slide 12
Lift on correct floor | Button Pressed | Open Lift Door
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?
Truth table – AND
IF both inputs are TRUE then the output is TRUE
A | B | P
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 13
Boolean function – OR
IF either input are TRUE then the output is TRUE
  IF either the cold tap OR the hot tap is turned on THEN water will start to flow
  What is P?
Cold tap on | Hot tap on | Water flows
FALSE | FALSE | ?
FALSE | TRUE | ?
TRUE | FALSE | ?
TRUE | TRUE | ?
A | B | P
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?

## Slide 14
Boolean function – NOT
IF the input is TRUE then the output is FALSE
IF the input is FALSE then the output is TRUE
  IF security beam is broken (FALSE) then the alarm is sounded (TRUE)
Beam broken | Alarm sounds
FALSE | ?
TRUE | ?
Beam broken | Alarm sounds
0 | ?
1 | ?
A | P
0 | ?
1 | ?

## Slide 15
More logic
Which of the following statements are TRUE?
(4 > 3) AND (5 > 7)
(2 < 8) OR (8 > 10)
NOT (5 * 7 > 30)
((7 div 3) >= 2) OR ((7 div 3) < 2)
((12 mod 5) < 2) AND ((12 mod 5) = 2)
  Mod gives the remainder after a division

## Slide 16
More logic
Which of the following statements are TRUE?
(4 > 3) AND (5 > 7) FALSE
(2 < 8) OR (8 > 10) TRUE
NOT (5 * 7 > 30) FALSE
((7 div 3) >= 2) OR ((7 div 3) < 2) TRUE
((12 mod 5) < 2) AND ((12 mod 5) = 2) FALSE

## Slide 17
Worksheet 1
Complete Task 1

## Slide 18
From truth tables to logic gates
Physical computer circuits are built using logic gates
The first three fundamental gates used to build circuits are:
  AND gate
  OR gate
  NOT gate

## Slide 19
Binary logic – AND gate
If both inputs are 1 (TRUE) then the output is 1 (TRUE)
Otherwise the output is 0 (FALSE)
Logic Diagram
Truth Table
INPUT
A
INPUT
B
OUTPUT
P
Logic statement: P = A AND B
A | B | P
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?

## Slide 20
Binary logic – AND gate
If both inputs are 1 (TRUE) then the output is 1 (TRUE)
Otherwise the output is 0 (FALSE)
Logic Diagram
Truth Table
INPUT
A
INPUT
B
OUTPUT
P
Logic statement: P = A AND B
A | B | P
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 21
Binary logic – OR gate
If either input is 1 (TRUE) then the output is 1 (TRUE)
Otherwise the output is 0 (FALSE)
Logic Diagram
Truth Table
INPUT
A
INPUT
B
OUTPUT
P
Logic statement: P = A OR B
A | B | P
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?

## Slide 22
Binary logic – OR gate
If either input is 1 (TRUE) then the output is 1 (TRUE)
Otherwise the output is 0 (FALSE)
Logic Diagram
Truth Table
INPUT
A
INPUT
B
OUTPUT
P
Logic statement: P = A OR B
A | B | P
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 23
Binary logic – NOT gate
If 0 is input it outputs 1 (TRUE)
If 1 is input it outputs 0 (FALSE)
Logic Diagram
INPUT
A
OUTPUT
P
Logic statement: P = NOT A
Truth Table
A | P
0 | ?
1 | ?

## Slide 24
Binary logic – NOT gate
If 0 is input it outputs 1 (TRUE)
If 1 is input it outputs 0 (FALSE)
Logic Diagram
Truth Table
A | P
0 | 1
1 | 0
INPUT
A
OUTPUT
P
Logic statement: P = NOT A

## Slide 25
Worksheet 2
Complete Task 2, Questions 11-13

## Slide 26
Combining logic gates
We can string logic gates together to make more complex circuits
INPUT
A
OUTPUT
R
OUTPUT
P
Logic statement:
P = NOT (A AND B)
INPUT
B
A | B | R = A AND B | P = NOT R
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 27
Combining logic gates
We can string logic gates together to make more complex circuits
INPUT
A
OUTPUT
R
OUTPUT
P
INPUT
B
Logic statement:
P = NOT (A AND B)
A | B | R = A AND B | P = NOT R
0 | 0 | 0 | 
0 | 1 | 0 | 
1 | 0 | 0 | 
1 | 1 | 1 | 

## Slide 28
Combining logic gates
We can string logic gates together to make more complex circuits
INPUT
A
OUTPUT
R
OUTPUT
P
INPUT
B
Logic statement:
P = NOT (A AND B)
A | B | R = A AND B | P = NOT R
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 29
Modelling real life – security Light
What would the circuit diagram for this situation look like?
  The security light must come on if it senses movement AND it is night time, OR if someone presses a manual override switch

## Slide 30
Modelling real life
Sensor detects
movement = TRUE
AND
Night time
= TRUE
OR
Manual override
Button = TRUE
=
Security
Light On
Security
Light
On
TRUE (1)
TRUE (1)
TRUE (1)
TRUE (1)
TRUE (1)
Sensor detects
Movement = TRUE
Night time = TRUE
Manual override
Button = TRUE

## Slide 31
Worksheet 1
Complete Task 3, Questions 14-16