## Slide 1
2
AQA
    A Level
      Product Design 7552
Applications of polymers
Unit 2 Performance characteristics of polymers

## Slide 2
Be able to explain the difference between thermoplastics and thermosets
To be familiar with a range of different thermoplastics and thermosetting polymers with specific reference to appropriate applications
Objectives

## Slide 3
Classification of polymers
There are two main types of polymers, which react to heat in different ways and have different molecular structures:
  Thermoplastics
  Thermosets
  Which type is most likely to have been used to make this child’s toy car and play people?
  Discuss the characteristics of the thermoplastics and thermosets

## Slide 4
Polymer variations
There are synthetic polymers and natural polymers
  Synthetic polymers are produced from finite resources such as coal, gas and oil
  Natural polymers come from a variety of sources such as rubber and amber, which come from trees

## Slide 5
Refining crude oil
Fractional distillation occurs when crude oil is heated in the crude oil distillation unit
  Each product has different sized molecules with different boiling points
  Different types of polymers are made from the different fuels

## Slide 6
Cracking
This is the process of converting the large hydrocarbon molecules found in the separated fuel types into smaller, more useful versions
  The large molecules do not flow very well and are not suitable to be converted into plastics
  Heat and pressure are used to break them up

## Slide 7
Polymerisation
After hydrocarbons are obtained from cracking, they are then chemically processed:
  Molecules of single compounds known as monomers join together
  These atoms are joined end to end to form long chains
  The long chains of molecules are called polymers
  MONO (one)    POLY (many)
  Polymers are the building blocks of all plastics

## Slide 8
Thermoplastics
Thermoplastics are the most commonly used plastic
  They have long chains of molecules, tangled together with no fixed structure or pattern
  They are generally soft and flexible with some shape memory

## Slide 9
Thermoplastics cycle
Thermoplastics can be formed using heat and reshaped many times without changing properties
  What are the environmental implications of thermoplastics being able to be heated and reshaped?

## Slide 10
HDPE
High-density polyethylene HDPE is tough and has a higher strength to weight ratio than LDPE
  HDPE is commonly used for bottles and drums containing chemicals, rigid plastic toys, storage boxes, buckets, garden bins and bags for life
  It is sometimes simply referred to as ‘polythene’
  HDPE is harder than LDPE but also has good chemical resistance

## Slide 11
Rigid PVC
Polyvinyl chloride (PVC) is one of the most widely used polymers and can be both rigid and flexible
  Rigid PVC is tough, hard and commonly used for plumbing pipes as well as guttering and down pipes
  Additives can be used to increase fire retardancy
  It has good chemical and weather resistance
  uPVC is used to make the sections used for window frames and external doors

## Slide 12
Flexible PVC
Plasticisers are added to PVC to increase flexibility
  Flexible PVC has a range of applications from hose pipes and electrical insulation to inflatable products, clothing and upholstery as an alternative to leather
  Flexible PVC is water resistant
  It has good chemical resistance
  What properties make flexible PVC an idea material for wire shielding and electrical tape?

## Slide 13
LDPE
Low density polyethylene (LDPE) is derived from ethylene – it is quite flexible, but also tough
  LDPE is used in packaging where flexibility is required like squeezy bottles and snap on lids, carrier bags and toys
  It can be either translucent or opaque
  Has excellent resistance to chemicals
    LDPE film is also combined with board and aluminium foil to make packaging laminates
    What applications are these materials used for?

## Slide 14
PP
Polypropylene (PP) is a tough, flexible polymer with excellent fatigue resistance
  Applications include food packaging, medical equipment, hinged lids, moulded furniture and rope
  It is available in translucent form and in a range of colours
  PP is resistant to chemicals and solvents
  PP is commonly used for boat rope – Why do you think it is an ideal material for this application?

## Slide 15
HIPS
High Impact Polystyrene (HIPS) is a rigid lightweight polymer with high impact strength
  HIPS is food safe and commonly used for yoghurt pots, cutlery and salad bowls, some single use coffee cups, plastic cutlery and transparent casings
  It has the ability to retain heat without deformation
  It has a glossy appearance
  What property makes HIPS ideal for use in disposable or single use plastic products?

## Slide 16
PMMA (acrylic)
Polymethyl methacrylate (PMMA) is more commonly known as acrylic and is a tough lightweight material
  Its clarity in transparent form means it is often used as a lightweight shatter-resistant alternative to glass and is also used for shower trays, baths, car lamp covers and lenses in glasses
  It can be a clear plastic but is available in a very wide range of colours
  It has relatively poor resistance to chemicals compared to many polymers
  What trade names is acrylic commonly known by?

## Slide 17
ABS
Acrylonitrile Butadiene Styrene (ABS) is hard and tough with excellent impact strength
  ABS is widely used for domestic appliance casings, computer screen housings, rigid suitcases, safety helmets, car bumpers and wing mirrors
  ABS has very good resistance to acids, alkalis, oils and grease
  It is easily moulded with a high quality surface finish which can be painted
  Why would ABS be an appropriate material for a musical instrument case?

## Slide 18
Nylon
Nylon was the first commercially successful thermoplastic polymer
  Nylon is used for mechanical components such as machine screws and gears as well as woven textiles such as rope, parachutes, tents, seat belts and carpets
  Nylon has a low coefficient of friction
  It’s durable and resistant to abrasion
  It is heat resistant
  What properties make it idea for use in bearings?

## Slide 19
Thermosetting plastics
Known as condensation polymerisation because each time two monomers form a bond a small molecule of water is produced
  The long chains of molecules are cross-linked and form a very rigid molecular structure when thermosets are cured, usually with a chemical catalyst causing it to harden
  This reaction is exothermic and generates heat

## Slide 20
Thermosets
Thermosets are more brittle than thermoplastics and are best suited to stiffer mouldings
  They are very hard and waterproof when solid, making them ideal for use as adhesives
  Thermosets are more difficult to mould and cannot be reheated and reshaped
  They retain their shape well at high temperatures
  Are all thermosets self-finishing?

## Slide 21
Urea formaldehyde (UF) is a hard, opaque resin made from urea and formaldehyde, a naturally occurring organic compound
  UF is used as an adhesive to bind materials such as MDF and plywood and as a moulded resin in electrical casings, socket and switches
  UF has good resistance to deformation by heat
  UF has a high tensile strength
  What properties make UF an ideal material for use in 3-pin plug casings?
UF

## Slide 22
MF
Melamine formaldehyde (MF) is a hard, scratch resistant, opaque polymer
  It is often used to create surface coatings and decorative laminates as well as picnic ware, toilet seats, kitchen utensil handles and buttons
  MF has good resistance to heat and chemicals
  What may happen to a melamine formaldehyde cup if dropped on a hard floor and why?

## Slide 23
Polyester resin
Polyester resin is the most common form of resin used in the marine industry
  Polyester resins are used to produce glass reinforced plastic (GRP) boat hulls, bath tubs and chair seats, by coating chopped strand matting a process called laying up
  To cure, the resin base must be mixed with a catalyst
  Polyester resins are resistant to water, heat and chemicals
  What techniques are used during a lay-up to achieve a high quality finish?

## Slide 24
Epoxy resin
Epoxy resin is a clear resin that also needs to be mixed with a catalyst to cure
  It is hard and tough and is commonly used as an adhesive to join dissimilar materials, as a surface coating and for encapsulating electrical components like LEDs
  It maintains its integrity at high temperatures
  It has good chemical resistance
  Why might epoxy resin be used instead of polyester resin in laying up carbon fibre reinforced plastic?

## Slide 25
Plenary Task
Complete the Plenary Task on your Worksheet