## Slide 1
4
AQA
    A Level
      Product Design 7552
Design communication
Unit 12 Product design and development

## Slide 2
Explain and demonstrate a range of communication and presentation techniques for conveying proposals and intentions to others
Objectives

## Slide 3
Starter
What is design communication?
  How are design intentions conveyed to others?
  What are the advantages of using visuals over spoken or written words?
  People say ‘a picture speaks a thousand words’
  What does this mean?

## Slide 4
Clear communication
Whether generated by hand or using CAD software, various visual tools are used to simplify complex information
  Colors and textures
  Pictograms and symbols
  Images, shapes and emoji’s
  Words and fonts
These tools make up a kind of visual shorthand that users can decode

## Slide 5
Worksheet task
Complete Task 1 of Worksheet 4

## Slide 6
Presenting ideas and intentions
You must be able to explain and demonstrate your design ideas through a variety of different communication techniques
  2D and 3D sketches
  Mixed media and rendering
  Technical drawings and dimensions
    Would you convey your ideas to a client and a manufacturer in the same way?

## Slide 7
Data vs ideas
Communicating data and communicating ideas are very different skills
  What are the top priorities when visualising data?
  What do you aim for when communicating initial ideas?
  What is the purpose of a final presentation drawing compared to development sketches?
  How are technical drawings used?

## Slide 8
Sketching techniques
Whether hand drawn or computer generated, various 2D and 3D methods are used to develop and communicate ideas
  3D drawings are better for representing the look and feel of an object
  2D drawings show profiles, dimensions, mechanical and electrical concepts
  Which of these would be more useful to a client?

## Slide 9
3D drawing techniques
Graphical projection and perspective are useful drawing skills for presenting designs
  There are three key types of 3D drawing styles:
    Oblique projection
    Isometric projection
    Perspective drawing
What are the key differences between isometric and perspective techniques?

## Slide 10
Oblique projection
Oblique projection is a simpler technique and useful in the early stages of design
  What are the problems with oblique projection?

## Slide 11
Isometric projection
Isometric projection enables designers to draw an object in three dimensions which aids visualisation
  All lines are drawn at a 30° angle away from the nearest corner of the object and accurate measurements can be added

## Slide 12
One-point perspective sketch
This is one of the simplest styles, that you may sketch in a notebook, however its use is limited

## Slide 13
One-point perspective
If you look square onto an object, it appears to get smaller & converge towards a single vanishing point
  Perspective drawing looks more realistic as it emulates this

## Slide 14
Two-point perspective
Two point uses two vanishing points, so shapes that project towards them appear smaller
  This vanishing effect simulates the natural way we observe objects
  A rule can be used to draw the main structure with freehand sketching to add detail and curved forms

## Slide 15
Two-point perspective
Does this look more realistic than oblique or isometric projection?

## Slide 16
Three-point perspective
This can give a dynamic effect to a composition and makes concepts more interesting
  All the vertical construction lines will end at the third vanishing point
  The nearer the third vanishing point to the centre of the drawing, the greater the distortion
  This can create an extreme point of view which can make for a striking effect in architectural design

## Slide 17
Three-point perspective
Where are the three vanishing points?

## Slide 18
Mixed media and rendering
Drawings can be embellished further with colour, tone and shadows to create depth, texture and show surface finishes
  Mixed media representations can combine pen, pencils, spirit markers, chalk and water colour
  Using spirit based markers to build up layers of colour is the traditional way designers render their work
  Increasingly, CAD packages can achieve similar effects more rapidly in a more versatile format, making alterations and different colour schemes and finishes

## Slide 19
Presentation drawings
Use of rendering and mixed media brings an idea to life
  Why is this important when showing ideas to clients?

## Slide 20
Technical drawing
Once ideas are finalised, dimensions and assembly details must be communicated to the manufacturer
  Technical, or working, drawings give practical details to enable a product to be manufactured
  Orthographic projection, cross-sectional and exploded views are ideal for this stage of design development

## Slide 21
3rd angle orthographic drawing
Orthographic drawings typically include three 2D views – the plan, front and side elevations
  What does the symbol in the bottom corner show?

## Slide 22
Dimensions and conventions
Set standards and conventions for technical drawing make it easier to convey ideas
  Line styles and symbols are used for different features e.g. hidden, solid or central features
  Datum points set points on a drawing from which several dimensions are taken – where is the datum point below?
  Why do these conventions make it easier to convey ideas?

## Slide 23
Worksheet task
Complete Task 2 of the Worksheet

## Slide 24
Built to scale
Orthographic drawings are invaluable to the anyone involved in the manufacture/build phase of a project
  Standard conventions are used in these drawings to show dimensions and structural details clearly with minimal text
  They are drawn to scale – what does this mean and why is it useful?

## Slide 25
Sectional drawings
These truncate an object at a given point to show internal features that are otherwise hidden from view
  Sectional views may be incorporated into a 3D view or separately in 2D
  Again, these are essential for communicating ideas between designers and manufacturers
  They can also be used with clients and customers to highlight interesting or unique features
  Hatched sections show solid material and dotted lines show hidden features

## Slide 26
Exploded views
An exploded drawing shows how component parts of a product are assembled
  Components are aligned so its easy to show where each part fits together
  Extensively used for flat pack furniture assembly instructions or manuals supplied with kit models

## Slide 27
Make or break
In summary, technical drawings like these are vital to take a product from a concept to reality
  They allow material quantities and costs to be calculated and demonstrate how a product and its components interact
  They ensure equipment can be set up accurately and within tolerance to produce safe, high quality products that are fit for purpose

## Slide 28
Worksheet task
Complete Task 3 of the Worksheet

## Slide 29
Plenary
Suggest a suitable drawing method for each of the following:
  Layout of seating for a new restaurant
  Internal structure of an engine part
  Final design to pitch to potential investors
  Explain a design to a manufacturer for injection moulding