## Slide 1
2
AQA
    A Level
      Product Design 7552
Inclusive design
Unit 11 Product design considerations

## Slide 2
Understand how products are developed to be inclusive in their design
Understand how products are designed for a wide range of users including the disabled, children and the elderly
Objectives

## Slide 3
Starter
Big button phones are designed to make use easier for a target market
  Discuss which features of this handset make it suitable for elderly and disabled users
  How have the designers tried to balance form and function?
  Do you think the design would put off any particular group of users?
Now complete the Starter activity on Worksheet 2

## Slide 4
Worksheet 2
Complete the Starter activity on Worksheet 2

## Slide 5
Inclusive design
British Standards Institute (2005) defines inclusive design as:
  The design of mainstream products and/or services that are accessible to, and useable by, as many people as reasonably possible… without the need for special adaptation or specialised design

## Slide 6
Inclusive vs exclusive
Designers must be aware that the design decisions they make, may include or exclude certain user groups and therefore they should
  understand the diversity of their potential user groups
  be aware of variations in capability and need
  make informed decisions
  Small changes can make a significant difference
  Give an example of where you have seen inclusive design in practice

## Slide 7
Everyday tools
Consider the potato peeler throughout history
  The way it has been used and the people who used it have influenced its design and function
  Paring knives
  Straight peelers
  Spiral peeler / corers
  Swivel peelers
  ‘Y’ peelers
    What social changes do you think may have prompted greater consideration of the design of the potato peeler?

## Slide 8
Oxo Peeler
This peeler is designed in response to some specific user needs, to be a more inclusive utensil
  Designers often take user frustration and feedback as a starting point for design improvements and new designs
  What design details have been integrated to achieve this and how will they help the user?
  Who will find using it easier as a result of these changes?
  Which users might find it more difficult and why?

## Slide 9
Built environments
Public buildings are required to provide safe, easy and inclusive access for all people regardless of disability, age or gender and include:
  Access up to, into and within a building and its facilities
  Access to public transport provision
  Appropriate car parking

## Slide 10
Principles
The Commission for Architecture and the Built Environment (CABE) promote the principals of inclusive design as:
    Inclusive
    Responsive
    Flexible
    Convenient
    Accommodating
    Welcoming
    Realistic

## Slide 11
Worksheet 2
Complete Task 2 of Worksheet 2

## Slide 12
Feeling the way
Subtle ergonomic changes and improvements to existing designs can immediately include a whole new user group
  Incorporating recognised textures or relief symbols enables visually impaired users to navigate within the built environment
  Name the tactile writing system used by people who are visually impaired

## Slide 13
Tactile warnings
Grids of tactile studs can be laid into surfaces including pavements and platforms
  They alert blind and visually impaired people about imminent danger
  Warn of surface or level changes
  Provide directional instructions
New and exciting smart technologies are now being developed to fulfil a similar role

## Slide 14
Sounding out ideas
People with hearing impairment or total hearing loss similarly have specific needs that can be met through good, thoughtful design and improvement
  Hearing aids are getting smaller, more efficient and customisable
  Communication devices offer voice to text facilities
  What products use sound as an alert or a warning?
  How could these be adapted to meet the needs and ensure the safety of a deaf or hearing impaired person?

## Slide 15
Empathetic design
It is always going to be a challenge for a designer to thoroughly understand the challenges of a user with specific needs
  Gloves have been designed to simulate reduction in the ability of movement in the hands, replicating issues faced by those who suffer with arthritis
  These allow designers to empathise with the problems their clients face and design products with a better understanding of these needs

## Slide 16
Flexibility
The needs of a user may change over time, for example, toddlers have specific needs which change as they grow up
  Flexibility can increase inclusivity
  An adjustable product will be open to a wider range of users
  Longevity of the product is also money saving
  What addition could be made to this adjustable chair to help improve safety of younger users?

## Slide 17
Risks of bad design
Everyday, bad designs cause confusion
  The US Department of Treasury was taken to court when it was found that visually impaired citizens could not distinguish between the denominations of the newly released bank notes
  In response designers created a currency denomination reader called iBill which is issued to visually impaired citizens
  What features have been added to the new £5 and £10 notes to help visually impaired users discriminate between denominations?

## Slide 18
Repercussions
Unfortunately, the repercussions of bad design or the lack of inclusivity in design can be much more serious
  Certain user groups are discriminated against
  Certain user groups may be put in danger
  Certain user groups feel excluded
  Discuss situations in which alternative options can be deployed to increase inclusivity and accessibility

## Slide 19
Improving designs
Complete Task 3 of Worksheet 2

## Slide 20
Is the extra mile that far?
If designers incorporate the principals of inclusive design into everything they do ‘inclusive design’ becomes ‘design’
  Inclusive design is universal design which benefits everyone
  Inclusive design is good design
  Inclusive design can change lives
  In what ways do you think that you have benefitted from inclusive design in day to day life?