## Slide 1
6
AQA
    A Level
      Product Design 7552
Efficient manufacturing techniques
Unit 11 Product design considerations

## Slide 2
Be aware of, and able to explain, the different ways in which a product can be designed to allow for more efficient manufacture
Objectives

## Slide 3
Ease of manufacture
Discuss the term ‘efficient manufacture’
  Consider productivity, costs, resources and waste
  How can manufacturing be made more efficient?
  How does efficiency facilitate ease of manufacture?

## Slide 4
Efficient manufacture
To increase efficiency, companies regularly use data to evaluate operations, this helps them to:
  reduce waste, pollution and use of raw materials
  minimise environmental impact
  maximise productivity
  maximise output
  maintain quality
  reduce costs
    Why may companies also explore alternative resources, materials, manufacturing techniques and aids?

## Slide 5
Efficient design
There are various design strategies that can be used to increase the ease and efficiency of manufacture; these include:
  designing to reduce material thickness
  designing integrated fittings
  using pre-made components
  working to standardised sizes
  In what way could adding texture to a moulded part, as opposed to applying a finish, reduce the number of manufacturing processes used?

## Slide 6
Reducing thickness
Reducing the weight and thickness of materials used saves resources and lowers costs
  This must be done whilst maintaining the strength and integrity of the part or product
  The thickness of materials used can be reduced if ribs or webs are incorporated into the design to ensure rigidity and the overall strength of the material
  What products can you identify as using ribs or webs in this way?

## Slide 7
Ribs
Ribs can be used with a number of materials and may be created in different ways
  Ribs may be integrated into a material by pressing, moulding, folding or weaving
  In some cases ribs of a stronger or more rigid material may be added to thin sheet to increase strength and create structure
  What other materials can be ribbed to reduce thickness, weight and increase strength?

## Slide 8
Webbing
Webbing is a term used to describe the reduction of material thickness by using integrated gussets and webs to strengthen and support a structure
  In plastic products they are often created by injection moulding, whilst in metal products they may be cast or machined
  They may also be fabricated or moulded by laying-up
  Why is a webbed lid preferable to a flat solid lid when used for a plastic storage box like the one pictured?

## Slide 9
Worksheet 6
Please complete Task 1 of Worksheet 6

## Slide 10
Integrated fixings
Removing the need for fixings or adhesives reduces the numbers of parts and processes, which in turn saves time and cost and increases recyclability
  Snap fitting parts, also called push-fit, are often moulded and feature integral clips or ridges that ‘snap’ into place when pushed
  Snap fittings are usually detachable
  Snap fittings enable rapid assembly and disassembly
  In what common products may you find snap fittings?

## Slide 11
Types of snap fitting
There are four main types of snap fitting types, each achieving a closure or mating in a different way
  Cantilever
  Annular
  Torsion
  U-shaped
    In what ways does the fastening on this fitness tracker differ from that of a conventional watch?

## Slide 12
Cantilever snap fitting
The cantilever snap fitting is widely used in a number of everyday products
  This design incorporates a cantilevered beam or beams which allow deflection in order for the tang at the end to locate
  In a multiple use fixing the tang must be able to be accessed so that pressure can be applied to enable removal
  A cantilever snap fitting meant for one-time use will feature a sharply angled tang – How does this create a permanent fixing?

## Slide 13
Annular snap fitting
Annular snap fittings are multi-use and used in products like press fit pen, cup and bottle caps
  They work by a method known as ‘hoop strain’ where a more elastic part is pushed onto a more rigid part
  A ridge on the male part mates with a gully in the female part
  Annular snap fittings are usually circular however a ball and socket joint is also an annular fixing
  What may happen to an annular fixing with frequent use?

## Slide 14
Torsion snap fitting
Torsion snap fittings are more complex and less widely used however they are suited to applications where regular opening and closing is required
  Acting as a catch, torsional fixings have a pivot point and hinge which allows them to open when pressure is exerted
  They may also have a spring enabling them to snap closed when released
  Shear force is exerted to open the fixing much like one half of a spring clamp

## Slide 15
U-shaped snap fitting
A variation of the cantilever fitting, U-shaped snap fittings are commonly used in closures included those used in battery housings
  The U-form increases the length of the beam and creates a spring allowing greater deflection
  This shape is often used where materials are less flexible
  How is this form of snap fitting usually operated?

## Slide 16
Internal moulded screw posts
Where snap fittings are not appropriate, products that require occasional assembly and disassembly may use internally moulded screw threads/posts
  Commonly used in electrical and electronic product casings
  They enable easier disassembly
  They are easy and economical to manufacture in a single mould
  They are designed for use with self-tapping screws. Why must caution be taken when tightening this type of fitting?

## Slide 17
Worksheet Task
Complete Task 2 of your Worksheet

## Slide 18
Pre-made components
Many manufacturers purchase standardised components from external suppliers to use in the production of their products
  This allows them to circumvent many costs involved in manufacturing specialist parts in-house
  By taking advantage of other companies facilities and specialisms, they can ensure a high quality product
  What issues could arise as a result of buying in pre-made parts?

## Slide 19
Standard Patterns
Patterns and templates in standardised sizes are used when designing and making a range of products including garments
  Body forms are used to create patterns in different fits and sizes for commercial clothing manufacturers and the home seamstress
  Using standardised sizing in patterns ensures consistency, however body shapes vary and adjustments can be made when sewing at home
  Some commercial clothing manufacturers and brands use ‘vanity sizing’
  Why is this used and what problems can this cause?

## Slide 20
Textured moulds
Textures can be both functional and used to enhance the aesthetics of a product
  Improving grip, creating lettering and logos and simulating other materials such as leather and woodgrains
Using a mould surface to achieve a textured moulding is another way of increasing efficiency
  The finish is integrated into the moulding or casting process removing the need for additional finishing
  What methods are used to create textures on mould surfaces?

## Slide 21
Self-finishing
Using self-finishing materials such as polymers is another way manufacturers reduce the number of additional processes required and:
  to enhance the appearance of part or product
  to ensure a product is safe
  to protect the material
It reduces overall manufacturing time and costs, increasing output
  What other materials could be considered self-finishing?

## Slide 22
Worksheet Task
Please complete Task 3 of your Worksheet

## Slide 23
How efficient?
Discuss the ways in which this polymer laundry ball has been manufactured with efficiently in mind