## Slide 1
7
AQA
    A Level
      Product Design 7552
Design for disassembly
Unit 11 Product design considerations

## Slide 2
Be able to explain how a product can be designed and manufactured with disassembly in mind
Understand how integral fixings are designed into products to aid disassembly
Know how active disassembly is achieved using smart materials and biodegradable components
Objectives

## Slide 3
Breaking it down
Discuss why is it important for a product to be able to be disassembled easily
  What factors affect the ease with which a product may be disassembled?
  Which factors inhibit simple disassembly?

## Slide 4
The need for ease
Ease of disassembly is important as it ensures:
  easier analysis of products for research and development
  easier maintenance, repair and reuse of components
  easier recycling and consequently a reduction in the use of virgin materials and resource depletion
  an increase in the value of end-of-life products
  a reduction in the need for specialist breaking and sorting facilities
  fewer parts and products going to landfill

## Slide 5
The challenge
In recent decades, developments in manufacturing and technology have resulted in the shortening of expected product lifespans
  This has led to a greater number of products going to landfill
  In what way has consumer demand contributed to this trend?
  Why do electrical and electronic products pose a particular challenge when it comes to disposal at the end of their useful life?

## Slide 6
Scrappage
Historically scrap vehicles have been stripped down or broken so that metals and other materials & parts of value could be retrieved and sold or reused
  This type of reclamation only retrieved the parts of value
  It was often a brutal process as cars were not designed with disassembly in mind
  In recent years systems have been developed to allow more comprehensive breaking, reclamation and recycling

## Slide 7
Disassembly
Disassembly is the process used to retrieve parts, components and materials for reuse and recycling
  In recent years, there has been a focus by designers to reduce the number of parts and components in a product
  Manufacturers are now obliged to consider the ease with which their products are broken down and processed at end of life
  What strategies might designers employ to reduce the number of parts used in the products they design?

## Slide 8
Design for disassembly
Designers use various strategies in order to reduce parts and for ease of disassembly, these include:
  Prioritise materials and parts that can be reused or recycled
  Selection of appropriate manufacturing methods
  Integrating fixings or simplifying joining methods for quick disassembly
  Incorporating smart and biodegradable materials in anticipation of end-of-life

## Slide 9
Material Selection
Materials should be chosen for ease of disassembly and processing at end-of-life without compromising the structural integrity of the product
  Ease of manufacture must be considered including the potential to integrate fixtures and finishes
  Ultimately, disassembly can be made easier by using fewer materials per product
  What methods are used to identify many materials used in products and parts?
  Indicate their potential for recycling

## Slide 10
Integration
Incorporating fittings and fixtures within a product, part or moulding enables quicker and easier disassembly
  Reducing the amount of time it takes to dismantle a product
  Reducing the number of separate fixings, fasteners and parts required
  Avoiding the need for adhesives which can cause problems when separating materials
  Where integrated fittings and fixtures are not viable, what type of fastenings enable easy disassembly using simple hand tools?

## Slide 11
Reduction
A designer may seek to minimise the number of different materials, parts and processes used
  This makes disassembly easier and less time consuming
  Facilitates easier recognition of material types and enables materials to be sorted for reuse or recycling
  Ultimately, the fewer parts used the higher the likelihood of disassembly and the lower the likelihood of a product ending up in landfill

## Slide 12
Worksheet 7
Complete Tasks 1 and 2 of your Worksheet

## Slide 13
What to avoid
To produce sustainable products that are serviceable, easy to disassemble and recycle there are some things manufacturers should actively avoid
  Using a large number of parts and different types of materials
  The use of irreversible adhesives in laminations and joints
  Adding paints and finishes that contaminate materials
  Using a range of different types of fixings
  Use of any hazardous materials
  Integrated batteries

## Slide 14
Automated disassembly
Liam is a robot designed by Apple to fully disassemble an iPhone in 11 seconds
This enables materials and parts to be recovered including
  Components
  Precious metals
  Heavy metals
  Minerals
  Fixings

## Slide 15
Active disassembly
Active disassembly involves the use of smart materials to speed up the disassembly process including:
  Shape memory alloys (SMA)
  Shape memory polymers (SMP)
This is known as active disassembly using smart materials or ADSM
    What possibilities do shape memory alloys offer to the process of disassembly?

## Slide 16
Shape Memory Alloy (SMA)
Smart materials are used for active disassembly, as they can deform or experience a change in shape under the influence of an external stimulus
  SMA fixings can be activated at end-of-life by direct heat or by using an electric charge
  This may cause the fixing to open, deform or disengage enabling easier disassembly
  Screws and bolts can be designed to loose their threads
  How could this be used in the disassembly of electronic products?

## Slide 17
Potential benefits of ADSM
ADSM is still development however there are clear advantages to its use in the disassembly of products
  It doesn’t damage parts, enabling them to be used again
  It could enable the disassembly of products with many small, fiddly parts
  Using SMA and SMP fixings could make the disassembly process faster and more efficient, reducing the number of products and components sent to landfill
  Active disassembly using smart materials effectively increases end-of-life recycling rates for electronic products

## Slide 18
Worksheet Task
Please complete Task 3 of your Worksheet

## Slide 19
Biodegradable parts
Designers are always seeking new and innovative ways of making parts and products that cause little or no impact on the environment
  Some products are now made from natural starch-based biopolymers like PHA, bamboo and even compressed paper pulp
  These are compostable and given the right conditions, a combination of the bacteria in the earth and heat, they will break down and assimilate safely
  What parts of the eco toothbrushes pictured are biodegradable and what might they be made from?

## Slide 20
Innovative producers
Evoware is an Indonesian enterprise that aims to provide innovative solutions to the problem of plastic waste from packaging products by using a seaweed-based material that:
  dissolves in warm water
  is available in both 100% biodegradable and edible forms
  If stored properly, this material will last up to two years
  What type of products could a material like this be incorporated into?

## Slide 21
Worksheet Task
Please complete Task 3 and 4 of Worksheet 7

## Slide 22
Based on the strategies you have explored during the lesson, discuss how this product was designed with ease of disassembly in mind
How might it be improved?
Taking it apart