## Slide 1
AQA
    AS Level
      Computer Science
      Paper 2
Assembly language
  Unit 5
  Computer organisation and architecture

## Slide 2
Objectives
Use basic machine code operations expressed in mnemonic-form assembly language
Understand and apply immediate and direct addressing modes

## Slide 3
Assembly code
Computers can only process instructions that are written in machine code
A machine code instruction has an operation code (opcode) and an operand
Assembly language uses mnemonics to represent operation codes and addresses
Suggest some typical assembly code mnemonics for common operations carried out by the processor

## Slide 4
Registers and accumulator
In a simple computer, all calculations may be carried out in a single register called the Accumulator
Other computers may have up to 16 general purpose registers used to hold values temporarily and perform calculations
The assembly code instructions are unique to a given computer architecture
All the instructions for a given computer form its instruction set

## Slide 5
Five common operations
Common instructions might include:
  <operand> could be:
  an actual value, specified by # or
  a value stored in another register specified by R
LDR Rd, <memory ref> | Load the value stored in <memory ref> into register d
STR Rd, <memory ref> | Store the value in register d into the memory location specified by <memory ref>
ADD Rd, Rn, <operand> | Add the value specified in <operand> to the value in register n and store the result in register d
SUB Rd, Rn, <operand> | Subtract the value specified by <operand> from the value in register n and store the result in register d
MOV Rd, <operand> | Copy the value specified by <operand> into register d

## Slide 6
Examples
LDR R1,300 ;load contents of 300 into R1
ADD R1,R1,301 ;add contents of 301 to R1
MOV R2,R1 ;copy contents of R1 into R2
SUB R3,R2,#5 ;subtract 5 from R2, put in R3
STR R3,302 ;store contents of R3 in 302
If address 300 contains 20 and address 301 contains 10, what are the contents of R1, R2, R3 and address 302 after execution of these instructions?

## Slide 7
Immediate and direct addressing
The instruction
SUB R3, R2, #5
uses immediate addressing, i.e. it uses the actual value 5 as the operand
The instruction
LDR R1, 300
uses direct addressing, i.e. it uses the memory address (300) holding the value as the operand

## Slide 8
Example 1
Three numbers are stored in locations 301, 302, 303
  Using instruction formats below, write instructions to add the three numbers and store the result in location 304
  <operand> can be interpreted as a value (indicated by #, e.g. #35) or as a register (indicated by R, e.g. R0)
LDR Rd, <memory ref> | Load the value stored in <memory ref> into register d
STR Rd, <memory ref> | Store the value in register d into the memory location specified by <memory ref>
ADD Rd, Rn, <operand> | Add the value specified in <operand> to the value in register n and store the result in register d
MOV Rd, <operand> | Copy the value specified by <operand> into register d

## Slide 9
A possible solution
LDR R1, 301
LDR R2, 302
ADD R1, R1, R2
LDR R3, 303
ADD R1, R1, R3
STR R1, 304
There are many variations that could also be correct

## Slide 10
Adding comments
Adding a comment to each line helps to make the code understandable:
LDR R1, 301 ;load contents of 301 into R1
LDR R2, 302 ; load contents of 302 into R2
ADD R1, R1, R2 ;add R2 to R1, store in R1
LDR R3, 303 ; load contents of 303 into R3
ADD R1, R1, R3 ;Add R3 to R1, store in R1
STR R1, 304 ;store result in 304

## Slide 11
Branch instructions
There are no IF statements in assembly language
Instead, compare and branch instructions are used
CMP Rn, <operand> | Compare the value stored in register n with the value specified by <operand2>
B <label> | Always branch to the instruction at position <label> in the program
B<condition> <label> e.g. BEQ, BNE, BGT, BLT | Conditionally branch to <label> if the last comparison met the conditions specified by <condition>: EQ: Equal to 0 NE: Not equal to GT: greater than LT: Less than

## Slide 12
Example 2
Two numbers are stored in locations 301, 302
Store the larger of the two numbers in location 303
  Use the instructions below in addition to LDR and STR:
CMP Rn <operand> | Compare the value stored in register n with the value specified by <operand>
B <label> | Branch to the instruction at position <label> in the program
B<condition> <label> e.g. BEQ, BNE, BGT, BLT | Conditionally branch to <label> if the last comparison met the conditions specified by <condition>: EQ: Equal to 0 NE: Not equal to GT: greater than LT: Less than

## Slide 13
A possible solution
LDR R1, 301 ;load 1st number into R1
STR R1, 303 ;assume R1 > R2
LDR R2, 302 ;load 2nd number into R2
CMP R1, R2 ;Compare R1 to R2
BGT LABEL1 ;If R1>R2 branch to LABEL1
STR R2, 303 ;else, store R2 in 303
LABEL1
… (continue)

## Slide 14
While loops
The equivalent of a WHILE loop can also be written using Compare and Branch instructions
Suppose a user inputs numbers into register 0 using the statement INPUT R0
  The last number input is a “dummy” value of 0
  The total of these numbers is to be stored in location 100
Start
Input number
Number = 0?
Add to Total
No
Yes
Store Total in location 100
End
Set Total to 0

## Slide 15
A loop to add numbers
MOV R1, #0 ;initialise R1 to hold total
LOOP
INPUT R0 ;input a number
ADD R1,R1,R0 ;add number to R1
CMP R0, #0 ;compare number with 0
BNE LOOP ;branch if not zero
STR R1, 100 ;store total in location 100
There are many variations that could also be correct

## Slide 16
Worksheet 4
Now try the questions in Task 1

## Slide 17
Logical bitwise operators
Instructions to perform AND, OR, NOT and XOR operations typically look like this:
AND Rd, Rn, <operand2> | Perform a bitwise logical AND operation between the value in register n and the value specified by <operand2> and store the result in register d.
ORR Rd, Rn, <operand2> | Perform a bitwise logical OR operation between the value in register n and the value specified by <operand2> and store the result in register d.
EOR Rd, Rn, <operand2> | Perform a bitwise logical exclusive or (XOR) operation between the value in register n and the value specified by <operand2> and store the result in register d.
MVN Rd, <operand2> | Perform a bitwise logical NOT operation on the value specified by <operand2> and store the result in register d.

## Slide 18
AND OR XOR NOT
Inputs A 1010 1010 1010 1010
B 1100 1100 1100
Result
Can you fill in the results of each of the operations:
A AND B, A OR B, A XOR B, and NOT A?
AND, OR, XOR, NOT

## Slide 19
AND, OR, XOR, NOT
AND OR XOR NOT
Inputs A 1010 1010 1010 1010
B 1100 1100 1100
Result 1000 1110 0110 0101

## Slide 20
Example 4
The AND function can be used to mask out certain bits of a number
  This could be used to change an ASCII number to a pure binary number by masking the first four bits
For example, the ASCII character 7 is 0011 0111
LDR R2, 201 ;load ASCII char from loc 201
AND R3, R2, #00001111B ;AND it, store in R3
(#00001111B represents the Binary value)

## Slide 21
Example 5
The OR function can be used to set certain bits to 1 without affecting other bits
  This could be used, for example, to turn on specific lights in a set of 8 lights
Light numbers 1 2 3 4 5 6 7 8
Present output 0 0 0 0 0 0 0 0
OR with 0 0 0 0 0 0 1 1
  What does this do?
  Can you write the assembly code instructions to turn on lights 7 and 8? Assume the bit pattern for the light is in memory location 200

## Slide 22
Example 5 - Solution
To turn on lights 7 and 8:
LDR R2, 200 ;load bit pattern into R2
ORR R3, R2, 00000011B ;OR operation
STR R3, 200 ;store the bits back in 200

## Slide 23
Example 6
The NOT function can be used to find the two’s complement of a number:
A 0110 1100
NOT A 1001 0011
Add 1 0000 0001
2’s complement 1001 0100
If the number is in R1, the assembly language statements to carry out this operation could be:
MVN R1, #01101100B ;perform NOT operation
ADD R1, R1, #1 ;add 1 to result in R1

## Slide 24
Worksheet 1
Now try the questions in Task 2

## Slide 25
Logical Shift operations
A logical shift left of one bit moves all the bits one place to the left
LSL R2, R1, #1
R1
R2
  The format of the instruction is
1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
LSL Rd, Rn, <operand> | Logically shift the value stored in register n by the number of bits specified by <operand> and store the result in register d

## Slide 26
Logical shift right
A logical shift right of two bits moves all the bits two places to the right
LSR R2, R1, #2
R1
R2
1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1 | 1

## Slide 27
Logical shift right
A logical shift right causes the least significant bit to be shifted into the carry bit and a zero moves in to occupy the vacated space
R1:
After the instruction LSR R2, R1, #1
R2:
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1
Carry

## Slide 28
Worksheet 4
Now try the question in Task 3

## Slide 29
Plenary
Be aware that instruction formats vary – you will be given the format of instructions to use in any questions that involve writing assembly language
Be sure you can define the terms operator, operand, direct addressing, immediate addressing and give examples