## Slide 1
AQA
    AS Level
      Computer Science
      Paper 2
Network topology
  Unit 6
  Communication: Technology and consequences

## Slide 2
Describe star and bus topologies for a local area network
Differentiate between physical and logical network topologies
Explain the operation of physical star and logical bus network topologies
Describe the advantages and disadvantages of each topology
Objectives

## Slide 3
Home network
Wireless
router

## Slide 4
School Local Area Network
Switch
Router
Server

## Slide 5
Local Area Networks (LANs)
One computer, not connected to any other computing device is called a ‘standalone’
As soon as you connect two or more computers together they form a network
All networks fall into one of two categories:
  Local Area Network (LAN)
  Wide Area Network (WAN)

## Slide 6
Local Area Networks (LANs)
Local Area Network: two or more computers connected together within a small geographical area, for example confined to one building or site
Can you think of some obvious advantages of having computing devices connected in a LAN?

## Slide 7
Network topologies
A network topology is the arrangement of the various computing devices which make up a computer network
  Bus topology: an arrangement where nodes are connected in a daisy chain by a single central communications channel
  Star topology: an arrangement where a central node or hub provides a common connection point for all other nodes

## Slide 8
Bus network topology
Terminator
Terminal
Server
Backbone cable

## Slide 9
Operation of a bus network
All nodes are connected to a single backbone cable
Each end of the backbone is connected to either a terminator or a computer which stops signals ‘bouncing back’
Each node is passive
Data is sent in one direction at a time only
Only one computer can transmit successfully at any one time
  Carrier Sense Multiple Access (CSMA/CD) technology is used to enable nodes to transmit on the same cable

## Slide 10
Bus network
What are the advantages and disadvantages of a bus network?
Advantages | Disadvantages

## Slide 11
Bus network
Advantages | Disadvantages
Inexpensive to set up | Main cable is a point of failure
Devices can easily be added | Limited cable length
Good for small networks | Performance degrades with heavy use, owing to data “collisions”
 | Poor security

## Slide 12
CSMA with Collision Detection (CSMA/CD) detects two nodes attempting to transmit simultaneously
  Both nodes cease transmission and wait a random amount of time before reattempting
  CSMA with Collision Avoidance (CSMA/CA) is used with wireless networks
Carrier Sense Multiple Access

## Slide 13
Star network topology
Switch / Hub

## Slide 14
Computers are connected to a central node. This is often either a hub or a switch
  A switch sends each communication to the specific computer it is intended for
  A hub broadcasts the message to every computer on the LAN
Operation of a star network

## Slide 15
MAC addressing
Every networked device contains a Network Interface Card (NIC)
Each NIC is attributed a unique Media Access Control (MAC) address hardcoded in manufacture
3B-84-D8-A3-5C-7F
  A switch holds all of the MAC addresses for each device connected to it and uses these to direct packets of data to the correct device

## Slide 16
Star network
What are the advantages and disadvantages of a star network?
Advantages | Disadvantages

## Slide 17
Star network
Advantages | Disadvantages
Easy to isolate problems | Can be expensive to set up because of the length of cable required
Good performance | Central device is point of failure
More secure if a switch is used as data is sent only to the recipient | 

## Slide 18
Physical vs logical topology
Bus or Star?
Switch
Router
Server

## Slide 19
Physical vs logical topology
The physical topology of a network defines how the devices are physically connected
The logical topology defines how the devices communicate across the physical topologies
  A network wired in star topology can behave logically as a bus network by using a bus protocol and appropriate physical switching

## Slide 20
Worksheet 2
Now do the questions in Tasks 1 and 2 of the worksheet