## Slide 1
AQA
    A Level
      Product Design 7552
Scales of production
Unit 10 Modern industrial and commercial practice
1

## Slide 2
Describe the characteristics of different scales of production including unit production systems, quick response manufacturing and vertical in-house production
Understand the value of different scales of production to the manufacturer and the consumer
Objectives

## Slide 3
Starter
What might be the level of demand for each knife?

## Slide 4
Scales of production
Scale refers to ‘size’ or ‘level’, which depends on the:
  Type of product
  Demand (long and short term)
  Unit cost
  Set-up costs
Explain the term 'economy of scale'
Notes: 4

## Slide 5
A need for products
For millennia humans have been making products to make their lives easier
  Clothing, tools and dwellings are some of the earliest artefacts
  Products were made to trade for food and other products
  Professions were established and skills were handed down the generations
  As demand increased, production methods changed
Notes: 5

## Slide 6
Increasing production levels
Achieving consistency and quality across multiple products became challenging
  How did makers and crafts people improve accuracy and speed up their production processes to meet demand?
Scales of production
Unit 10 Modern industrial and commercial practice
Notes: 6

## Slide 7
Historical context
As far back as 500 BC the Chinese were using division of labour and mass production methods
They produced:
    Agricultural tools
  China and terracotta products
  Weapons
The development of which manufacturing method greatly contributed to this?
Scales of production
Unit 10 Modern industrial and commercial practice
Notes: 7

## Slide 8
Industrial revolution
Industrial revolution, circa1760, saw an increase in automation
Linear assembly processing began in many areas including:
  Ship building
  Bridge construction
  Tower building
  Locomotive manufacture
Which key invention drove the industrial revolution?
Notes: 8

## Slide 9
Production lines
In the early 1900s Oldsmobile and Ford introduced production lines to their factories
  This coincided with the standardisation of components and parts
  Why is standardisation important?
    Which major event of the early 20th century accelerated the development of mass production and why?
Notes: 9

## Slide 10
Bespoke or one-off
Bespoke, one-off or ‘made to measure’ products are:
  ‘Tailor made’ to specific user needs
  Made by highly skilled people
  Made predominantly ‘by hand’
  Of high-quality using quality materials
  Time consuming to produce
Why do people pay extra for one-off products?
Notes: 10

## Slide 11
One-off products
A bespoke product is often seen as an investment as each product is unique
These products can include:
  Suits and dresses
  Artwork, ceramics and jewellery
  Architecture
  Furniture
Does a set of six chairs for a client count as one-off production?
Scales of production
Unit 10 Modern industrial and commercial practice
Notes: 11

## Slide 12
A one-off profile
A business producing bespoke products often has the following characteristics:
  A small company or crafts person with a limited number of staff
  Close communication with the client
  High-quality materials are used
  Highly skilled labour is required for handcrafted elements
  Unique and high-quality products are produced in low volumes
  High unit cost
https://www.youtube.com/watch?v=gZLGj4V_yBs
Notes: 12

## Slide 13
Batch production
Batch production is used when a greater number of products are required
  From more than one, to thousands of units
  Use of jigs, moulds, formers and templates for accuracy, consistency and efficiency
  CAD/CAM may be used
Why are some batch produced items referred to as 'hand-finished'?
Notes: 13

## Slide 14
Batch produced goods
Batch production is suited to seasonal products with limited demand
Types of products include:
  Printed items such as newspapers, magazines and books
  Most clothing
  Perishable food products
  Seasonal goods
Why are many items of sports equipment batch produced?
Notes: 14

## Slide 15
Batch production profile
Businesses that batch produce products often have the following characteristics:
  A simple production line
  Some level of automation
  Skilled and semi-skilled workers
  Flexibility to adapt their product line
  Produce limited product runs
  Lower unit costs
https://www.youtube.com/watch?v=aS8490xEI1E
Notes: 15

## Slide 16
Mass or line production
Mass or line production is used when a high number of products need to be produced quickly and consistently
  Uses a production/assembly line
  High-level of automation
  High initial set-up costs
What roles might skilled workers play in automated production?
https://www.youtube.com/watch?v=zrzKih5rqD0
Notes: 16

## Slide 17
Mass produced goods
Mass production requires very high capital investment
It is suited to high and continuous products runs including:
  Packaging and containers such as boxes, bottles and cans
  Many food products
  Materials, such as steel and timber stock
  Paper stock and paper products
Why might some mass produced items be made in batches?
Notes: 17

## Slide 18
Mass production profile
Businesses mass producing products often have the following characteristics:
  High set-up costs and capital investment
  Shift work is used to facilitate 24/7 production
  Both skilled and unskilled labour required
  Expensive purpose made tooling and machinery required
  High-level of automation
  Low unit cost
  Less flexibility for product diversity and slow to respond to change
https://www.youtube.com/watch?v=4ewRVKrFBdg
Notes: 18

## Slide 19
Scales of production
Complete Task 1 of Worksheet 1
Notes: 19

## Slide 20
Efficient production methods
Manufacturers often seek to implement increasingly more efficient systems
  This can be in response to market 'pull' or demand
  It is often to gain a competitive advantage through:
    A reduction in lead time meaning their products are the first to market
    The need to cut costs, meaning that they can undercut the competition
What is meant by the term Kaizen?
Notes: 20

## Slide 21
Lean production
Lean manufacturing strives to reduce waste and stems from a Japanese philosophy originating at Toyota
There are seven distinct areas for waste reduction:
    Overproduction
    Waiting
    Transportation
    Over processing
    Excessive inventory
    Unnecessary motion
    Defects
Scales of production
Unit 10 Modern industrial and commercial practice
Notes: 21

## Slide 22
Unit production systems (UPS)
UPS use overhead tracks to move component parts, usually garments, on hanging carriers
  Workers at each station perform a specific task before returning the product to the carrier and to be sent to the next workstation
  A UPS offers increased control of workflow
  Streamlines assembly and speeds up production
  Automatic movement of products reduces labour costs
  Stages of production are logged, improving quality control
    What other advantages does this system offer?
https://www.youtube.com/watch?v=Kx8xQpTyGis
Notes: 22

## Slide 23
Quick response manufacturing
QRM reduces lead times in response to demand
  Production is triggered by consumer demand and not through traditional methods such as trend forecasting
  Time-based competition (TBC) is a strategy used to get ahead of the competition and is a feature of QRM
Scales of production
Unit 10 Modern industrial and commercial practice
https://www.youtube.com/watch?v=PCF8FgVH-Nw
Notes: 23

## Slide 24
QRM profile
Reduced time to market through:
    A reduction in external and internal lead times by improving communication and systems
    The ability to respond more efficiently to customer pull, market demand and fluctuations in fashion
    Increasing flexibility in the manufacturing process using ‘flow’ production methods
    Increasing the amount of ‘added value’
Why is team work so important?
Scales of production
Unit 10 Modern industrial and commercial practice
Notes: 24

## Slide 25
Vertical production
Vertical ‘in house’ production increases productivity and profits by integrating parts of the supply chain within the main company
  This frequently involves the acquisition of other companies responsible for the supply of raw materials, delivery and retail
Scales of production
Unit 10 Modern industrial and commercial practice
Notes: 25

## Slide 26
Need a reliable supply chain?
Vertical in house production is a way to ensure a robust and reliable supply chain
Advantages of owning the supply chain are:
  Fixed prices for parts and services
  A reliable source and supply of parts and services
  Transparent and shared quality assurance procedures
Disadvantages include:
  Diversification of core business, potential lack of skills
  Greater administration and complex management structure
  Very high capital outlay
Notes: 26

## Slide 27
Case study
Microsoft has bought out over 200 companies and has stakes in many more
  Most of these are digitally based and add strength to the Microsoft brand and portfolio
  Company acquisitions also reduce potential competition
  Latest additions include Cloud management, 3D gaming and Artificial Intelligence companies
Give examples of other companies that use this strategy
Notes: 27

## Slide 28
Plenary
Complete Task 2 and 3 of the worksheet
Notes: 28

## Slide 29
Notes: 29