## Slide 1
AQA
    A Level
      Product Design 7552
Digital design and manufacture
Unit 10 Modern industrial and commercial practice
4

## Slide 2
Describe the pros and cons of using CAD compared to manually generated alternatives
Explain how CAD is used to develop and present ideas for products
Understand different industrial applications for CAD
Describe how CAM is used to manufacture products
Objectives

## Slide 3
Starter
Discuss the advantages of using digital design and manufacture to produce embroidered logos
What would be the limitations of carrying out this task by hand?

## Slide 4
Digital design and manufacture
CAD/CAM has numerous advantages
  Streamlined design, development, testing and presentation
  Increases in speed and accuracy
  Entire production systems can be integrated (CIM)
  Digital files are shared easily among designers, manufactures, clients and consumers
    Are there any disadvantages to CAD/CAM?

## Slide 5
Artisans and labourers
Sophisticated CAD/CAM systems have replaced the need for manual labour
  Loss of hand-made / artisan skills
  A large workforce is no longer needed which can lead to unemployment and the break-up of communities

## Slide 6
Set-up and risks
Shifting to CAD/CAM is expensive and can be risky
  Setting up hardware and updating software is costly
  Existing staff need retraining while new recruits with the desired skills may demand higher wages
  Digital files are easy to replicate which can make designs difficult to protect against intellectual copyright theft

## Slide 7
Computer aided design
The advantages of CAD make it vital to modern design and manufacture
  How can computer aided design be used to develop ideas and present them to clients?

## Slide 8
Working drawings
Working drawings, whether drawn with CAD or by hand, include vital details for manufacturers
  Dimensions
  Elevations
  Sectional views
  Notes on manufacturing details
    Explain why different elevations and sectional views are important when designing and manufacturing
    Why are hand-drawn working drawings increasingly less common?

## Slide 9
2D CAD software
2D CAD is used for artwork, to show technical details and can be used to export files for CAM
  Drawings are created and modified easily with built-in software tools such as array/mirror/scale/dimension
  CAD files use layers to show how design features integrate, mimicking the tracing paper used when drawing by hand
  Which CAM machines use 2D CAD drawings?

## Slide 10
3D CAD presentation drawings
Presentation drawings offer virtual 360° views and walk-through tours
  Virtual lighting gives clients and focus groups a realistic idea of the final product
  3D renderings can quickly compare different materials and colourways
  2D drawings can be exported from 3D designs and software can offer different viewing options e.g. wireframes or solid view
    Discuss whether virtual models make physical prototypes redundant

## Slide 11
Presenting ideas
How does CAD benefit companies with an international client base?
  How do high-quality renderings and animations of a product benefit design teams?
  How could VR technology be used in product design and architecture to market new products?

## Slide 12
Worksheet task
Complete Task 1 of Worksheet 4

## Slide 13
From CAD to CAM
The variety methods for outputting a digital file make CAD very attractive to manufacturers
  Name the CAM machines that are used in school and in industry
  CAM machines are operated by computer numeric control (CNC)
  What does this term mean?
  What is G-Code?

## Slide 14
Laser cutting
Laser cutters convert 2D CAD designs to CNC code to move a machine head along the X and Y axes
  Laser beam cut or engrave materials
  Depth of cut is affected by the speed of the machine head and the power of the laser
  The workpiece doesn’t require clamping
  It is a high-precision and self-finishing process
  Requires extraction; some materials produce toxic fumes
    What are the limitations of the laser cutting process?

## Slide 15
CNC Routing
CNC routers offer versatility both in terms of movement and materials
  CNC routers operate on X, Y and Z axes to create more complex shapes
  Routers can waste thick materials using a variety of cutting tools which can be changed automatically
  Requires extraction and for the workpiece to be clamped
    What sort of products are made with CNC routers?

## Slide 16
Case study
Unto This Last is a medium-sized company specialising in high-end furniture made using CNC
  Veneered plywood is used to make the component parts
  Once designs are painstakingly perfected to customers’ specifications they can be reproduced as required
  CNC routing is flexible and versatile, so different product ranges can be developed and manufactured quickly in-house

## Slide 17
CNC Milling
CNC milling can be used to cut complex 3D forms
  Variety of cutting tools are used to machine complex shapes
  Cooling lubricants can be used when cutting metal to prolong the life of the tools and give a superior finish
  Used to make engine parts and moulds for mass production processes

## Slide 18
Turning with CNC
As the name suggests, turning involves a spinning workpiece, not spinning the cutting tool
  Used to manufacture shapes which require rotational symmetry along the central axis
  Completes operations such as cutting, boring, knurling and thread cutting
  Swarf is created by both milling and turning

## Slide 19
Plotter cutting
Plotters read 2D CAD files and cut materials such as vinyl, paper and lightweight card
  A machine head holding a blade or pen passes from left to right
  Simultaneously, rollers move the material back and forth
  Plotters can incorporate printing functions so graphics can be printed, cut and scored at the same time
  Often used with self-adhesive vinyl to create signage and vehicles decals

## Slide 20
CAM in a nutshell
Increases in the use of CAD/CAM in industrial manufacturing has had a huge impact including:
  Increased precision and consistency
  Greater control and accountability
  Increased output
  Waste reduction
  Increased efficiency
    Can you think of any disadvantages of CAM?

## Slide 21
Worksheet 4
Complete Task 2

## Slide 22
Plenary
Complete Task 3 of your Worksheet