## Slide 2
Objectives
Understand what is meant by an output device
Understand each of the following output devices and why they are required
  Speakers
  Light emitting diode (LED) screens
  Liquid crystal display (LCD) projectors
  Liquid crystal display (LCD) screens
  Digital light processing (DLP) projectors
  Actuators

## Slide 3
Starter
Think about the computers and devices you use
  What output devices do they use to interact with you?

## Slide 4
Starter
Output devices transfer data produced by a computer and turn it into a human-readable form
Examples include:
  Displays and projectors
  Printers
  Speakers
  Actuators

## Slide 5
Speakers and headphones
Digital data is sent from the computer to a Digital to Analogue Converter (DAC) where it is converted into an analogue signal
  The signal is then boosted using an amplifier and finally sent to a speaker

## Slide 6
Actuators
Actuators are output devices used to move mechanisms or systems
  One example of where an actuator is used would be an automatic door to a supermarket
  Give at least three other examples where actuators may be used

## Slide 7
Actuators
Some examples include:
  Central locking on cars
  Opening and closing valves on pipes
  Each part of a robotic arm will have an actuator to rotate it
  Food and drink manufacturing
  Moving the head of a 3D printer

## Slide 8
LCD screens
Liquid Crystal Display (LCD) screens are made from millions of pixels
  Each pixel is effectively a separate red, blue or green light that can be switched on or off electronically using liquid crystals to rotate polarised light
  The pixels are switched on or off very rapidly to make the moving colour picture

## Slide 9
LED screens
LED screens are very similar to LCD screens
  LCD screens are backlit with a fluorescent backlight
  LED screens use LEDs (light emitting diodes) to light them, but an LCD film is still used to turn the pixel colours on or off

## Slide 10
LED versus LCD screens
Using LEDs to back-light LCD screens has a number of advantages over the older fluorescent technology:
  They reach their maximum brightness almost immediately
  The image is sharper with more realistic and vivid colours
  They produce a brighter light which leads to better picture definition
  Since LEDs are very small, this allows the screens to be much thinner in construction
  They last almost indefinitely which makes the screens much more reliable
  They consume very little power and therefore produce very little heat and reduce running costs

## Slide 11
LED screens
Giant LED screens use LEDs for each individual sub-pixel
  They are very bright, so suitable for use outside in the day
  Many individual modules are combined together to build the screen, so they are perfect for festivals and music events

## Slide 12
Worksheet 4
Complete Task 1 on Worksheet 4

## Slide 13
DLP projectors
DLP (digital light processing) projectors use millions of micro-mirrors on a small microchip within the projector (each mirror corresponds to a single pixel)
  When these micro-mirrors are tilted towards the light source, they are in the ‘on’ status
  If they are tilted away from the light source, they are in the ‘off’ status
  The micro-mirrors can switch between ‘on’ and ‘off’ thousands of times a second creating different and changing shades of grey light

## Slide 14
Using grey light
DLP projectors use a grid of mirrors that can each produce over a thousand shades of grey
  If a micro-mirror is in the ‘on’ status more than it is in the ‘off’ status, then it produces a lighter shade of grey – if it’s the other way round, then a darker shade of grey is produced
  This creates a greyscale video image using grey ‘mirror’ pixels

## Slide 15
Adding colour with DLP
A strong white light passes through colour filters on a rapidly spinning wheel which converts it into red, green or blue light
  A filtered green light shone onto a tilted ‘off’ mirror reflecting dark grey light, projects a dark green pixel
  A purple pixel is created by rapidly changing a pixel from blue to red which our brain interprets as blend of the two colours

## Slide 16
Digital Light Projectors (DLP)
How a DLP projector works
Light source
Projected output

## Slide 17
LCD projectors
Like DLP, LCD projectors depend on a very bright source of white light
  The white light is sent to Dichroic mirrors and the light is reflected back with red, green or blue wave lengths
  The three coloured light components pass through three LCD screens containing the image from the computer to be projected

## Slide 18
LCD projectors
The three images are then combined using a prism to produce the full colour image which then passes through a lens and is projected on to a screen

## Slide 19
Worksheet 4
Complete Task 2 on Worksheet 4

## Slide 20
Plenary
Discuss the answers to the following questions with a partner
  Explain the differences between an LED screen and an LCD screen
  Explain the differences between a DLP projector and an LCD projector
  Give four ways in which actuators are used in your life

## Slide 21
Plenary
  LED and LCD screens
  The screens work in the same way, but the backlighting of an LCD screen uses a fluorescent light, whereas an LED screen uses LEDs. Large LED screens use LEDs for each pixel
  DLP and LCD projectors
  LCD projectors use three LCD screens, one for red, green and blue. The three images are then combined into colour
  DLP projectors have a mirror for each pixel and a rotating wheel with the colours red, green and blue
  Give four ways in which actuators are used in your life
  Automatic doors; car door locks; valve opening on car components; moving a rollercoaster forward and many more