## Slide 1
AQA
    A Level
      Product Design 7552
Accuracy in design and manufacture
Unit 14 Design processes
7

## Slide 2
Understand and explain the importance of accuracy in manufacture
Explain how testing can eliminate errors in production
Evaluate the use of measuring aids for ensuring consistency in accuracy and reducing human error
Objectives

## Slide 3
Starter
In pairs, discuss how jigs, templates and other aids could be used in the production of a violin

## Slide 4
Accuracy in manufacture
Accuracy is a vital part of commercial manufacture for all levels of production
  It is necessary to ensure products function effectively
  The correct use of measuring and marking out tools reduces the need for additional equipment to reduce errors especially important in mass production
  Name some measuring tools you have used in the school workshops

## Slide 5
Marking out and measuring
Depending on the material, a variety of tools are used when marking out for manufacture
  Which tools are common to most material types?

## Slide 6
Marking out different materials
Different materials call for slightly different tools
  For timbers a marking knife, marking gauge, mortice gauge, sliding bevel and a try square are required along with a sharp, wide leaded pencil known as a carpenter’s pencil
  Metals use engineers squares, scribers and scribing blocks, vee block, callipers, centre punch and Vernier gauges, additionally metal can be painted with engineer’s blue
  What is engineers blue and how is it used?
  How do you ensure a marked line is parallel to an edge when working with woods and metals?
  Why might laser devices be used for measuring in larger scale production?

## Slide 7
High precision
For precise measurements, where fine tolerances are required additional equipment is used
  Micrometres, Vernier callipers and dial gauges can all be used to precisely measure components
  Coordinate measuring machines (CMM), profile projectors and digital test gauges are often used in industry
  Digital readouts are usually preferred over mechanical dial indicators by many as the display is easier to read

## Slide 8
Metric vs imperial
It is worth considering the units in which drawings and parts are measured and made in
  In product design the metric international system of units is normally used, however the USA still used the imperial system
  Many CAD software packages are produced in the USA and may default to imperial units
    Why might the majority of countries around the world use the metric system of measuring?

## Slide 9
Accuracy
Accuracy is defined as the conformity of a measurement to the required value
  The miniaturisation of parts has increased the level of accuracy required in manufacture
  The amount of tolerance required in products can vary considerably depending on size and function
    Put the products shown below in order of allowable tolerance

## Slide 10
Datums
Datum surfaces are an important factor to consider - they are the edge from which other measurements are taken
  Datum surfaces reduce the amount of cumulative error in manufacture
  How can they achieve this?

## Slide 11
Testing
Quality control ensures all components remain within tolerance and are dimensionally accurate
  Testing can be carried out using a profile projector, also called an optical comparator to accurately check measurements
  Alternatively, trained engineers may be required to check parts using digital micrometres or Vernier callipers which may provide more flexibility

## Slide 12
Go no-go gauge
Go no-go gauges are inspection tools that are used to check work against a given tolerance
  They can be used quickly and easily by unskilled workers
  The check involves two tests – the workpiece has to pass one test (go) by fitting one gauge, then the workpiece must not fit and fail the other (no-go)
    What are the benefits of using this test in mass production?

## Slide 13
Increasing production speed
Accuracy and speed of production can be increased and improved through a number of methods
  Jigs help control the motion of the tool, remove the need for marking out and ensure cuts are in the same place every time
  Fixtures are frames with holding points and clamps and are used when machining, welding and gluing
  Templates allow a pattern to be transferred onto material and ensure the same shape is always marked out
    How can the use of jigs, fixtures and templates reduce the need for high level skills?

## Slide 14
Worksheet 7
Complete Tasks 1 and 2 of your Worksheet

## Slide 15
Plenary
Explain the need for tight tolerances in a highly engineered product like a Rolex watch