## Slide 1
AQA
    A Level
      Product Design 7552
Quality assurance and quality control
5
Unit 15 Responsible design

## Slide 2
Know how strategies, procedures and checks are used to assure quality
Understand quality assurance systems and their application including Total Quality management, Scrum and Six Sigma
Be able to suggest appropriate quality control systems including monitoring, checking and testing
Understand how to ensure that products components are manufactured within acceptable tolerances
Objectives

## Slide 3
Starter
What's the difference between QA and QC?
  In pairs, define both quality assurance (QA) and quality control (QC) - use examples to explain the different principles
  How do the QA and QC work together to produce quality and fit-for-purpose products and services?

## Slide 4
Quality Assurance (QA)
QA is a procedure or system which is followed in order to achieve the desired level of quality
An effective quality assurance procedure involves:
  Measurement of variables
  Comparisons with specifications
  Constant monitoring of processes
  Using feedback loops to prevent errors
Quality assurance is process led and focuses on defect prevention

## Slide 5
Understanding QA
You need to know about QA for:
  waste reduction
  accurate manufacturing
  applying tolerances
You also need to know about these QA systems:
  Total quality management (TQM)
  Scrum
  Six Sigma
  Critical path analysis (CPA)

## Slide 6
Simple planning systems
A simple way to plan a sequence of manufacturing events is by using a flowchart
  A flowchart is a type of diagram that shows a workflow or process and is usually read top to bottom, left to right
  They highlight critical control points and allow feedback
  Flowcharts help manufacturers to identify possible problems such as bottlenecks
    Identify the manufacturing events denoted by each of the shapes on the right

## Slide 7
Gantt chart
Gantt charts are named after their inventor, Henry Gantt in the early 19th century
They are a widely used project management tool showing:
  the phases of a project
  individual tasks
  key milestones
  required resources
  Tasks are usually shown on the vertical axis whilst timings are recorded on the horizontal axis

## Slide 8
Kaizen = constant improvement
Kaizen, in Japanese means change for the good and is the guiding principle behind lean manufacturing
  Its aim is to improve efficiency and eliminating waste in all areas of production
Kaizen relies on:
  employee collaboration
  evaluation and innovation
  practical improvement
  How might Kaizen play a part in the management of quality in manufacturing?

## Slide 9
Total Quality Management
Based on the principals of Kaizen, Total Quality Management (TQM) is a customer focused, process centered strategy
Key features include:
  Integrated strategies and systems
  Employee involvement
  Communication
  Constant feedback
  Continuous improvement

## Slide 10
Scrum development process
Scrum is a quality driven, agile framework for managing product development and problem solving
Named after a rugby scrum used to restart a match
  Scrum is initiated by the product owner with a product backlog (a wish list of items to bring to the market)
  The scrum master leads scrum team in series of sprints (shorter focused tasks delivered by the team)
  Scrum uses different types of sprint meetings and lists to ensure everything is kept on track

## Slide 11
Scrum lists and meetings
The sprint backlog is a list of products to produce in the next sprint
The scrum board contains a list of tasks for each team member and tracks their progress
  Each of the four types of meeting is used to explore different aspects of the sprint. These are:
  Sprint planning – used to set up the sprint parameters
  Daily ‘stand-ups’ – used to check if everything is going to plan
  Sprint review – used to deliver the results and get feedback
  Sprint retrospective – used to reflect on what can be improved

## Slide 12
Six Sigma
Created at Motorola in 1986, Six Sigma aims to improve process and management performance
  Six Sigma projects follow a methodology inspired by W. Edward Deming's ’Plan-Do-Study-Act’ Cycle (PDSA)
  It comprises five phases: Define – Measure – Analyse – Improve – Control (DMAIC)
‘Six Sigma’ refers to the number of allowable defects, 3.4 defects per million (DPM)
  Identifying and removing the main causes of errors improves efficiency, productivity and quality and limits waste
  Many large corporations now use Six Sigma

## Slide 13
Process planning
Businesses use various methods of planning and charting projects including:
  Project evaluation and review techniques (PERT)
  Critical path analysis (CPA) or critical path method (CPM)
Both are project modelling tools that are used to map out every stage of a project in sequence
  Both PERT and CPM rely on arrow and node diagrams
  They calculate the longest path of all planned activities to their individual end points or to the end of the project
  Some tasks have float, meaning that there is room for them to be delayed without making the project longer

## Slide 14
Critical path analysis (CPA)
CPA is a six step method used to plan sequential activities, showing them as nodes, usually boxes joined with arrows with each box including details of the duration of each task
  Stage 1: Specify each task
  Stage 2: Sequence activities
  Stage 3: Draw network diagram
  Stage 4: Estimate timelines
  Stage 5: Identify the critical path
  Stage 6: Update diagram to show progress

## Slide 15
Project evaluation and review
Project evaluation and review (PERT) is very similar to CPA, however it does not give a single estimate of project duration
  Instead it allows the user to calculate a realistic timescale based on three variables which can assist long term planning
  Optimistic duration (O)
  Most likely duration (M)
  Pessimistic duration (P)
  The final calculation to find the most realistic duration (E) is: E = (O + 4M + P ) ÷ 6

## Slide 16
Worksheet 5
Complete Task 1 and 2 of your Worksheet

## Slide 17
Getting it right
Accurate measuring, marking out, manufacturing and testing ensures quality products are made
  Name and identify the digital tools pictured and explain their use in quality control procedures
Notes: Adapted from Edexcel Unit 6 -2 TS4 S3

## Slide 18
Measuring accuracy
Measuring materials accurately requires tools with accurate reference or ‘datum’ points – surfaces or edges from which all other measurements are taken
Measuring tools include:
    Traditional tools such as rules, squares callipers and gauges
    Digital micrometres and callipers
    Laser and probe scanners
    A dial test indictor or DTI (pictured) uses a probe to test accuracy from a specific reference point
Notes: Taken from Edexcel Unit 6 -2 TS4 S5

## Slide 19
Tolerance
High volume production aims for absolute accuracy and efficiency but there is a small margin for error
  This margin for error is called the tolerance and can apply to hole depth, length, angle, thickness, weight, elasticity and so on
  Go-no go gauges can be used to test components to see if sizes fall within a given tolerance
  All products must be within tolerance or they will be rejected during quality control checks
Notes: Taken from Edexcel Unit 6 -1 TS4 S16

## Slide 20
Quality control (QC)
Quality control ensures product standards are met
  Various tools are used to ensure parts have dimensional accuracy and are within tolerance
  What features do machines in the school workshop have to help ensure accuracy?
  What checks might be put in place to control the quality of products in large scale production?
Notes: Taken from Edexcel Unit 6 -2 TS4 S7

## Slide 21
Visual checks
Visual checks are still used to check quality throughout the production process to ensure that:
  supplied materials comply with the manufacturer’s requirements
  parts and components are within tolerance
  finished products and components match the product design specification
  products comply with relevant standards
  Why do visual checks often take the form of random spot checks used within a production line?

## Slide 22
Probe scanning
Coordinate measuring machinery (CMM) is used to check the measurements of finished components
Probe scanning:
    uses a calibrated probe pin and highly sensitive sensors
    tests dimensional accuracy
    can scan dynamically along a surface or measure using predetermined data points
    enables comparison of points against 3D CAD models

## Slide 23
Laser scanning
Non-contact co-ordinate measuring machinery (CMM) is also used
Laser scanning:
  uses a laser reflected off the surfaces of a product
  Can take thousands of accurate measurements very quickly
  creates an accurate comparative 3D CAD model
  can spot potential wear and tear in a system and accurately predict maintenance

## Slide 24
Non-destructive testing
The internal structure of materials or manufactured parts can be checked using non-destructive testing (NDT) methods such as:
  Ultrasound
  X-ray analysis
These can be used to measure wall thickness and detect internal faults not visible to the naked eye
    What type of faults might be identified using NDT?

## Slide 25
Plenary
Complete Task 3 of your Worksheet