## Slide 1
1
AQA
    A Level
      Product Design 7552
Performance characteristics
Unit 1 Performance characteristics of paper and boards

## Slide 2
Understand the common sources and manufacturing process of papers and boards
Know the common stock forms of papers and boards
Be able to identify specific qualities for a selection of papers and boards
Objectives

## Slide 3
Starter activity
Using the three samples provided, complete the Starter activity of Worksheet 1 to note any observations relating to the following characteristics:
    Whiteness
    Opacity
    Strength
    Absorbency
    Finish
    Cost

## Slide 4
What is paper made from?
Both paper and board are made from cellulose fibres derived from plants
  The fibres pictured are from waste sugarcane that has had the sweet juice extracted for sugar
  The shredded cane, named ‘bagasse’, is processed to make popular paper products
    What other sources of cellulose fibre are used for paper and board products?

## Slide 5
Paper and board sources
Sources of cellulose fibres include:
    flax
    hemp
    straw
    cotton
    bamboo
    and most commonly wood
What’s this ream of paper made from?

## Slide 6
Are special trees needed?
The best cellulose fibres for paper production comes from wood due to quality of the fibres length and strength
  Deciduous and coniferous trees can be used
  Why is it more common to use softwoods for paper production?

## Slide 7
What goes into making paper?
It’s made from debarked, chipped wood or other cellulose fibres and:
  acetic acid and/or other chemicals are used to break down the lignin that bonds the cellulose fibres
  fillers like clay and calcium carbonate are often added
  brightening agents such as bleach
  and finally lots and lots of water

## Slide 8
Wood free pulp
The solution is heated to 140º Celsius which produces a fibrous liquid, known as pulp
  Dyes and sizes can also be added to the pulp depending on the desired final appearance
  It takes a minimum 500ml of water to make one A4 sheet of 80gsm photocopy paper
  Nearly all of this water is filtered and reused
  After the cooking process the remaining, lignin free, fibres are called ‘wood free’ pulp
  How much water is needed to make a ream of photocopy paper; that’s 500 sheets?

## Slide 9
What are paper qualities?
The type of paper or board required is usually governed by the following properties:
  Whiteness – including level of brightness
  Opacity – how see through is it?
  Strength – does it resist tearing?
  Absorbency – for water or ink?
  Finish – matt, satin or gloss
  Cost – to match a price point
  Which properties affect printability?

## Slide 10
Creating the perfect paper
The five ingredients that can be ‘tweaked’ are::
  the source of the cellulose fibres
  the fillers that smooth out the finish of the paper
  the sizing agents that increase absorbency
  the calendaring process through different rollers to create specific thickness and surface finish
  additional finishes like UV varnish or texturing
Which stage uses chalk?

## Slide 11
Sizing reduces absorbency
Sizing agents are chemicals added to the pulp or sprayed and rolled to the base paper
  Internal sizing is added to the pulp and affects paper quality and the paper’s ability to run smoothly through machines
  Surface sizing is added to improve strength, reduce absorbency and hence improves printability
  Give examples of paper where little or no sizing is required
  Why would printing on sized paper result in deeper and richer colours?

## Slide 12
Coated finishes
The application of surface sizing is the main difference between coated and uncoated stock
  Coated paper reduces ink absorption which results in brighter, richer and sharper images with deeper blacks
  There are two main coatings:
  Clay which increases its smoothness
  Polyethylene (PE) increases gloss and wet strength

## Slide 13
Uncoated paper
Uncoated paper is not treated with any sealant
  This allows greater and faster absorption of water or ink
  As printing ink is applied it goes deeper into the paper rather than drying on the surface
  The result is that colours appear dull and the paper is weaker compared to coated paper
  The benefits are that it can be given a wide range of textured finishes
  How is the pattern around the edge of the serviette created?

## Slide 14
Paper and board finishes
A wide range of finishes are available for both the sheen and the texture of the paper
  Matte (matt) is smooth, dull in appearance and good for any high quality print job
  Satin has lower reflective levels than gloss paper, but more than matte
  Gloss is a shiny, higher quality coated paper
  Textures are created with a felt roller covered in woven wire
  Felt, wove and velum are increasingly smooth textures, whereas column, linen and laid have lines at different depths and positions; cockle resembles handmade paper

## Slide 15
Strength factors of base paper
Tear resistance depends on four factors
  The way the cellulose fibres bond to each other
  The strength of the cellulose fibres
  The length of the cellulose fibres; longer being stronger
  The quantity of fillers used; more fillers mean less strength
  Which surface finish adds tear resistance?

## Slide 16
Tear resistance testing
The Elmendorf tear test is the most widely used for paper and board
  It calculates how much force is used to continue a tear in a sample
  Samples are partially cut and clamped in position
  A pendulum tears the sample and continues to a resting point which is noted on a scale in Elmendorf units
  The Smithers Pira test is similar and measures multiple sheets

## Slide 17
Impact resistance
Another way to measure the strength of paper and board products is to subject them to an impact force
  The main ways papers and boards are damaged through impact are:
    packaging being damaged during transportation and use
    indentation through used of implement on the surface, such as pens and pencils

## Slide 18
Fit for purpose
Paper qualities are usually considered depending on the end use, for example:
  The paper’s weight - will it be posted? Airmail letters are very lightweight meaning cheaper to transport
  Longevity - newsprint is for one-off use and low quality will suffice
  Impact strength - corrugated board for packaging is directionally reinforced and structurally strong
  Waste and cost efficiency - e.g. does the design fit or tesselate on the stock sizes?

## Slide 19
Die cutting
Commercially, paper and board can be cut, scored, perforated and creased in one action with a die cutter
  Large quantities of identical shapes can be produced quickly
  The die is made by skilled technicians using a CAD drawing and laser cut plywood backing plates
  Nets for packaging and stationery products are made this way

## Slide 20
The anatomy of a die cutter
Metal rules or blades (usually steel) are embedded in the desired shape in the laser cut plywood form
  The material is placed on the cutting plate and pressed onto the die which cuts, scores, creases or perforates the material
  What do the ejection rubbers do?

## Slide 21
Folding and creasing
The difference between creasing and folding is subtle
  Creasing paper or board involves making a line that is permanently present after the material has been creased or folded either by hand or with a creasing rule
  The cellulose fibres become permanently crushed and weakened resulting in a crease line
  Folding in industry means to create a shape e.g. a box, an envelope or pamphlet
  Fold the corner of a piece of paper and press firmly, now fold it flat – can you get rid of the crease line?

## Slide 22
Scoring
Scoring is used to make a more exact line
  Scoring is the same process as cutting but the blade doesn’t go all the way through the material as less pressure is used
  Score lines partially cut the material allowing a sharp edge or joint to be created that can articulate accurately

## Slide 23
Perforations
These small cuts in a paper or board allow for portions to be folded or torn off with good accuracy
  Usually created with a perforation rule in a die cutter
  They can be created by hand using a perforation cutter where different profile wheels can be attached

## Slide 24
School-based cutting & scoring
Tools you will use:
    Safety rule
    Cutting mat
    Scalpel for cutting
    Blunt edge knife for scoring
  Which CNC machines can be used in school to cut and score paper and board?

## Slide 25
Revisiting paper qualities
Complete Task 1 of your Worksheet to describe the manufacturing processes applied to the paper samples
  Use Starter activity of your Worksheet for guidance
  Using the samples provided, explain what different processing has taken place during manufacture considering:
  Whiteness – opacity – strength – absorbency – finish
    You may add any additional characteristics you find such as texture, lamination, printability and so on

## Slide 26
Worksheet 1
Complete Task 2 to recognise die cutting processes

## Slide 27
Plenary
Why are cellulose fibres needed in the production of papers and boards?
Why might bleaching agents be added to pulp?
What is the process used to decrease the absorbency of papers and boards?
Die cutting cuts paper and board: What other processes can it perform?