## Slide 1
2
AQA
    A Level
      Product Design 7552
Applications of papers and boards
Unit 1 Performance characteristics of papers and boards

## Slide 2
Be able to name a range of papers and boards and describe their performance characteristics
Understand how some papers and boards can be designed to be impact resistant
Evaluate the properties and applications for a range of different paper and board products
Objectives

## Slide 3
Starter
What’s the difference between paper and board?

## Slide 4
Two-minute challenge
Place these papers & boards in the correct order by their weight
  Cartridge paper
  Mountboard
  Tracing paper
  Tissue paper
  Photocopy paper
  Layout paper
  Foil-lined board
  Bleed proof paper

## Slide 5
And the winner is…?
There is no way of knowing exactly as the ranges overlap, you would need compare actual samples
  Tissue paper: 10 - 35gsm
  Layout paper: 40 - 60gsm
  Tracing paper: 40 - 120gsm
  Bleed proof paper: 70gsm
  Photocopy paper: 70 - 150gsm
  Cartridge paper: 120 - 150gsm
  Foil-lined board: 200 - 400gsm
  Mountboard: 500 - 2500gsm

## Slide 6
GSM or Microns
Paper is classified by both weight and size
  Paper weight is measured in grams per square metre (GSM)
  Paper-based materials that weigh more than 220gsm are usually classified as boards
  Board is usually measured in microns (μm); 1000μm is 1mm of thickness
  Paper sizes are set globally using the A, B and C series, more on this next
  How does a paper or board’s performance characteristics change with an increase in its weight?

## Slide 7
As easy as A-B-C
ISO 216 governs paper sizes internationally
  A series is for standard trimmed paper stock
  B series is for alternative sizes often used in industry
  C series sizes are used for envelopes
Commercial untrimmed sizes:
  RA series which is 105% of A series
  SRA series being 115% A series
  Why do we need untrimmed sizes?

## Slide 8
Card or board?
Paper over 220gsm tends to be called card, but when is it board?
  Cards and boards are available in a range of thicknesses and strengths
  Card is usually measured in GSM but board more often in microns
  Board can be made from recycled paper unless it is of food grade
  Boards can be laminated to other materials or layered to enhance strength or surface finish or durability
  How can we accurately measure thickness?

## Slide 9
Corrugated card
Corrugated card is made up of one or two flat outer layers, called liners, and a corrugated medium
  Flexible in the single layer form otherwise directionally rigid with a good strength to weight ratio
  Shock-absorbing, lightweight and good thermal insulation make it perfect for packaging
  Why is it stronger in one direction than the other?

## Slide 10
Weight ranges available
The different corrugated or ‘fluted’ boards include:
  Single wall: 3000 - 5000μm
  Double wall: 6000 - 10000μm
  Triple wall: 12000 - 15000μm
  Name a suitable application for each type

## Slide 11
The perfect package?
It is easy to handle when packing and loading
  The outer layer can be printed on for branding and advertising
  Readily available in a range of sizes
  Cheap due to lower grade raw materials and a natural finish
  Fully recyclable
  However, it readily absorbs moisture
  Cannot pack very heavy items as it can tear or collapse when stacked
  What might prevent it being easily recycled?

## Slide 12
Tracing paper
Semi-transparent, grey in colour
  Good for tracing ideas and overlaying or transferring one image to another
  Relatively hard and strong
  Usually around 40-120gsm
  Acid is used to treat the paper giving it its transparency and making it resistant to grease

## Slide 13
Layout paper
Slightly transparent but greater opacity than tracing paper
  Off-white colour around 50gsm
  Not as strong as tracing paper
  Good for tracing ideas and laying out plans
  Often used in a sketch pad or large sheet format
  Takes pencil well

## Slide 14
Bleed proof paper
Designers use bleed proof paper for hand drawn marker renderings
  It does not allow ink or solvent based marker pens to bleed through
  Highly sized with high opacity giving deeper colours
  Normally 70gsm

## Slide 15
Cartridge paper
It has a creamy off-white colour, primarily used for sketching
  The surface qualities take various drawing media very well
  Used in Art and D&T departments for use with pens, pencils, pastels, crayons, inks and some paints
  Slightly textured finish
  Why might this be more expensive than copier paper?

## Slide 16
Watercolour paper
Artists use this for painting in watercolours
  Highly absorbent – therefore little or no sizing
  It can withstand large amounts of water and retain its structural integrity, remaining flat when dried
  It has a matte, lightly textured finish

## Slide 17
Photo paper
There are three main types of photo quality paper
  Inkjet paper has a non-porous treated surface so image stays sharp
  Laser paper has surface coatings designed to permit the plastic particles in toner to melt and bond onto the surface of the paper
  Photographic paper which has a photosensitive coating, reacts to light and the image develops over a short time
  What are the advantages and disadvantages of printing your photographs at home?

## Slide 18
Mount board
Used for mounting photos and pictures before framing
  It’s structurally very strong
  Available in a wide range of colours
  It normally has a white core which shows when it is cut at a 45° angle when used as a mount for framing
  Good for making final models but too expensive for prototypes

## Slide 19
Bleached card
Bleached white card, also called solid white board, is highly brightened and treated on both sides
  It is used for a range of products including high-end packaging and greeting cards
  It holds print very well and has a luxurious feel to the surface
  Usually available between 200 to 500gsm
  What could accidentally happen if you signed the card with a fountain pen, and why?

## Slide 20
Duplex board
This twin layered board is usually used for packaging
  The top layer is normally white, but available in range of colours
  It is food safe and can be coated to increase water and oil resistance
  It folds, cuts and prints well
  Usually around 200-500gsm
  How can you differentiate this from bleached card?

## Slide 21
Foil backed and laminated card
Some boards are coated or laminated with other materials to enhance their working properties
  Foil linings create an impermeable layer protecting the contents from light, air, odour and bacteria
  Polyethylene is used as a food safe liner, an adhesive between the card and foil layers and as an outer coating
  How could combining materials in this way affect biodegradability and recyclability?
  Name some uses for foil-coated boards

## Slide 22
Tetra-Pak® deconstructed
Tetra-Pak® is made up of six layers:
  74% paperboard
  22% polyethylene
  4% aluminium foil
Benefits include:
  Perfect for storage of liquid foods and beverages
  Foil layer insulates and protects
  Contents remain sterile for a long time
However, specialist recycling is required

## Slide 23
A sweet alternative
Tetra-Pak® has launched a range of containers that are made from 100% plant-based, renewable materials
  The Tetra Rex® range has made all plastic elements using bio-polymers, processed from sugarcane
  Even the LDPE film and HDPE lid
  The paperboard is certified by the Forest Stewardship Council (FSC)

## Slide 24
Metal effect card
The bright metallic effect can be added to the surface of card by bonding a metallic foil layer
  The card can be further processed with the addition of embossing to give it texture
  Matte and shiny gloss tones can be blended to create dramatic patterns
  Laminated versions can be used for cake boards and other food grade products

## Slide 25
Moulded paper pulp
The ubiquitous eggbox is perhaps the most iconic paper pulp packaging product
  Pulped paper is a very economical way to create specific forms for protective and secure eco-friendly packaging
  It has limited printability but is 100% recyclable

## Slide 26
Worksheet 2
Complete Task 1 and 2 of your Worksheet

## Slide 27
Plenary
Define the difference between paper, card and board
Explain which materials are ideal for the packaging
What qualities would you look for in different boards if you had to package a mobile phone?
Which papers and boards are the most absorbent?