## Slide 2
Objectives
Understand that a computer needs a network interface card (NIC) to access a network
Describe the role of a router in a network including:
  The routing of packets
  IP address assignment
  Connecting local networks to the internet

## Slide 3
Starter
When a tablet is first unboxed it cannot use the Internet or home network
  What hardware is used in connecting the tablet to the Internet?

## Slide 4
Starter
Key hardware:
  The tablet contains a Network Interface Card (NIC)
  The tablet connects to a router which contains a wireless access point (Wi-Fi)

## Slide 5
Network interface card (NIC)
Every device that connects to a network requires a network interface card (NIC)
  In larger computers this may be a large card as shown
  More commonly, it is built into the motherboard
  A NIC is also required on any smartphone or tablet

## Slide 6
IP addresses
When computers connect to networks they each have a unique address, just like each house in the UK has an address
  Each address has a 32-bit number
  It is usually written in denary with a dot separating each byte
  The address allows data to be sent to the correct computer
11000000 . 10101000 . 00000001 . 00111001
.
192
168
1
57
.
.
32-bit address

## Slide 7
Data packets
When data is sent through the Internet or a TCP/IP network, it is split up into much smaller quantities known as data packets
  These packets each store a small amount of the data
  Each packet may take a different route through the network
Data
Data
Data packets

## Slide 8
Worksheet 1
Complete Task 1 on Worksheet 1

## Slide 9
Router
Routers are used to send data to a specific destination on a network
    A home router, also known as a hub, will route packets from one part of a network to another
    What else might a typical home router/hub do?

## Slide 10
Router
The home router will route packets. It also:
  Contains a wireless access point for Wi-Fi connections
  Connects the local network to the internet using a modem
  Assigns IP addresses to each computer that connects to it

## Slide 11
IP address assignment
A DHCP server (Dynamic Host Configuration Protocol) is built to home routers
  When a new device connects to the network it is assigned an IP address by the DHCP server
1. Do you want to be 192.168.1.5 ?
2.
Yes please
3. Smartphone IP address: 192.168.1.5

## Slide 12
Connecting to the Internet
A router is used to connect a network to the Internet
  In a home network, the router is combined with the modem, switch, wireless access point and firewall
  In a large business, the router is likely to be a dedicated item of hardware
  The computers and devices will then connect to dedicated switches or wireless access points
Internet

## Slide 13
Worksheet 1
Complete Task 2 on Worksheet 1

## Slide 14
Plenary
Work with a partner to create a list of at least two items of hardware that are used to connect devices to the Internet
  For each item of hardware, describe to your partner what it does

## Slide 15
Plenary
Item of hardware | Purpose
Network interface card (NIC) | Inside each computer or device to connect it to the network
Router, which contains: Router Wireless access point Modem | The router sends data to a specific destination on a network; It assigns IP addresses if it contains a DHCP server; It connects the private/local network to the Internet The wireless access point may be inbuilt to the router – it allows devices to connect wirelessly A modem will be part of a home router – it converts data from digital to analogue (radio or optical)