## Slide 1: Half/Full Adders
Appendix Module 2

## Slide 2: Binary Addition Recap
Simple Rules of Binary Addition over 1 or 2 Bits
Notes: Show how 0+1 = 1, 1+1= s0, C1, 1+1+1 = s1 c1

## Slide 3: Binary Addition Recap
If All 0 then Sum is 0, Next Carry is 0
If there’s ONE ‘1’ then Sum is 1, Next Carry is 0
If there’s TWO ‘1’ then Sum is 0, Next Carry is 1
If there’s THREE ‘1’ then Sum is 1, Next Carry is 1
Worked Example:
CARRY |  |  |  |  | 
A | 0 | 1 | 1 | 0 | 1
B | 1 | 0 | 1 | 1 | 0
SUM |  |  |  |  | 
TASK (2mins): Create Revision
Flash Card of the rules!

## Slide 4: Binary Addition Rules Recap
If All 0 then Sum is 0, Next Carry is 0
If there’s ONE ‘1’ then Sum is 1, Next Carry is 0
If there’s TWO ‘1’ then Sum is 0, Next Carry is 1
If there’s THREE ‘1’ then Sum is 1, Next Carry is 1
Worked Example:
CARRY 1 | 1 | 1 | 0 | 0 | -- / 0
A 0 | 0 | 1 | 1 | 0 | 1
B 0 | 1 | 0 | 1 | 1 | 0
SUM 1 | 0 | 0 | 0 | 1 | 1

## Slide 5: The Half Adder
Ignoring the Carry,
what sort of Logic Gate gives the “SUM” output?
What sort of Logic Gate gives the “Carry” output?

## Slide 6: Whiteboards!
Draw the complete logic circuit and then write out the Boolean Equations for the HALF ADDER. The truth table for the HALF ADDER is shown below:
HINT:
S = ?
C = ?

## Slide 7: Whiteboards!
Draw the complete logic circuit and then write out the Boolean Equations for the HALF ADDER. The truth table for the HALF ADDER is shown below:
S = A ⊕ B
C = A ● B

## Slide 8: A Half Adder – Flash Card
S = A ⊕ B
C = A ● B

## Slide 9: The Full Adder
Like we showed in the worked example, we need to be “aware” of the carry from the last adder…

## Slide 10: The Full Adder – Worksheet Activity (5m)
INPUTS |  |  | OUTPUTS | 
A | B | C_IN | SUM | C_OUT
0 | 0 | 0 | 0 | 
0 | 0 | 1 |  | 0
0 | 1 | 0 | 1 | 
0 | 1 | 1 |  | 
1 | 0 | 0 | 1 | 
1 | 0 | 1 |  | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 

## Slide 11: The Full Adder - Activity
INPUTS |  |  | OUTPUTS | 
A | B | C_IN | SUM | C_OUT
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 12: A Complete “4 Bit” Ripple Adder
CARRY |  |  |  |  | 0
A |  | 0 | 1 | 0 | 1
B |  | 1 | 0 | 1 | 1
SUM |  |  |  |  | 
INPUTS |  |  | OUTPUTS | 
C_IN | A | B | SUM | COUT
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
<- Using Whiteboards Complete

## Slide 13: Plenary / Quiz
How many Full or Half Adders (Maybe a combination?) are needed to work on a FOUR bit wide addition? And Why?
From Memory, draw the HALF ADDER Logic Circuit

## Slide 14: Plenary / Quiz
How many Full or Half Adders (Maybe a combination?) are needed to work on a FOUR bit wide addition? And Why?
From Memory, draw the HALF ADDER Logic Circuit:
HOMEWORK
WorkSheets from the Appendix B Adders Section