## Slide 1
AQA
    A Level
      Product Design 7552
Forming processes
1
Unit 6 Processing and working with papers and boards

## Slide 2
Explain the ways paper and board can be shaped into different products such as packaging
Describe a range of shaping processes including die cutting, laser cutting, creasing and bending
Objectives

## Slide 3
Starter
How can the shape and form of papers and boards be manipulated?
  What tools and machinery can be used to shape paper and board?
  Why might we need to change the shape of paper and board?

## Slide 4
Shaping methods
This topic focuses on the following processes:
  Creasing
  Bending
    Discuss what you know about these processes in pairs
  Die cutting
  Laser cutting

## Slide 5
Creasing
Creasing compresses the cellulose fibres which allows paper or board to fold more easily
  The compressed fibres reduce the thickness of the material, improving flexibility and reducing splitting of the fibres
  How is scoring different from creasing?
  Would it be better to score or crease a corrugated box? Why?

## Slide 6
Worksheet Task
Complete Task 1 of Worksheet 1

## Slide 7
What is die cutting?
What do die cutters and cookie cutters have in common?

## Slide 8
Die cutting
Dies cutting is used to cut identical profiles out of paper and board
  Dies are made from shaped steel blades embedded into a plywood substrate
  Dies are pushed against sheet materials to create the desired shape – just like a cookie cutter
  In high-volume production die cutting is carried out in-line during printing
    What other operations can be performed with a die cutter?

## Slide 9
How is die cutting used?
Die cutting is used to cut 2D shapes for large batch and mass production
  Commonly used for packaging developments, greetings cards and card coasters
  Die cutters are also used to create kiss cuts for “peel and stick” products like stickers and labels
  Rotary die cutters can be web fed or sheet fed - what does this mean?

## Slide 10
Making the die
Dies are fairly costly to make but will produce many high-quality cuts
  Dies can cut, score, crease and perforate in one action – how would the shape of a steel cutting blade be modified to make perforations?
  Laser cutters are used to cut slots in the plywood for the steel blades – what does this tell you about the accuracy of the die?
  How have the die cutters pictured been designed to reduce waste?

## Slide 11
Rotary and flatbed dies
Rotary die cutting has higher set-up costs but is more efficient and more accurate
  It’s faster than flatbed die cutting and cost effective with high-volumes
  There’s less waste compared with flatbed dies and tighter tolerances can be achieved e.g. kiss cuts
  Flatbed dies are best suited to low volume production
  Flatbed dies can be changed swiftly which reduces downtime
Rotary die cutter
Flatbed die cutter

## Slide 12
Laser cutting
Laser cutters can be used to shape paper and board
  Materials of various thicknesses can be cut, etched or scored by changing the speed and power settings
  Laser cutting produces similar shapes and forms to die cutting, but why would laser cutting be more suitable for making personalised wedding invitations?

## Slide 13
Pros and cons
Choosing the manufacturing method for a product can make or break a business
  Laser cutting is ideal for personalised products, prototypes and short production runs
  Design files can be edited easily so you can respond rapidly to market trends
  Die cutting has higher set-up costs but it’s much faster, and thicker materials can be cut without burns along the cut lines
  Why can’t laser cutters be used to create a crease?
  Which can produce more intricate cuts?

## Slide 14
Worksheet Task
Complete Task 2 of your Worksheet

## Slide 15
Plenary
Precisely designed nets, folding mechanisms and pre-glued parts allows packages/products to be cut then transported flat, then assembled by the user
  Discuss the economic and environmental advantages of this