## Slide 1
AQA
    A Level
      Product Design 7552
Bonding, jigs and fixtures
2
Unit 6 Processing and working with papers and boards

## Slide 2
Explain the use of adhesives and fixings on paper and board
Describe how jigs and fixtures are used to aid the manufacture of paper and board products
Objectives

## Slide 3
Get stuck in
Complete the Starter task on Worksheet 2

## Slide 4
Paper and board adhesives
Many water-based, solvent-based and hot-melt adhesives are used with paper and board
  Most papers and boards are absorbent so adhesives sink into the surface readily – this makes them easy to glue
  Paper and board adhesives are often non-flammable, non-toxic and solvent-free while others contain VOCs and require careful storage and extraction and/or ventilation in use
  What are VOCs?
  What PPE might you use when applying adhesives?

## Slide 5
Polyvinyl acetate
Polyvinyl acetate (PVA) is a non-toxic, water-based white glue that dries clear
  Can be applied with a roller or brush for fast coverage but is only suitable for use with absorbent substrates
  Can be watered down to seal porous materials and for use in decoupage
  Must be applied thinly to avoid wrinkling
  Drying times vary depending on materials used – parts must be clamped while drying if there is any resistance between surfaces

## Slide 6
Hot-melt glues
Hot-melt glues are used extensively in packaging
  Easily integrates into automated, high speed manufacturing lines
  Dries quickly and bonds dissimilar materials
  Makes packaging easy to open
  Not suitable for heat sensitive materials as it can damage the substrate
  Not suitable for use in environments or during processes that operate at high temperatures – why?

## Slide 7
Solvent Cements
Solvent cements dissolve the surface of a material allowing parts to be fused together
  Polystyrene cement can be used to fuse foam core together
  It must be used sparingly otherwise too much of the material will dissolve
  Polystyrene cement emits toxic fumes so must be used in a well ventilated area
  What factors could affect the curing time of an adhesive or solvent?

## Slide 8
Contact adhesive
This adhesive is applied to both of the surfaces to be bonded and left to go tacky – it bonds on contact
  Can bond dissimilar materials but only suitable for heavy weight boards as it is too wet for thinner substrates
  With a distinctive yellow colour and thick consistency, it can be difficult to apply discretely
  Sold in tubes, tins or sprays
  Solvent-based, so should be used with caution

## Slide 9
Spray adhesives
Spray adhesives give a thin and even coverage
  Repositionable spray adhesives are ideal for experimentation; other types offer instant adhesion without drying time
  Can be difficult to control so workstations must be protected and the workpiece may need to be masked off
  The fine spray won’t wrinkle thin substrates
  Used for presentation boards and mounting photographs and artwork
  What H&S precautions must be taken?

## Slide 10
Food safe packaging
Water-based and hot-melt glues are the most widely used adhesives for food packaging
  Discuss why solvent-based adhesives should be avoided when making food packaging
  Why is takeaway food packaging often adhesive-free?

## Slide 11
Adhesive tapes
Tapes come in various widths, colours, adhesion strengths, transparencies and finishes
  Provides an instant bond, ideal for sealing parcels, joining materials edge to edge and scrapbooking
  With the exception of masking tape, most will cause damage if removed
  Customised tape can be used to promote a brand or alert a potential hazard
  How does the use of tape affect recycling?

## Slide 12
Fixing with components
Paper and board fixings allow dissimilar materials to be joined instantly
  For example, rivets and eyelets can be used to join dissimilar sheet materials and fabric
  They can create spinning parts and add reinforcement
  Rivets also add an aesthetic accent to key features
    What other fixing methods use components?

## Slide 13
Worksheet Task
Complete Task 1 and 2 of Worksheet 2

## Slide 14
Jigs and fixtures
Compare scissors and a paper trimmer
  How does the paper trimmer provide a more accurate method of cutting paper repeatedly?

## Slide 15
What is a jig?
A jig is a device used to control the location and/or motion of a tool in relation to the workpiece
Jigs may be bought-in tools or custom made devices
Jigs allow tasks to be performed:
  repeatedly
  accurately
  more efficiently
  Which part of a holepunch could be classified as a jig?

## Slide 16
Fixtures
A fixture holds a workpiece in position while a task is performed
  Jigs can hold a workpiece in position and guide a tool
  Fixtures can be used to hold a workpiece square while several operations are performed
  Parts may be held at a particular angle to help with assembly

## Slide 17
Advantages of jigs and fixtures
If a given operation needs to be repeated a number of times, it’s often beneficial to use a jig/fixture
  Reduces cost of production
  Increases efficiency
  Greater accuracy and consistency
  Less skilled labour required
  Can increase safety
  Improved quality
    What are the disadvantages?

## Slide 18
Worksheet task
Complete Task 3 of your Worksheet

## Slide 19
Plenary
Test your knowledge of how adhesives, fixings, jigs and fixtures can be used with papers and boards
  How can jigs be used when working with papers and boards?
  What are the precautions that should be taken when working with solvent cements?
  What are the disadvantages of PVA?
  Aside from adhesives, how can papers and boards be joined?
  What is the difference between a jig and a fixture?