## Slide 1
AQA
    A Level
      Product Design 7552
Finishing papers and boards
3
Unit 6 Processing and working with papers and boards

## Slide 2
Describe a range of printing processes and their suitability for different products and scales of production
Explain a range of finishing processes that can be used to enhance the appearance and functionality of papers and boards
Objectives

## Slide 3
Starter
What is printing and why do we print on products?

## Slide 4
How do we make colour?
RGB and CMYK are different colour processes
  Red, green and blue (RGB) is a colour mode linked to visual displays which produce light e.g. screens, cameras & TVs
  Print media is usually created by overlaying cyan, magenta, yellow and black (CMYK) – what does K stand for here?
  Spot colours can be used when the perfect colour can’t be mixed from the CMYK range or may be used to cut costs

## Slide 5
Graphics software converts RGB colour to layers of CMYK ready for printing
  Whatever printing method or colour process is used, each colour must be printed separately (except when using digital printing, where all four colours are printed in one operation)
  Registration marks are used to ensure each layer of colour is aligned properly - you may have noticed these markings on printed media
Layers of colour

## Slide 6
Printing processes
Different printing processes have different methods of transferring a graphic on to a substrate
The processes you will need to know about are:
  Screen printing
  Flexographic printing
  Offset lithographic printing
  Digital printing

## Slide 7
Screen printing
A versatile process ideal for short print runs and used to print posters, t-shirts and tote bags
  Can be set-up in a home workshop or on an industrial scale
  Jigs are used to speed up production and help align the screens as different colours are applied
  Set-up costs are fairly low as the screens can be cleaned and reused for other jobs
  With the right ink, it can be used on almost any substrate

## Slide 8
Preparing the screens
Before printing can begin, the screen must be prepared – every colour requires a different screen
  A fine mesh screen is coated with photo emulsion and left to dry in the dark
  A monochrome transparency of the artwork is placed on top of the screen to mask off key areas
  Light is used to fix the exposed photo emulsion to the screen
  Excess photo emulsion is rinsed away

## Slide 9
Making a print
Once the screens have been prepared, they are laid on the substrate and ink is forced through the screen
  A squeegee is used to apply a thin, even coating of ink

## Slide 10
Worksheet Task
Watch the link videos which demonstrate the screen printing process
  In pairs, discuss the pros and cons of screen printing
  Complete Task 1 of Worksheet 3

## Slide 11
Offset lithography
The most common and cost-effective commercial printing method, suitable for high-volume production
  It’s rapid, has a low unit cost and produces high-quality prints
  Used for magazines, books and catalogues
  The oil-based inks and water used in this process repel one another – this principle is the basis of offset printing

## Slide 12
Offset printing plates
The artwork is separated into different layers of colour (CMYK)
  Each layer is used to etch a printing plate made from thin aluminium sheet
  Printing plates are treated to make an oleophilic image area and a hydrophilic non-image area
  Oil-based ink is attracted to the oleophilic image area only

## Slide 13
How offset litho works
First a printing plate is installed on the plate cylinder
  Then ink and water are added to the printing plate
  The ink is offset onto the smooth blanket cylinder
  The print is created when the substrate is passed between the blanket and impression cylinders
  How are further colours and finishes added?

## Slide 14
Flexographic printing
Flexography uses a flexible photopolymer printing plate
  Uses water-based inks which dry fast; this makes the process efficient
  Cheapest method for high-volume printing which works on wide range of materials
  Prints on a wide variety of substrates as well as 3D forms, such as drinks cans
  How do water-based inks reduce the environmental impact?
  Consider how photo emulsion is used in screen printing – how you think a photopolymer plate is formed?

## Slide 15
How does flexo work?
A step by step guide:
  Ink is collected from the reservoir and transferred to the anilox roller
  Tiny cells on the surface of the anilox roller collect the ink
  The doctor blade controls how much ink reaches the flexographic printing plate
  Flexo is a form of relief printing – what does this mean?

## Slide 16
Digital printing
Most of you will use digital printing at home or school
  The two main types of digital printing are ink jet printing and laser printing, both print ink directly onto the substrate
  Digital printers only operate on a four colour printing process – ink/toner cartridges are available in monochrome or CMYK
  How does this affect the printing of spot colours?

## Slide 17
Digital prints
Unlike other print processes, set-up costs are low
  Digital files are sent directly to the printer – no need to make printing plates and each individual print can be customised
  Suitable for a variety of different substrates including textiles
  Quality and speed depends on whether ink jet or laser printing is used as well as the capabilities of the printer
  Used for shorter print runs e.g. pamphlets, brochures, posters

## Slide 18
Laser printing
Electrostatic energy transfers toner to the substrate
  Each colour (CMYK) requires a separate drum in the printer
  The drums are positively charged with electrostatic energy then a laser negatively charges certain areas of the drum
  Positively charged toner powder, sticks to all the negatively charged areas
  A transfer belt picks up toner from all four drums and deposits them onto the substrate in one operation
  Why do fresh printouts from laser printers always feel warm?

## Slide 19
Ink jet printing
This process deposits ink directly onto the substrate
  The printer is loaded with ink cartridges (CMYK) which act as reservoirs for the printhead
  The printhead passes over the substrate from right to left, squeezing out tiny droplets of translucent ink with each pass
  High quality prints (720 DPI or more) need at least six passes to build up the image in sufficient detail

## Slide 20
The drawbacks of digital
The lead time on digital printing is faster than any other process, set-up costs are negligible and each print can be customised – what’s not to like?
  Use of the CMYK process means colours cannot be matched as accurately as other processes e.g. offset litho
  Surface damage is more common as the ink/toner sits on top of the substrate as opposed to sinking in to the surface
  Not cost effective on high volume print runs
  Fewer compatible substrates

## Slide 21
Worksheet task
Complete Task 2 of your Worksheet

## Slide 22
Finishing processes
A variety of finishes can be added to print materials
The processes you will need to know about are:
  Embossing
  Debossing
  How could these finishes enhance a printed product?
  Varnishing methods
  Laminating
  Foil blocking

## Slide 23
Embossing and debossing
These finishes raise or indent the surface of a substrate to add functionality and/or enhance aesthetics
  Braille, commonly found on packaging for medicine, uses embossed dots to enable blind people to read
  Embossing and debossing can be used to add texture, value and a sense of status to paper and board products
  What’s the difference between embossing and debossing?

## Slide 24
How it works
The substrate is stamped between two shaped steel plates under heat and pressure
  The plates shift the fibres of the substrate into a given shape without ripping or cutting
  Often applied without any ink – a technique known as blind embossing
  Why is blind embossing considered an eco-friendly method of conveying a message?

## Slide 25
Foil blocking
A decorative dry process which applies coloured metallic foils to papers and boards
  A profiled metal die, heated to 100-200°C, stamps the foil onto the substrate – flatbed or rotary dies can be used
  Use of heat and pressure bonds the foil to the substrate
  Often combined with embossing and other finishes

## Slide 26
Lamination
Lamination adds a highly durable, tear-proof and wipe-clean film to packaging, posters and books
  The polymer film is bonded to the front and/or back of a substrate to cover the entire surface
  Films are available in matt, silk and gloss as well as metallic, holographic and soft-touch finishes
  Glossy laminates give graphics a punchy, high-contrast look and matt laminates are more subtle
  Why does lamination make recycling harder?

## Slide 27
Encapsulation
Encapsulation is a form of lamination that is carried out using a desktop laminator
  A paper sheet is placed in a plastic pouch and fed into the laminator under heat and pressure
  The plastic fuses to the paper, leaving a telltale transparent margin – this protects even the cut edges against moisture
  It’s not a particularly versatile process in terms of substrate type, size and weight but it’s quick, convenient and very durable

## Slide 28
Varnishing and spot varnish
Varnishes add a protective barrier and offer different finishes and textures
  Applied in liquid form and printed onto a substrate like an ink
  Can cover the entire surface or can be added to specific areas only – this called a spot varnish
  Water-based varnishes dry quickly and are more eco friendly; solvent-based varnishes are half the price but more toxic
  Specialist UV varnish cures under UV light – this varnish is so glossy it’s often mistaken for a lamination

## Slide 29
Quick quiz
Recap your understanding of lamination, encapsulation and varnishing
  Adding a UV varnish is a more complex process. How would this affect the cost?
  How can you tell a laminated material from a varnished one?
  Why is spot varnishing more expensive than applying a varnish edge to edge?
  Which gives the best protection against moisture and why?

## Slide 30
Quick quiz
Recap your understanding of lamination, encapsulation and varnishing
  Adding a UV varnish is a more complex process. How would this affect the cost? Costs would increase
  How can you tell a laminated material from a varnished one? Laminated materials are usually hard to tear
  Why is spot varnishing more expensive than applying a varnish edge to edge? A customised screen/plate must be prepared
  Which gives the best protection against moisture and why? Encapsulation, as the edges of the substrate are sealed

## Slide 31
Plenary
Complete Task 3 of your Worksheet and discuss your responses as a class