## Slide 1
1
AQA
    A Level
      Product Design 7552
Performance characteristics of polymers
Unit 2 Characteristics of polymers and additives

## Slide 2
Be able to describe the performance characteristics of polymers including polymer based sheet and film
Understand how additives are used to enhance the properties of polymers
Objectives

## Slide 3
Starter
Identify which polymer types and forms may have been used in this collection of picnic ware
Discuss which material properties and characteristics you think would be required in each case

## Slide 4
Mechanical properties
Mechanical properties are the characteristics a material displays when subject to an external force
You need to know about:
  Toughness
  Flexibility
  Elasticity
  Mouldability

## Slide 5
Toughness
The toughness of polymers determines their ability to absorb energy and deform plastically without cracking
  Cycle helmets are worn to protect the head in a collision or if you fall
  The polymer material absorbs the energy from the impact and is specially designed to split, dissipating the energy
  Which car parts like ABS utilise polymers for their impact toughness?
  Why are polymers chosen for some car parts over metals?

## Slide 6
Elasticity
Elasticity is a material’s resistance to distortion and ability to return to its original shape
  Polyurethane is used in the textile industry to produce fabrics that have good elasticity
  Balloons are made from polymers called elastomers such as rubber or latex
  If you blow up a balloon and then deflate it, does it return to its original shape or has it been elastically deformed?
  What other polymer products are routinely inflated and require excellent elasticity?

## Slide 7
Flexibility and folding
Flexibility is the ability of a material to be bent or folded without breaking whilst stiffness is a measure of how rigid a material is
  Flexible PVC sheet is often sold by the roll and used for protective coverings – film is used for laminating
  Thermoplastics vary in their level of flexibility, often relating to their thickness in comparison, thermosets tend to be very rigid and stiff when set
  What happens if you repeatedly fold a piece of flexible high impact polystyrene (HIPS) sheet along the same axis?
  If the same movement was applied to a piece of sheet metal, what would the result be caused by?

## Slide 8
Mouldability
A polymer’s ability to be shaped into a form or mould will dictate the type of product it is used for
  Thermoplastics are usually moulded in a hot or molten state, usually under mechanically exerted pressure, using compressed air, hydraulics or rotation
  Thermosets are usually moulded in cold liquid form and cured (set) using a catalyst (hardener)
  What method is commonly used to mould a thermoplastic sheet over a former in the school workshop?

## Slide 9
Ability to be cut and scored
The ability of a material to be scored, cut and folded depends upon the hardness of the material
  Acrylic is hard and easily scored and ‘snapped’ however it may chip or crack when machine cut
  HDPE and HIPS are softer and more flexible so will score less well but can be cut more easily without chipping
  What tools would you use to cut thin thermoplastic sheet and film such as in a workshop?
  What methods are used in industry for cutting the plastic film used to create plastic carrier bags?

## Slide 10
Worksheet Task
Complete Task 1 of Worksheet 1

## Slide 11
Physical properties
Physical properties are the measurable characteristics a material displays
You need to know about:
    Insulation
    Self finishing
    UV resistance
    Melting points
    Transparency and translucency
    Resistance to chemicals and liquids
    Ability to be combined with other polymers and additives

## Slide 12
Thermal insulation
Thermal insulators reduce heat transfer, especially between objects and people
  The insulating properties of polymers are exploited in products such as saucepan handles and kitchen utensils
  Some polymer materials are formed with air trapped inside them to create foams that are used as insulation in packaging and in the construction industry
  Why might a thermosetting polymer be used for saucepan handles rather than a thermoplastic?

## Slide 13
Electrical insulation
An electrical insulator is a material that does not allow electricity to flow freely through it
  Polymers are very good electrical insulators, making them especially useful for electrical product casings and shielding
  Electrical light fittings and sockets are often made from urea formaldehyde, a thermoset which is heat and burn resistant - Why is this important?
  How could the manufacture of this screwdriver further improve its electrical insulation to protect the user from electrical shock?

## Slide 14
Melting points
A melting point is the temperature at which a material changes state from solid to liquid
  When heated, thermoplastics become soft, pliable and ‘plastic’ and can then be shaped and moulded
  The melting point of a polymer will often dictate its application
  Thermosetting polymers do not melt but start to decompose and char at high temperatures
  What are the health and safety implications of melting some plastics?

## Slide 15
In the same way that skin is burnt by exposure to the sun, polymers are also effected by its UV radiation
  UV ‘bleaches’ the colour from polymers like ABS, which is commonly used for products such as garden furniture
  It also effects the polymer’s mechanical properties, degrading it and making it more brittle
  Acrylonitrile styrene acrylate (ASA) has been developed as an alternative for ABS as it retains its colour and has greater UV resistance
UV resistance

## Slide 16
Some polymers are selected specifically for their chemical resistance
  High density polyethylene (HDPE) is particularly resistant to chemicals and is used to manufacture bleach bottles and chemically resistant piping
  HDPE is also used in large sheets to line landfill sites, acting as a barrier between the waste and the soil
  What are the risks if chemicals from landfill leach into the soil?
Resistance to chemicals

## Slide 17
Generally most polymers are resistant to liquids however the length of time they can be used varies
  Both HDPE and Polyethylene Terephthalate PET are used in plastic water bottles however there are differences
  HDPE is reusable and recyclable
  PET is recyclable, but should not be reused as overtime the plastic may leach chemicals into the water
  What do we call polymers that are not designed to be reused?
Resistance to liquids

## Slide 18
Suitability for food packaging
Polymer films and moulded polymer sheet are commonly used in many types of food packaging
  They hygienically protect the goods inside by creating a barrier to oxygen, liquids, foreign airborne bodies and tampering
  They prolong the shelf life, help keep the flavour and protect the quality of the contents
  How has plastic packaging changed the way we buy and use our food?

## Slide 19
Problematic food packaging
Food packaging takes on various forms from pots, trays and boxes to film, bags and bottles
  Films and bags can be heat sealed to keep the food inside airtight and fresh
  Some bags, films and trays are specifically designed to allow the food to be cooked whilst still packaged
  Many ready meals come in film sealed black plastic trays
  What problems arise when it comes to recycling packaging like this?

## Slide 20
Transparency
Transparency dictates how permeable a material is to light radiation – how see-through it is
  If it is translucent, some light may pass through but will be diffused and objects on the other side will not be clear
  If it is opaque it is impermeable to light
  What applications may there be for a translucent polymer?
Clear polymer sheets and films are popular in applications where visibility is important
  As a replacement for glass in windows and signs
  In packaging to allow the buyer to see the contents

## Slide 21
Self-finishing
Polymers are widely regarded as self-finishing which means no additional surface finishing is required
  In manufacture, the surface of the mould, whether smooth and highly polished or textured, will dictate the surface finish
  Pigments can be added to polymers pre-production, removing the need for secondary surface colouring
  In a school workshop, why might polymers require finishing post-production?

## Slide 22
Worksheet Task
Complete Task 2 of Worksheet 1

## Slide 23
Additives for processing
Additives are sometimes used to make polymers easier and more efficient to process
  Plasticisers enhance flow characteristics and enable polymers to be moulded at higher temperatures
  Thermal antioxidants help to prevent oxidation due to heat exposure during the manufacturing process
  Lubricants improve polymer flow by decreasing viscosity
  How might this aid the injection moulding process?

## Slide 24
Additives for performance
Additives may also prolong the lifespan of products
  Antioxidants reduce the degradation and deterioration from exposure to air and water and help prevent cracking and discoloration
  UV light stabilisers help improve the material’s resistance to degradation by UV light
  Which type of products are particularly vulnerable to oxidation and degradation?

## Slide 25
Additives to improve function
Additives are used to enhance the performance characteristics of polymers
  Fire retardants increase the material’s resistance to fire
  Plasticisers are used to make materials more stretchy
  Antistatic additives are used to reduce the build up of static charge
    Fillers including sawdust and minerals can be used to add bulk and improve the properties of the polymer – What functions do you think these provide?

## Slide 26
Additives for biodegradability
Additives are also used to increase the biodegradability of thermoplastic polymers
  Thermoplastics degrade very slowly, ultimately breaking into particles that will not assimilate into the soil but instead pollute and find their way into the food chain
  Bio-batch materials are additives that enable a thermoplastic to biodegrade meaning they can be broken down more quickly and safely by natural bacteria
  Bio-batch materials are used in plastic films – What type of products might these films be used to create?

## Slide 27
Recyclability
Recycling is the process of recovering waste polymers and reprocessing them into useful materials and products
  Recycling polymer waste prevents it from being sent to landfill or dumped
  It reduces reliance on the production of new material from finite resources
  How can we tell if plastic products are recyclable?
  What are the major obstacles to polymer recycling?

## Slide 28
Plenary Task
Complete the Plenary Task 3 on your Worksheet