## Slide 1
3
AQA
    A Level
      Product Design 7552
Stock forms and types of polymers
Unit 2 Performance characteristics of polymers

## Slide 2
Be aware of the different stock forms of polymers including sheet, film, granules, rod and other extruded forms, foam and powder
Explain why different polymer based sheet and film are suitable for a range of different applications
Objectives

## Slide 3
Stock Forms
Polymers are available in a wide range of stock forms
    Sheet
    Film
    Granules
    Rod and other extruded forms
    Foam
    Powder
Which factors might affect the selection of stock form for polymers?

## Slide 4
Sheet
Sheet is one of the most recognisable polymer stock forms and is available in a range of different types
  Solid cast or extruded sheet
  Fluted sheet
  Laminated sheet
Sheet polymer may be used in flat form or may be cut or moulded
  What machine would you use to cut multiple identical key fobs from a sheet of 5mm acrylic?
  How would you produce the outer casing for a toy car from a HIPS sheet in the school workshop?

## Slide 5
Film
Polymer film is commonly associated with clear food wrap however it comes in a variety of forms
  Packaging film
  Membranes
  Carrier bags
  Photographic film
  In what type of composite materials are polymer film membranes used and what purpose do they serve?

## Slide 6
Granules
Many thermoplastics are produced in granule form for easy processing when making moulded forms
  Granules can be measured accurately and melt more quickly
However granules have other uses
  PVC and rubber granules are also used for sports and playgrounds surfaces and even for filling soft toys
    Tiny plastic granules have been used in cosmetic products
    What are these called and what problem do they pose?

## Slide 7
Rod
Extrusion is the method by which polymer granules like Nylon and PP are melted and formed into a continuous profile
  Rod comes in a range of dimensions and is often used in the manufacturing of precision plastic parts including:
    bearing
    gears
    seals
    Why might polymer bearings be used in applications where they come into contact with food?

## Slide 8
Other extrusions
A range of more complex extruded forms can be produced by using metal profile dies
  Various thermosetting polymers can be extruded including PVC, PP and HDPE to form products such as:
    tubing
    window frames
    edging, seals & moldings
    adhesive tapes & wire insulation
    What type of additives may be added to the polymer mix prior to extrusion?

## Slide 9
Foam
Foams are commonly produced using a combination of polymer, additive / catalyst, heat and air or gas
  When mixed, the material to expands and tiny gas bubbles are trapped and then burst, creating a spongy porous foam
  Foams have many uses including:
    exercise and sleeping mats
    packaging and insulation
    soft furnishings
    model making
    Can polymer foams be recycled?

## Slide 10
Powders
Polymer powders are often used as a coating for metal surfaces to protect them against corrosion
  Electrically charged or heated metal parts are dipped or sprayed in powdered polymer to create coatings on:
    railings
    bike and car parts
    household appliances
  Powdered polymers are also used in 3D printing to produce prototypes where they are cured or sintered by a laser

## Slide 11
Foam board
Foam board is a lamination of two white card face layers sandwiched around a foam core
  Foam boards are lightweight and easy to cut and score, having a variety of uses including presentation boards framing artwork and model making
  Solvent-based adhesives must be used carefully as they can melt the foam core, making joining parts more difficult
    What functional opportunities do the card faces present?

## Slide 12
Fluted polypropylene
Fluted PP is a lightweight extruded sheet with integrated channels or flutes which is available in a wide range of colours
  Also known by the trade name Correx®, it is often used for display and signage such as an estate agent’s ‘for sale’ board
  It is easily creased and bent lending itself to net construction for applications like foldable boxes, folders and folios
  What properties make this an ideal material for transporting artwork?

## Slide 13
Translucent polypropylene
Translucent PP sheet is a very tough, tear and water resistant material that may be coloured or clear and can be printed on and laser cut safely
  It is very flexible and can be scored and folded to create an envelope style opening or a polymer hinge
  It is often used for document folders and lightweight boxes as well as strong plastic packaging
    Translucent PP sheet has high light transmission – What type of school-based projects is this useful for?

## Slide 14
Styrofoam®
Often used in the school workshop, Styrofoam® is a dense extruded foam that is usually blue in colour
  It is available in sheet and block form in a range of thicknesses and can be cut and shaped with a variety of tools including a hot wire
  It is commonly used for model making
  It can also be used for making robust moulds and formers
  What precautions should be taken when cutting and sanding Styrofoam?

## Slide 15
LDPE sheet
Low density polyethylene sheet is a tough flexible material with very good chemical resistance
  It is available as a very thin film or sheet, making it a practical solution for applications including:
  Food wrap and bags
  Carrier, bin and freezer bags
  Packaging including air pillows and bubble wrap
  What makes this material ideal for use as a pond liner?

## Slide 16
Plastazote® foam
Plastazote® is an engineered foam which is tough, flexible and very lightweight
  It has excellent impact resistance making it ideal for use in protective packaging, protective sportswear
  It is also used for exercise and yoga mats
  Its insulating properties make it useful for piping covers
    Why is it an ideal material for making roll mats used by hikers and campers?

## Slide 17
Cellulose acetate
Cellulose acetate is a tough, transparent, naturally derived thermoplastic film that is biodegradable
  Cellulose acetate film was introduced in the early 1900s as a photographic film and is still used for this application to this day
  Other uses include a biodegradable packaging material
  How can vintage cellulose acetate movie film be stored to reduce the likelihood of degradation?

## Slide 18
Polylactide sheet and film
Also known as Polylactide acid or PLA, this is a biodegradable polymer
  It is made from renewable resources like corn starch or sugar beet
  It is also compostable and recyclable
  It is commonly used as a sustainable alternative to petrochemical based packaging such as PET
  A huge amount of corn is needed to produce PLA
  What problems might arise as demand for the material grows?

## Slide 19
Worksheet 3
Complete Tasks 1 and 2 of your Worksheet

## Slide 20
Plenary
Name six different stock forms
How is the profile made on extruded stock forms?
What are the ingredients used when making foam?
When might powdered stock forms be used?