## Slide 1
2
AQA
    A Level
      Product Design 7552
Performance characteristics of smart materials
Unit 5 Composite, smart and modern materials

## Slide 2
Define the term smart material
Describe how smart materials respond to a given stimuli
Explain the suitability of smart materials within a given context
Objectives

## Slide 3
Starter
What makes materials smart?
  How would you expect a smart material to behave?
  Describe a smart material you are familiar with

## Slide 4
What is a smart material?
Smart materials have one or more property that is dramatically altered by an external stimulus
  Properties such as colour, shape, viscosity, volume and conductivity are affected by a given stimulus
  The stimulus and the properties linked to a smart material affect how and where it is used
  What kinds of external stimuli might affect a smart material?

## Slide 5
External stimuli
All materials are affected by their environment to some extent
  For example, wood swells in moist conditions and most metals become brittle at extreme temperatures
  Smart materials show dramatic changes according to subtle environmental differences
  External stimuli include changes in temperature, levels of light, moisture and pressure

## Slide 6
Examples of smart materials
You will need to be familiar with the following smart materials:
  Shape memory alloys
  Thermochromic pigment
  Phosphorescent pigment
  Photochromic pigment
  Electroluminescent wire
  Piezoelectric material
  Complete Task 1 to explore these smart materials further

## Slide 7
Shape memory alloys
Shape memory alloys (SMAs) can be "programmed" to remember a specific shape
  When SMAs are bent out of shape, they will return to their programmed shape at a given temperature
  SMAs can be activated by changes in weather, body temperature and even electrical current
  A common SMA is nitinol – an alloy of nickel and titanium
  How could SMAs be programmed?
Notes: Fade the arm behind the writting

## Slide 8
Programming SMAs
SMA is programmed into a given shape with heat or a high electric current
  The SMA is held in the desired shape using a jig, then heated in a furnace or with a flame or with electric current above the transformation temperature
  Once cooled, the SMA can be deformed and will return to the shape dictated by the jig when heated
  The activation temperature needed to stimulate reforming is dictated by subtle changes in the composition of the alloy

## Slide 9
SMAs in use
SMAs are commonly used in glasses frames, orthodontic braces and heat sensitive valves
  SMAs are used in orthodontic wire – body heat affects the wire which gently pulls the teeth into position
  SMAs are expensive so only commercially viable in high-cost commodities
  How could SMAs be used in a tap to prevent scalding?
https://www.youtube.com/watch?v=2lv6Vs12jLc

## Slide 10
Worksheet task
Complete Task 2 of Worksheet 2

## Slide 11
Thermochromic pigment
Thermochromic pigment changes colour or opacity with a change in temperature
  The pigment can be mixed into materials and finishes such as varnishes, paints, dyes as well as polymers
  It may transform from opaque to transparent or change colour
  How can thermochromic pigment be used to improve safety?

## Slide 12
Phosphorescent pigment
Phosphorescent or glow in the dark materials respond to light
  Phosphorescent materials absorb energy from natural / artificial light sources and emit light in the dark
  Typically, the glow will fade within a few hours in a dark environment
  Commonly used in watch faces, toys, stickers, paints and safety signs e.g. fire exit signs

## Slide 13
Photochromic pigment
This smart material changes colour or opacity with the level of ultraviolet light in a reversible reaction
  Commonly used in spectacles, clothing and novelty items
  Like all smart pigments, photochromic pigment can be used as an additive to affect the properties of other materials and finishes

## Slide 14
Electroluminescent wire
This material is made from copper wire coated in phosphor which glows when an alternating current is applied to it
  Electroluminescent (EL) wire has a pliable plastic coating so it’s flexible and suitable for use outdoors
  Unlike LED strip lighting, EL wire produces a 360° unbroken thread of light
  Used in lighting, accessories for bicycles, vehicles and costumes

## Slide 15
Worksheet task
Complete Task 3 of Worksheet 2
https://youtu.be/-qC8GyKOTgc

## Slide 16
Piezoelectric materials
These materials convert mechanical energy into electrical energy, and vice versa
  Pressure or vibrations is converted to electrical charge which can be used or stored for later use
  Piezoelectric materials include crystal, ceramic, bone and even viruses
  Piezo electricity is used to create a spark in lighters, trip burglar alarms and generate the sound for fire alarms
  Discuss how PE materials would be used in each of the products listed above
https://www.youtube.com/watch?v=ce4rz-Qx1A0

## Slide 17
How are they used?
One of the first uses for piezo electric materials was in ultrasonic detectors for submarines used in WWI
  A grid of quartz crystals held between two steel plates resonates when electric current was applied
  This cell emits sound underwater – the underwater terrain was measured by timing the return of the echo
  This is the basis of all sonar and ultra sound technology

## Slide 18
Wearable technology
Many of you will be wearing piezo electric materials
  If you have a digital watch, the chances are, it contains a quartz crystal component which helps keep time
  Watch the link video to find out more
https://www.youtube.com/watch?v=1pM6uD8nePo

## Slide 19
Plenary
Give some examples of external stimuli that could affect a smart material
How could smart materials be used in a nightclub?
Can smart materials be used to increase safety?
Which smart material could read your pulse rate?
Which smart materials are affected by light levels?
Which smart materials can be affected by electrical charge?