## Slide 1
3
AQA
    A Level
      Product Design 7552
Performance characteristics of modern materials
Unit 5 Composite, smart and modern materials

## Slide 2
Define the term modern material
Describe the key properties of a range of modern materials
Explain the suitability of a modern material for a given application
Objectives

## Slide 3
Starter
How could a fabric save your life?
How would you feel if you had to a trust fabric to stop a bullet?

## Slide 4
What are modern materials?
Modern materials are developed by engineers and scientists through research and experimentation
  They are sometimes discovered by accident but usually are developed to perform a particular function
  Modern materials are developed for specialist applications but many make their way into a range of products due to their enhanced properties
  Give some examples of modern materials?
Notes: Design – blend image to a black/grey green background

## Slide 5
What you need to know
You will need to be familiar with the following modern materials:
  Kevlar
  Polymorph
  Precious metal clay
  High density modelling foam

## Slide 6
Kevlar®
Kevlar is a lifesaving material
  This high performance aramid fibre is spun into thread and woven into fabric that can stop a bullet and offer thermal protection at over 120°C
  It’s lightweight, hardwearing and extremely strong and stiff
  It is heat and chemical resistant and five times stronger than steel
    Kevlar is used in bulletproof vests but where else might it be used?

## Slide 7
Discovering Kevlar
Kevlar was discovered in 1965 by Stephanie Kwolek at DuPont laboratories
  DuPont wanted a strong, stiff and lightweight material that could be used as an alternative to steel reinforcements in tyres
  As a fabric, it’s used in high performance protective clothing and accessories
  As a fibre, it’s used as an additive to enhance the performance of composite materials
https://www.youtube.com/watch?v=L1pepaAdkWA&t=833s

## Slide 8
Increased safety and efficiency
Kevlar fibres have excellent impact resistance as well as tensile and torque strength
  High performance vehicles for land, sea and air use Kevlar to create tougher, safer and lighter products
  The Eurofighter is made from material reinforced with Kevlar – this allows it to fly faster and farther before needing to refuel

## Slide 9
Worksheet task
Complete Task 1 and 2 on Worksheet 3
Notes: Image from https://www.wunderstore.co.uk/Sports/Cycling/Helmets-and-Accessories/Brand-Troy-Lee-Designs

## Slide 10
Polymorph
This a thermoplastic modern material which becomes malleable at low temperatures
  When heated in hot water to 62° it’s easy to mould by hand and can be remoulded many times
  Once cooled, it is extremely tough and durable with similar properties to nylon
  It’s also non-toxic and biodegradable
  Why is polymorph considered to be a user-friendly material?

## Slide 11
Enhanced ergonomic design
Polymorph can be used safely and easily at home
  It’s used to create personalised and ergonomic products and parts such as handles, orthodontic moulds and gum shields
  Particularly useful for the elderly or those with disabilities or deformities
  Suggest some products that could be enhanced with polymorph

## Slide 12
Precious metal clay
Precious metal clay (PMC) is made from precious metal particles held in a water-based, non-toxic organic binder
  PCM can be shaped by hand or with moulds and formed like any modelling clay
  The moisture and binding agents are burnt off during the firing process – the finished product contains over 90% precious metal
  PCM shrinks by about 5-15% during firing
  What are the benefits of using PMC over traditional techniques?

## Slide 13
PMC pros and cons
PMC is an accessible material as it can be used with minimal tools and metalsmithing skills
  It’s easy and quick to work with and can be fired in a kiln or with a butane torch
  It can be used to set stones and slip can be used to join PMC parts
  However, it can dry out if it is worked or stored for too long and it is not as strong as sterling silver
  It’s more expensive than traditional materials but set up costs are minimal
https://www.youtube.com/watch?v=d3WXnUyoSok

## Slide 14
High density modelling foam
HDMF is a rigid, lightweight and strong material used for high quality 3D models
  HDMF holds good surface detail and fillers, primers and paints can be used to create a high quality finish if desired
  It can be CNC milled or routed or shaped by hand
  A cheap and quick way to make moulds for vacuum forming and casting metals at low temperatures
  How is HDMF superior to other materials used for making solid 3D models?

## Slide 15
Worksheet task
Complete Task 3 on Worksheet 3
Notes: Image from https://www.wunderstore.co.uk/Sports/Cycling/Helmets-and-Accessories/Brand-Troy-Lee-Designs

## Slide 16
Plenary
Modern materials are used in design development as well as in final products
  How could modern materials be used in the design and development process of this helmet?
  Which modern materials could be use to make the final product?