## Slide 1
5
AQA
    A Level
      Product Design 7552
Biodegradable polymers
Unit 2 Performance characteristics of polymers

## Slide 2
Be able to explain the suitability of biodegradable polymers for given applications, making reference to their physical and mechanical properties
Understand how biodegradable polymers degrade
Be familiar with a range of biodegradable polymers
Objectives

## Slide 3
What happens next?
At end of life, if thrown into landfill:
  what would happen to a conventional plastic bag labelled ‘degradable’?
  what would happen to a bag labelled ‘biodegradable’?

## Slide 4
Degradable or biodegradable
All polymers are degradable, but some may take a 1000 years or more to do so
  Those called ‘degradable’ do so by breaking down very slowly into tiny plastic particles which do not assimilate back into the earth but remain, pollute and can get into the food chain
Biodegradable polymers are those that decompose due to the presence and action of living organisms
  Biodegradable polymers will break down without oxygen and turn into carbon dioxide, water and biomass, finally assimilating, however this can still take several years

## Slide 5
Compostable
There is some confusion over the differences between biodegradable and compostable
  Compostable means that the material breaks down under certain specific conditions into carbon dioxide, water, inorganic compounds and biomass
  It takes a much shorter time and leaves no toxic residue
    Not all compostable polymers can be done so in domestic compost – what problems might this cause?

## Slide 6
Biodegradable polymers
Biodegradable polymers or biopolymers fall into two categories:
  Those that are made from renewable raw materials including sugar and plant starches such as Polylactic acid (PLA)
  Those that are manufactured from petrochemicals with the addition of biodegradable additives (bio batch) which aid degradation
https://www.youtube.com/watch?v=PTM5WTJkHR0

## Slide 7
Oxy-degradation
Some biodegradable polymers are designed to break down when exposed to oxygen
  An additive is often used in plastic carrier bags to speed up the process
  The time it takes to break down can be ‘built in’ to the material
  First the material flakes, then, over a few months or years, the flakes turn to a powder
https://www.youtube.com/watch?v=vWne99E_zAw

## Slide 8
Photo-degradation
Polymers that are photo-degradable will start to break down when exposed to UV light
  Some weed suppressant sheeting is photo-degradable and can be used to temporarily block out light preventing growth until they break down
  These are commonly used in domestic gardens and allotments, commercial nurseries and agriculture
    What other benefits does photo-degradable weed suppressant sheeting offer gardeners?
Notes: Used a s a mulch to keep crops/plants warm

## Slide 9
Hydro-degradable
As the name implies, these polymers are designed to degrade and dissolve when exposed to water
  These polymers are ideally suited to applications that require a hygienic or leak-free seal before exposure to water
  Laundry liquid pods
  Hospital laundry bags
  Casings and capsules for vitamins and medicines
  Discuss some other applications for hydro-biodegradable polymers

## Slide 10
Worksheet Task
Complete Task 1 of Worksheet 5

## Slide 11
Corn starch polymers
Corn starch polymer is a naturally derived biopolymer which is commonly used in packaging and for single use applications
  It can be extruded to produce a sheet or film and can be injection moulded and used in 3D printers
  It is food safe and resistant to fats
  It is oxy-biodegradable
  It is UV resistant
  It is printable
https://www.youtube.com/watch?v=R2noqvlBxZk

## Slide 12
PotatoPak
PotatoPak is another starch based, compostable, natural biopolymer but made from potatoes
  Powdered polymer is inserted into a mould which is heated under pressure to make a rigid shape
  It is used for single use plastic items such as plates and bowls, food trays and cutlery
  By using an additive it can also be expanded and made into for packaging pellets
https://www.youtube.com/watch?v=ual_5N5Dw74

## Slide 13
Biopol®
Biopol® is the trade name for Polyhydroxybutyrate (PHB) a natural biopolymer made from bacteria
  It can be moulded, formed and extruded and can be used as an additive to promote bio-degradation in other thermoplastics
  It is made in to a range of disposable items including shampoo bottles, disposable razors and in the lining of nappies
  It has good UV resistance and does not dissolve in water

## Slide 14
Polylactide acid (PLA)
PLA is a synthetic biopolymer fermented and synthesised from corn starch
  PLA is used for packaging products including water bottles, carrier bags and plant pots
  It can be moulded, formed and extruded and is commonly used as polymer filament for 3D printing
  PLA can be recycled
  What are the benefits of using a biodegradable polymer in the manufacture of plastic plant pots?

## Slide 15
Polyhydroxyalkanoate (PHA)
PHA is a natural, compostable biopolymer powder made from mixed organic waste and fermented bacteria cultures, water and oxygen
  PHA is food safe and so is ideal for use in food packaging, bottles and films as well as plastic cutlery and crockery
  It can be formed and moulded like conventional thermoplastics
  It is also used in surgical fixings like screws and bone plates as well as sutures and drug delivery patches
  What makes it appropriate for this use?
https://www.youtube.com/watch?v=YWs_VVLNWC0

## Slide 16
Lactide
Lactide is a synthetic PLA based polymer
  It is compostable and hydro-degradable and its various applications utilise this property
  It has many biomedical application including use in pill and capsule casings as it allows the slow release of the medication
  It is also used in detergent pods
  How should these products be stored to ensure they do not prematurely degrade?
https://www.youtube.com/watch?v=KppS7LRbybw

## Slide 17
Glycolide
Similar to Lactide, Glycolide is also a synthetic PLA based polymer, it is available as a sheet and a film
  It is also known as Ecofilm and can be extruded to produce fine films for use in food packaging, packaging wraps and in floristry as a flower wrap
  It has similar properties to LDPE but is much stronger and is also used to make bags, bin liners and horticultural sheeting
  LACTEL is a company specialising in glycolide and other PLA derivatives
https://www.ecofilm.com/
http://www.absorbables.com/

## Slide 18
Worksheet Task
Complete Task 2 and 3 of Worksheet 5

## Slide 19
Plenary
Define the difference between degradable and biodegradable
What is PLA made from and what is its common use in schools?
Describe three different ways that polymers tend to degrade
What are the issues with recycling biodegradable polymers in the normal household recycling stream?