## Slide 1
4
AQA
    A Level
      Product Design 7552
Elastomers
Unit 2 Performance characteristics of polymers

## Slide 2
Be able to explain the sustainability of elastomers for given applications
Be able to make reference to relevant properties including the ability to be stretched and return to original shape, texture, finish and toxicity
Understand how elastomers including natural rubber, polybutadiene, neoprene and silicone are used to enhance products
Objectives

## Slide 3
Elastomers
Elastomers are polymers that are highly elastic and capable of recovering their original shape after being stretched
  Most elastomers are thermosets
  The polymer chains making up an elastomeric material are irregularly coiled and cross-linked
  When stretched, the molecules will straighten out in the direction of pull
  What happens when the materials is released?
  Name some elastomers and their uses

## Slide 4
Thermoplastic elastomers
Thermoplastic elastomers known as TPEs are polymer blends which can be heated and moulded without forming cross links
  Most TEPs are known by their trade names for example Elastron® & Riteflex®
  They display similar properties to the cross linked elastomers like rubber
  TEPs offer faster processing times than cross-linked elastomers
  Can TEPs be reprocessed?

## Slide 5
Stretching
All elastomers are flexible and elastic meaning that they can be stretched and still return to their original shape
  This property varies depending on the elastomer but can be very useful especially where the material will:
  expand or contract due to temperature changes
  be inflated and pressurised
  worn to compress an injury or keep water out
  Will elastomers continue to spring back over prolonged use?

## Slide 6
Grip
As flexible, impact absorbing materials, elastomers can be used to enhance the ergonomics of products
  These may take the form of sleeves or handles
  Over moulding is also used to create spongy grips and textures on other thermoplastic products
  These can be found on products like torches, pens, toothbrushes and sports bottles
  What is the disadvantage of over moulding when it comes to disposal?

## Slide 7
Texture
Elastomers are self-finishing but their finish will depend on the way they were processed
  Most elastomers can have textures pressed or rolled into them
  They can also be cast in textured moulds
  Natural and synthetic rubber are naturally smooth whereas open cell neoprene has a spongy texture and silicone rubber feels very silky to the touch
  Texture can be aesthetic, but in what way can it improve usability?

## Slide 8
The 1st elastomer
Natural rubber is obtained by tapping the milky sap of the rubber tree, it is also known as Indian rubber
  Brought to Europe in the late 15th century by Christopher Columbus from South America, its properties were only fully realised in 19th century
  It was used for flexible tubing
  Tyres and innertubes
  Waterproof clothing
  Rubber balls
  Balloons

## Slide 9
Vulcanisation
Vulcanisation is a process used to cure rubber making it harder, more durable and heat resistant
  A curing agent, sulphur, is added to the latex from the rubber tree
  When heated and pressurised, the sulphur atoms form cross links
  Vulcanised rubber is tough and can more easily retain its shape

## Slide 10
Natural rubber
Natural rubber is a mouldable, self finishing material
  It has excellent tensile strength, is tough, elastic and is hard and compared to other elastomers
  Natural rubber is a good insulator and can withstand low temperatures
  It is commonly used for in the automotive industry for gaskets, hoses and belts
  What makes rubber an excellent material for soling shoes?
https://www.youtube.com/watch?v=y6CJ6ojMT0A

## Slide 11
Safe to use
Natural rubber is non-toxic and so is safe for use in products that come into contact with the skin or may be sucked or chewed like teats for babies bottles
  It is also used for washing up gloves, swimming hats and verruca socks, all of which are required to stretch and provide a non-permeable barrier
  Some people are allergic to natural rubber (latex) and it can cause a severe skin reaction

## Slide 12
Polybutadiene
Polybutadiene or butadiene rubber (BR) is a strong synthetic rubber which is highly resistant to wear
  BR shares many of the properties of natural rubber
  It is particularly wear resistant against friction making it an excellent choice for hiking shoes
  It also has excellent thermal resistance against friction which is why it is used for specialist tyres for racing cars
  Suggest applications for butadiene rubber sheet and matting

## Slide 13
Worksheet Task
Complete Task 1 and 2 of Worksheet 4

## Slide 14
Neoprene
Neoprene® is polychloroprene rubber (PC rubber) which comes in both closed and open cell forms
  In its closed cell form it has a similar appearance to rubber and is dense, smooth, weather and heat resistant,
  In open cell form, it is more spongy and less dense
  Neoprene is more resistant to degradation than natural or synthetic rubbers and is used in applications such as hoses, door seals and gaskets
  Why would closed cell neoprene seals be used on the internal doors in a block of flats?

## Slide 15
Making a splash
Neoprene® is pliable and often used as a textile, it is probably most well known for its use in wetsuits
  It can be cut, stitched and glued
  Neoprene is stretchy, breathable and waterproof and is now commonly used in clothing and sports braces
  It is also used to make laptop and tablet cases and even some pencil cases
  Why is neoprene often used as an outer sheath for the handles of gym equipment?
https://www.youtube.com/watch?v=JkqBWJslHLw

## Slide 16
Silicone
Silicone rubber is a very stable, non-reactive material that is resistant to extreme temperatures
  Silicone rubber is widely used in homewares including ice trays, bakeware, kitchen utensils and oven gloves
  It is also used for watch straps, bracelets and hairbands
  It does not resist abrasion well but can be self-lubricating and is usually smooth to the touch
  What benefits would a silicone rubber ice tray have over a traditional rigid plastic one?

## Slide 17
Silicone in industry
Silicone is commonly used in industry and has wide ranging applications including:
  For seals and as a sealant
  For mould making
  As a lubricant
In its cured state it is non-toxic and it is also known for its use in medical implants and prosthesis

## Slide 18
Plenary
Complete Task 3 and 4 of Worksheet 4