## Slide 1
AQA
    A Level
      Product Design 7552
Working with polymers
Unit 7 Processing and working with polymers
1

## Slide 2
Be aware of how polymers can be formed into 3D shapes and products
Be able to explain the suitability of a range of different forming methods for a range of specific products and scales of production including extrusion and calendaring
Objectives

## Slide 3
Starter
Polymers have had a bad press recently
    Why is this?
    Is the material entirely to blame?
    How has our ability to form and deform polymers positively changed our lives?

## Slide 4
Scales of production
Whilst we might immediately associate plastic products with mass and continuous production methods, polymers are used at all scales of production

## Slide 5
One-off production
Crafts people and artists create a wide spectrum of hand made, one-off or bespoke products from sculptures to handmade furniture
  These are usually time consuming, require a high level of skill and will usually be expensive to produce
  Resins are commonly used for their decorative qualities
  For what application might you use polyurethane varnishes in a school workshop?

## Slide 6
Batch production
Batch production is a broad term for production runs of anything from ten to tens of thousands of products
  Consistency is vital therefore, jigs, templates and patterns are used to aid replication
  Processes are more highly mechanised than in one-off production
  Moulded furniture and toys and are often batch produced
  Why is batch production ideally suited to the production of some packaging products?

## Slide 7
Production aids
Jigs aid manufacture and speed up repeat processes adding increased accurately
  Jigs can help make accurate angles when line bending
  A jig might be used to help fold a polymer sheet and to make sure that folds run perpendicular to the edges of the sheet
  Jigs may help with positioning and dimensioning for example when drilling a hole
  How does the use of jigs increase efficiency in batch production?

## Slide 8
Patterns
Patterns are the positive forms used in resin casting to produce negative moulds
  The moulds enable identical copies to be made
  Patterns can be made from a range of materials including clay, wood and silicone rubber
  What are patterns usually sprayed with before they are cast to create moulds?

## Slide 9
Moulds
Moulds themselves may be made from a range of materials depending on a variety of factors including how many times the mould will be used and what is being cast or moulded
  Materials used include Plaster of Paris, silicon rubber, latex and GRP
  Moulds used for vacuum forming in school may be made from wood, MDF and Styrofoam™
  In industry, moulds are frequently made from tool steel – What does this ensure?

## Slide 10
Mass production
Mass production uses a production line to produce high numbers of identical products quickly
  It is more highly automated than batch production and requires less skilled labour
  Common day to day products such as food packaging, plastic bags and cups are usually mass produced
  Materials for mass production are generally purchased in bulk
  Set-up costs are high, so what factors help to lower unit costs?

## Slide 11
Continuous production is similar to mass production using a production line to manufacture quantity
  Only one product is made with very few, if any alterations
  As the name suggests, there is no downtime
  This is ideal for products such as HDPE milk bottles, PET drinks bottles and film used for refuse sacks and other plastic bags
  What makes continuous production suitable for these products?
Continuous production

## Slide 12
Worksheet
Complete Task 1 of Worksheet 1

## Slide 13
Calendaring
Calendaring is a production process using a series of rollers to produce a thin polymer sheet or film
  Polymer pellets are heated and softened
  The softened polymer feedstock is extruded through a series of heated rollers
  This flattens and stretches the polymer
  The final rollers cool the sheet and it is either rolled or cut to length
  What is calendared plastic sheet or film used to manufacture?
https://www.youtube.com/watch?v=0E5L_SsPxDE
https://www.youtube.com/watch?v=3yzaCEUwkqw

## Slide 14
Extrusion
Extrusion is a production method used to create a continuous flow of plastic that is pushed through a die to create a specific profile
  Extrusion is used for cables, pipes, mouldings, tubes, seals and window and door frames
  It is used to create the plastic film used for bags and packaging as well as the plastic filament used for 3D printing
  Is much waste produced during the extrusion process?

## Slide 15
Extrusion process
The extrusion process starts off in a similar way to injection moulding, using a die instead of a mould
  The die sets the profile of the extruded plastic and must be made to a very precise tolerance
  A continuous flow of the softened plastic passes through the die at just the right temperature and flow rate to hold the shape
https://www.youtube.com/watch?v=wE_KTLlrdMA

## Slide 16
Worksheet
Complete Task 2 of Worksheet 1

## Slide 17
Plenary
Which scale of production offers the lowest unit cost and are there any downsides to this?
Name four different polymer products that are extruded
How do jigs help speed up production and increase accuracy?