## Slide 1
AQA
    A Level
      Product Design 7552
Forming polymers
Unit 7 Processing and working with polymers
2

## Slide 2
Understand how 3D polymer products are formed
Understand and be able to explain the suitability of a range of different forming methods for a range of specific products
Objectives

## Slide 3
Processing polymers
Polymers in powder or granule form are processed to produce usable stock forms for manufacture
  What manufacturing method is used to produce polymer stock forms such as tube, cable and profiles?
  What method is used to produce thin sheet and film?

## Slide 4
Forming polymers
Polymers can be formed in a variety of different ways depending on several different factors
  Whether the product is being manufactured in the school workshop or in an industrial facility
  What product or part is being formed or moulded
  What scale of production is applicable
  What polymer material is being used
  Which methods of forming are commonly used in the school workshop?

## Slide 5
Vacuum forming is used both in the school workshop and in industry, vacuum-formed products include items such as plastic yoghurt pots and bath tubs
  HIPS (high impact polystyrene) is the most commonly used plastic to vacuum form within schools
  In industry, polyester, ABS and acrylic are also used
  Why is this process suited to use in the school workshop?
Vacuum forming

## Slide 6
Vacuum forming process
Once the mould has been produced, there are three main stages to the vacuum forming process
  A sheet of thermoplastic is heated and pressed onto the former (mould) by atmospheric pressure as a vacuum reduces the pressure below the softened thermoplastic
  The plastic takes on the shape of the mould, then cools and sets in position before the mould is removed

## Slide 7
Mould making
To ensure a good product is formed, the mould must have the following features – Justify each one
A mould must :
  have corners and edges rounded with a small radius
  have a positive draft angle > 3° to ensure easy removal
  have vent holes drilled where there are dips in the profile
  not have too deep a profile
  have a smooth finish
  avoid undercuts

## Slide 8
Line bending
Strip heaters are used for line-bending which is a means of creating a permanent fold in a piece of thermoplastic such as acrylic
  It is often used to create small products in the school workshop
  It is ideal for creating display stands, menu holders and photo frames
  What scales of production does the line bending process lend itself too?

## Slide 9
Line bending process
Marking out should be done carefully and accurately before the sheet is placed on the strip heater
  A line is marked on the polymer sheet often using a chinagraph pencil or non-permanent marker
  The strip heater is heated to temperature
  The marked line on the workpiece is placed across the heating strip
    What are the health and safety considerations when using a strip heater in the workshop?

## Slide 10
Line bending process
The time a line needs to be heated will depend on the type and thickness of the polymer sheet
  The polymer sheet is allowed to heat through
  The line is tested for flexibility and when ready, bent to the required angle
  Once the workpiece has set it can be cooled in a water tray
    What can be made to help ensure the polymer sheet is bent accurately?

## Slide 11
Laminating or layup
Thermosetting polymer resins can be combined with fibres to produce a variety of products
  This process is used to create rigid three-dimensional products like speed boats, rowing boats, canoes, caravan panels and even bumper cars
  What is the advantage of a fibre-based composite over a moulded thermoplastic?
https://www.youtube.com/watch?v=wYb_UjgJ5E0

## Slide 12
Layup process
Fibre strands or matting, like glass fibre, carbon fibre or Kevlar are used to create composites
  The mould may be made from timber, board or metal
  A release agent is applied to the mould
  Polyester resin gel coat is applied and cured
  Matting is laid into the mould and the resin is mixed with catalyst and brushed onto the matting
  In industry, chopped strands mixed with resin may be sprayed onto the mould
  It is then rolled to remove air bubbles and once even, allowed to set

## Slide 13
Worksheet 2
Complete Task 1 of your Worksheet

## Slide 14
Thermoforming
Like vacuum forming, thermoforming is the process of forming a heated, softened polymer sheet
  The difference from vacuum forming is that thermoforming uses both male and female moulds
  The male mould is lowered into the heated sheet, pressing it into the female mould
  A vacuum assists in pulling the polymer into the mould
  What packaging products could be manufactured using thermoforming?
https://www.youtube.com/watch?v=p5M0Yl2BUjE

## Slide 15
Injection moulding
Injection moulding is commonly used in industrial production to produce complex shapes
  Moulds are generally constructed from steel and are in two parts
  A number of different polymers are suitable for injection moulding and include ABS, acrylic and PVC
  Why is it important that moulds are very accurate and any blemishes are removed?

## Slide 16
Injection moulding process
The injection moulding process starts with the thermoplastic granules being fed into a hopper
  The hopper feeds an Archimedes screw that drags the granules past a heater where they are plasticised
  When the soft, pliable plastic reaches the end of the screw, a hydraulic piston forces it into the mould
  What are the benefits of using an Archimedes screw?

## Slide 17
Ejection and finishing
Water is used to cool and set the plastic quickly
  The mould is separated and ejector pins release the moulding; the process is then repeated
  Any excess polymer flashing is trimmed and usually recycled
  How does injection moulding lend itself to mass production?
  What are the tell-tale signs that a product has been injection moulded?

## Slide 18
Blow moulding
Blow moulding uses a two-part mould and compressed air to make hollow shapes
  Polymers like HDPE, PET, PP and LDPE are used to produce many hollow plastic products including garden water butts, bins and some hollow plastic toys
  It is also used to create packaging such as bottles and containers
  Why is a two-part mould used?
https://www.youtube.com/watch?v=8W6P5KU5ONQ

## Slide 19
Blow moulding process
Polymer granules are heated and extruded to create a plastic tube known as a parison
  The parison is fed into the mould and is pinched at the bottom as the mould closes tightly. It is filled with heated compressed air until the parison inflates to fill the mould
  The plastic cools and takes on the shape of the mould

## Slide 20
Blow moulding finishing
The cooled moulding is then released and finished
  Any excess or flashing created, where the mould has closed on the parison, is automatically trimmed
  This waste material is recycled and reused
  Products are then tested to ensure they are air and water tight and any rejects are sent for recycling
  High production moulds are often water cooled – How does this contribute to the efficiency of the process?

## Slide 21
Rotational moulding
Like blow moulding, rotational moulding is used to create hollow plastic forms
  Polymers like HDPE and PP are commonly used
  The process produces a seamless product
  It is used for heavy duty items like water tanks, communal recycling bins, kayaks and plastic slides
  Why isn’t blow moulding used to create these products?
https://www.youtube.com/watch?v=xc9pKiV5wag

## Slide 22
Rotational moulding process
Polymer granules or powder is weighed, depending on the desired wall thickness and put into the mould
  The mould is then placed on a rig in a huge oven and heated
  As it is heated it is rotated slowly in two axes allowing the polymer to coat the inside of the mould evenly
  Once the desired thickness is reached the mould is cooled
  There is slight shrinkage as the polymer cools – What is the advantage of this?

## Slide 23
Compression moulding
Compression moulding is used to form thermosetting polymers using a hydraulic press
  Polymers like urea formaldehyde and melamine formaldehyde are used to create fairly simple profiles such as electrical fittings
  It is also used to form elastomers for example rubber shoe soles and silicone cake moulds

## Slide 24
Compression process
Two separate moulds are used, a male and female, which when pressed together create a void
  The moulds are heated and a charge or preform of polymer is placed between
  Pressure is exerted on the moulds which come together, heating the charge and forcing it into the void to create the part
  It is then left to cool before the part is removed using an ejector pin
  The amount of polymer used is slightly greater than that needed to fill the void – Why is this?

## Slide 25
Worksheet Task
Complete Task 2 of Worksheet 2

## Slide 26
Plenary
How does the water cooling of the mould speed up the production process of moulding components
Which type of polymer is best suited to compression moulding?
What is the difference between vacuum forming and thermoforming mouldings
Why are ejector pins used in some two-part moulds?