## Slide 1
AQA
    A Level
      Product Design 7552
Finishing polymers
Unit 7 Processing and working with polymers
3

## Slide 2
Be aware of the ways that polymers can be finished to enhance their aesthetics or improve their function
Understand the use of solvent cements for bonding polymers with chemical welds
Understand how pigments and elastomers can be added or bonded to polymers in the moulding process
Objectives

## Slide 3
The finished product
What finishes, if any, may have been used on this corded hair dryer?

## Slide 4
Polymer finish
Most plastics are self-finishing which means they do not require any further finishing
  This means the material is ready to go straight from production
  Any texture comes from the surface finish of the moulds used to form them or the die profiles used when extruding
  Why are polymers often considered to be self-colouring?

## Slide 5
Adding pigment
Adding colour is often done for aesthetic appeal but can also contribute to the ergonomics and function of a product
  Pigments are usually fine powders which are added in production creating pigmented granules, sheet, film and other stock forms
  Sometime a manufacturer will use clear granules, creating their own mix of pigments
  How and where might pigments be added in a manufacturing process?

## Slide 6
Aesthetics
Whilst polymers can be polished, brushed and textured, aesthetic appeal may be added in a variety of ways
  Plastics can be coloured using pigments, paints and pigmented gel coats
  Plastic products can be enhanced using the technique of over moulding, by adding elastomers

## Slide 7
Thermochromic pigments
Thermochromic pigments can be added to polymers to create a colourful reaction to thermal changes
  Temperature sensitive thermochromic pigments can change from one colour to another or from colour to clear as temperature rises and falls
  Applications include plastic cutlery, bowls and cups for babies and young children and plastic films used in thermometers
  Where might non-reversible thermochromic pigments be used?
https://www.youtube.com/watch?v=SZ78qNpq3mA

## Slide 8
Phosphorescent pigments
Phosphorescent pigments are charged by exposure to natural light
  The phosphors in the pigment then release the energy they have stored whilst exposed, which produces a visible glow in the dark
  Applications include watches, toys and recreational items like frisbees, balls, wall decals and ceiling stars
  Suggest products where phosphorescent pigments are used to improve the function or even increase the safety of the product
https://www.youtube.com/watch?v=PkO9xFd_BqM

## Slide 9
Hydrographic printing
Colour images are printed onto water soluble film which floats in a tank
  The product is submerged and the image wraps around it giving a colourful and potentially dramatic finish

## Slide 10
Electroplating
Plastics are covered in a conductive layer or etched before plating with a metal
  Used predominantly in the automotive industry for car trims but also in electronics, bathroom fixtures and various household goods
  What benefits does electroplating have?

## Slide 11
Rubberising spray
A slightly textured coating with a matt finish can be sprayed onto various materials to provide grip
  Where might rubberising sprays be used?

## Slide 12
Polishing
Plastic can become rough or scratched when processed and can become weathered or faded if left outside
Polishing techniques are used to restore a high quality finish
  Brasso® is often used to give a lustrous shine to plastics and is commonly used in a school workshop

## Slide 13
Worksheet Task
Complete Task 1 of Worksheet 3

## Slide 14
Joining polymers
Whilst polymers can be heat welded, solvent cements are more commonly used to form a chemical weld
  Solvent cements are used in the plumbing industry to join PVC and ABS pipe,
  Once brushed on, the surfaces soften and permanently fuse together

## Slide 15
Chemical welds
Solvent cements come in two different forms
  Liquid solvent cement has a water like consistency and uses capillary action to travel along a joint and cannot fill gaps
  Tensol 12 is a thicker variety (acrylic cement) and can fill small gaps
  Both are methane-based and contain VOCs which are given off as they evaporate
  What are the advantages of using a thicker cement?
  Why should parts be clamped as the solvent evaporates and the bonds harden?

## Slide 16
UV hardening adhesive
UV hardening resins have been used in dentistry for many years but have also been developed for use in 3D printers and as a separate adhesive
  The liquid adhesive is applied to the surfaces that require bonding and UV light is shone on it which cures it
  The resulting bond can be very strong and is permanent
https://www.youtube.com/watch?v=NV6xHe060WE

## Slide 17
Finishing
The two main categories for applying finishes are protection and aesthetics, however some offer both
  Polymer finishes may be brushed on, sprayed on or applied
  Some spray-on products are solvent based and are not very environmentally friendly as they contain high levels of volatile organic compounds (VOCs)
  What precautions should be taken when using any solvent based products?

## Slide 18
Gel coating
As part of the layup process used to create a rigid GRP shell, a gel coat creates a coloured finish
  Pigment is added to the polyester resin
  This is applied to the inside of the mould and allowed to cure hard before layup continues
  The result is a pre-coloured high shine surface finish
  Is any additional finish then required?

## Slide 19
Painting
Acrylic spray paints are sometimes used to protect and colour moulded plastic parts and products
  Used on body coloured bumpers where ABS parts are mass produced and sprayed after production to match the vehicle
  Acrylic spay paint is water based and fast drying
  It adds additional UV protection and improved weather resistance
  When does acrylic spray painting make better financial sense than adding pigments?

## Slide 20
Preparation
To achieve a good painted finish, preparation is required as most polymers are self finishing, smooth and therefore not an ideal substrate for paint
  To prepare an ABS moulding for painting, the surface first needs to be thoroughly washed and dried
  It should then be abraded to provide a key
  It must then be cleaned again and any residual dust removed
  A primer is the applied and allowed to dry before applying several even coats of acrylic paint

## Slide 21
Overmouldings
As a finish, overmoulding can enhance both the look and feel of a polymer based product
  Thermoplastic elastomers or TPEs are often used to create an additional grip or texture
  Overmouldings can also work ergonomically, indicating where to grasp a product
  Overmoulding is commonly used in tool handles, sports equipment, toothbrushes, torches, sports bottles and power cables
  Why use TPEs rather than other thermoplastics?

## Slide 22
Creating overmouldings
Overmoulded products are usually injection moulded but this can be in different ways
  Two separate moulds can be used, one for the substrate and a second with a cavity for the overmoulding
  A single, duel cavity mould with two separate injection heads can be used in a continuous production line, this is called twin shot injection moulding
https://www.youtube.com/watch?v=jq4xt9tE5R0
https://www.youtube.com/watch?v=NoV0RbXnCbI

## Slide 23
Worksheet
Complete Task 2 of Worksheet 3

## Slide 24
Plenary
Name and describe the different adhesives available for bonding polymers
Explain the process of overmoulding
What is meant by the term self-finishing?
Describe the different types of pigments that can be added to polymers and discuss which applications they might be used for