## Slide 1
AQA
    A Level
      Product Design 7552
Performance characteristics
Unit 3 Performance characteristics of woods
2

## Slide 2
Describe the different performance characteristics of woods
Link material characteristics to their different uses
Objectives

## Slide 3
Starter
What is meant by the performance characteristics of wood and how might the timber frame pictured need to perform to be fit for purpose?

## Slide 4
Performance characteristics
Performance characteristics describe how a material behaves in different contexts and what it looks like
Performance characteristics of wood include:
  Grain pattern or direction
  Warpage, shrinkage and splitting
  Machining qualities
  Resistance to decay and moisture
  Toxicity
  Consider the terms above and complete Task 1 of Worksheet 2

## Slide 5
Wood grain
The structure of wood grain can affect workability and cost
  Many hardwoods, such as mahogany, oak and olive wood, are prized for their decorative grain pattern
  Beech has tight and fine grain which makes it easy to turn
  The end grain is the pattern which can be seen at the end of a piece of wood
  How is the pattern in the grain created?
  How do knots affect performance?

## Slide 6
Wood structure
The structure of wood can be explained by considering the biology of a tree
  Wood fibres are made from hollow straw-like cells (tracheid) which are held in a lignin
  Tracheid carry water and nutrients to and from the roots and leaves
  These straw-like cells make wood strong along its length
  How does the direction of the grain affect aesthetics, strength and workability?

## Slide 7
Reading the grain of wood can be tricky
  Identify the direction of the grain by looking for the rays rising to the surface of the wood
  Wood will always split in the direction of the rays
  Planing with the grain will avoid tearing the wood
    Why is cutting across the grain easier than cutting along it?
Going against the grain

## Slide 8
Anisotropic
The grain gives natural wood different physical properties in different directions – it is an anisotropic material
  Natural wood is stronger along the grain than across it
  Manufactured boards like MDF and plywood are not anisotropic
    How would anisotropic materials affect the design and manufacture of a product?

## Slide 9
Surface defects
Manufactured boards are uniform in their surface finish but natural woods are much less predictable
  Knots are tricky to work with and may fall out as wood shrinks
  Machining can create marks on the timber from the saw mill
  Woods can be damaged by insect attack, disease and rot
  Defects like this can affect the overall stability of the wood

## Slide 10
Worksheet 2
Complete Worksheet Task 2

## Slide 11
Distortions
Once timber is felled and sawn it must be seasoned to prevent it from distorting
  Wood is hygroscopic which means it behaves like a sponge – it absorbs moisture and swells up in damp conditions
  As water evaporates from freshly felled timber, it shrinks
  If moisture evaporates too quickly, or in an uneven fashion, the wood can distort – it may twist, warp, bow, cup or split

## Slide 12
Seasoning
Wood is seasoned before it’s sold to prevent warpage, shrinking and splitting
  Wood can be air-dried (AD) or kiln-dried (KD)
  Air-dried timber planks are stored under cover and left to dry naturally
  Kiln-drying uses steam to artificially dry the timber and speed up the drying process
  AD timber is best suited for external projects – Why?

## Slide 13
Warp, shrink and split
Seasoning increases stability, strength and resistance to decay but timber can still distort
  Distortions increase depending on the moisture content in the air and the different sections of the trunk
  A – Square sections can shrink to a diamond shape
  B - Boards tend to ‘cup’
  C – Uniform shrinkage
A
B
C

## Slide 14
Shrinkage
Wood swells and shrinks with the seasons or with the level of moisture in any given environment
  For example, when laying a wooden floor, wood will be left in the room where it is to be laid to acclimatise for a few days
  Wood that doesn’t warp, shrink or split very easily is called a stable timber
Most shrinkage occurs around the year rings
Radial shrinkage between 2-8%
Least shrinkage along the length

## Slide 15
Seasoning gives stability
Seasoning makes wood more stable, making it less likely to change shape or size during/after manufacture
The working properties of seasoned timber include:
    It is stronger and more stable
    It is less likely to decay or rot
    It is less likely to corrode metals
    It absorbs preservatives more readily
  Discuss why the seasoning process improves each of the working properties listed above
https://www.youtube.com/watch?v=VF6CNWCf2NY

## Slide 16
Worksheet Task
Complete Task 3 of your Worksheet

## Slide 17
Joining wood
There are many methods for joining wood both permanently and temporarily
  Suggest some methods for joining wood
  The high oil content in woods such as teak can make them difficult to glue
  The acid content in woods such as oak can corrode ferrous metal fixings
  Woods such as ash, beech and birch glue well

## Slide 18
Forming
Forming consists of both additive manufacturing and wasting processes as well as manipulation
  Wasting processes like carving, turning, milling and routing are used to form woods
  Steam bending changes the shape of wood without wasting or adding
  Laminating can be used to create curved structures

## Slide 19
Steam bending
Steam bending uses heat and moisture to make wood pliable
  Once heated in steam, some woods can be bent without breaking and held shape in a former until it is cool and dry
  Woods with an open pore structure, such as ash and beech, steam bend well
  Steam bending maintains the longitudinal strength of the wood to create durable frameworks

## Slide 20
Machining qualities
Manufactured boards offer a uniform quality and density which makes them predictable to work with
  Natural timbers can be difficult to machine as some are very hard and tough
  The density of natural wood is less predictable and natural oils in the wood can clog up cutting tools

## Slide 21
Laminating
Laminating combines wood and adhesives for different purposes
  Laminating can be used to create curves using aeroply and flexiply
  Natural wood boards are often joined using lamination to create larger, wider sections e.g. electric guitar bodies and structural beams in architecture
  Melamine formaldehyde or wood veneers can also be laminated to a material to enhance the surface properties
https://www.youtube.com/watch?v=jYp7QUOx4eY

## Slide 22
Worksheet task
Watch the link video and complete Task 4

## Slide 23
Resistance to decay
Wood can be treated to increase its resistance to decay through fungal and insect attack as well as rot
  In a dry and stable environment, free from insects and vermin, wood is extremely durable
  Many woods have a high oil content and so are less prone to decay and can be used outdoors without a preservative finish
    Which treatments could limit the process of decay in timbers?

## Slide 24
Insect attack
Beetles and other insects, such as termites, are attracted to the starches and sugars in woods
  Insects lay larvae in tiny crevices in the wood – once hatched, the larvae will bore through the wood from the inside out
  Tiny but mighty, insects can ruin the structural integrity of a building
  Dry, varnished or painted wood or wood with a high oil content is at low risk of insect attack

## Slide 25
Fungal attack
Damp or poorly ventilated conditions make an ideal environment for fungal attack
  Fungal spores attach to the wood and feed off the nutrients stored in the cells of the wood which causes rot
  Dry rot makes timber weak, dry and brittle but fungi is clearly visible when wood has wet rot
  Dry wood has a low risk of fungal attack
    Why does moisture increase the chances of fungal attack?

## Slide 26
Moisture resistance
Many woods are resistant to moisture and suitable for outdoor use without treatment
  Oily woods like teak and redwood will endure in wet conditions
  Marine ply is made from water-resistant hardwood veneers and waterproof adhesive so it can withstand wet conditions
  Paint, varnish or oil can be applied or wood can be pressure treated with preservatives to add moisture resistance

## Slide 27
Toxic trees
Tree sap and saw dust can pose health risks
  Wood dust and sap can irritate the skin, cause respiratory problems, nausea and affect vision
  Certain species of cedar can cause migraines, stomach problems and can affect the nervous system
    What precautions should be taken to make a safe environment when working with woods?

## Slide 28
Regulations
Control of Substances Hazardous to Health (COSHH) regulations state that wood dust must be limited to 5mg per cubic metre
  Extraction and ventilation systems and suitable personal protective equipment (PPE) must be provided in workplaces
  Very few woods are toxic in their natural state but certain timbers, such as beech and bamboo are considered food-safe and are ideal for kitchen utensils and toys

## Slide 29
Plenary
How might the grain of a wood affect a design?
How does the structure of wood affect its properties?
What are the advantages of a natural timber with high oil content?
Why does wood distort?
How might moisture affect wood?
In what ways might timber decay?
How can wood be bad for your health?