## Slide 1
AQA
    A Level
      Product Design 7552
Testing and finishing of woods
Unit 3 Performance characteristics of woods
3

## Slide 2
Identify different workshop and industrial tests that are carried out on woods
Describe how tests are set up and what is tested, measured and compared
Describe how material properties can be enhanced
Objectives

## Slide 3
Starter
What properties can be tested for in woods?
Why do we carry out tests on materials and products?

## Slide 4
Testing wood
Woods can be tested for:
  tensile strength
  toughness
  hardness
  corrosion
  malleability
Complete Task 1 of Worksheet 3 to help define these terms

## Slide 5
Testing methods
You will need to know the different methods of testing woods, both in a workshop and in industry
  How would you expect the results of workshop tests and industry tests to differ?
  How can you conduct a fair test?

## Slide 6
Tensile strength
Workshop tests are limited to the tools and equipment available
  Tensile strength can be tested by applying weight to a test piece and monitoring how much the material bends or deflects
  A rule or Vernier callipers can be used to measure the deflection
    Which factors must remain constant in this sort of test?
https://www.youtube.com/watch?v=DGj5T8Ack4o

## Slide 7
Hardness tests
Hardness measures how easily materials resist abrasion and indentation
  You could hit a centre punch into a material and measure the size of the dent created
  Abrasive wear can be tested by running a file or some glass paper over the surface of materials and compare the number and depth of any scratches
  How could you ensure consistency in these tests?

## Slide 8
Toughness
Tough timber can absorb impact
  Tough woods like birch and beech are used in tools and tool handles as they can absorb impact without breaking
  To compare the toughness of different materials, hold each test piece in a vice and hit each one in turn with the same force
  The most brittle materials will snap and the toughest materials will absorb the impact
  How could you ensure the same force is used for each test piece?

## Slide 9
Corrosion
Wood will not corrode like metals but will rot and is prone to insect and fungal attack
  Test pieces of the same size and shape can be left outside for a period of time and then inspected for damage
  Test pieces that have been exposed to the elements can then be tested for hardness to establish how the properties are affected by outdoor use
  The same test could reveal how woods and finishes weather and respond to UV light over time

## Slide 10
Malleability
Malleability is the ability of a material to be moulded without breaking
  This characteristic is not necessarily linked to wood as it will spring back into shape
  However, woods can be moulded using steam bending and laminating - some woods form more easily than others
  Flexible plywood is designed to be moulded
  Flexibility can be tested by measuring how far a thin test piece will bend before it snaps

## Slide 11
Worksheet activity
Compare the properties of a range of woods for yourself using these workshop tests
  Use Task 2 to record your findings

## Slide 12
Industrial testing
Industrial tests require specialist equipment which enables highly accurate tests
  A tensile testing machine clamps a test piece at each end and pulls the material apart until it breaks
  A worm drive pulls the clamps apart at a constant rate and the load and distance travelled is plotted

## Slide 13
Tensile testing
Results from a tensile testing machine will show the following:
  Stretching force applied
  Distance travelled
  Point A marks the ultimate elastic limit – the most the material will stretch
  B marks the yield point when the elastic deformation becomes irregular
  The breaking point at C shows the point at which the material snaps

## Slide 14
Janka hardness test
The Janka test measures the ability of wood to resist scratches or dents
  The test measures the average force needed to plunge a 0.44” or 11.28mm steel ball halfway into a piece of wood
  Other tests include the Vickers, Brinell and Rockwell hardness tests which use indenters of different shapes and materials
    Why would this be useful when selecting materials for flooring?

## Slide 15
Charpy and Izod tests
Two standard industry toughness tests are the Charpy and Izod test
  Test pieces are prepared to a set size with a 2mm deep notch in the centre
  The test piece is positioned carefully before a pendulum is dropped to strike the test piece
  The distance the pendulum travels after breaking the test piece is a measure of the toughness of the material

## Slide 16
Toughness testing machine
Impact or toughness testing machines consist of a stand and a pendulum
  The scale on the top if the stand measures the pendulum swing
  The test piece or specimen is positioned or clamped
  The starting point for the pendulum in the Izod test is lower than the starting position for the Charpy test

## Slide 17
Comparing Izod and Charpy
Test specimens are positioned differently in each test
  In the Charpy method, the test material is placed horizontally with the notch facing away from the hammer
  In the Izod method (pictured), the test piece is clamped vertically with the notch facing the hammer

## Slide 18
Non-destructive tests
Tests for tensile strength, toughness and hardness, damage or break the material being tested
  Non-destructive testing can detect faults in a material or product without causing any physical damage
  These tests help identify imperfections below the surface of a material invisible to the naked eye
  Where might non-destructive tests be used?

## Slide 19
Ultrasonic testing
Ultrasonic testing detects internal defects using sound waves
  Sound waves are pulsed into the material and the intensity of the reflected sound waves is recorded
  Ultrasonic testing is suitable for any material, is highly accurate, quick and portable

## Slide 20
X-ray testing
X-ray beams are passed through a material and project an image on to a film or screen
  X-ray testing can measure the density and width of individual tree rings - dense material is opaque white, whereas less dense material is feint
  X-rays can detect damage and splits inside the wood and provide information about the properties of a timber and how a tree has been affected by its surroundings

## Slide 21
Thermal conductivity
Wood is an excellent natural thermal insulator due to the air pockets in its cell structure
  The Guarded Hotplate method is used to test the thermal conductivity of wood

## Slide 22
The Guarded Hotplate method
This test sandwiches a material test piece between two temperature controlled plates
  One plate is kept hot and the other is kept cold – the test measures the time taken for the test material to reach a constant temperature
  This is one of the oldest and most trusted methods but the test is time consuming, only suitable for solid materials and it cannot perform tests in extreme temperatures

## Slide 23
Electrical conductivity
Timber is an electrical insulator and is not routinely tested for electrical conductivity
  However, water does conduct electricity
  As a hygroscopic material, wood absorbs moisture from its surroundings and will conduct electricity if the water content and electrical charge is high enough
  What safety risks could this pose?

## Slide 24
Why bother?
How might the results from a destructive materials test affect design decisions?
What’s the point in using a non-destructive test to assess a structure that’s already in use?

## Slide 25
Wood enhancement
The working properties and aesthetics of woods can be enhanced in several ways
  Combining wood with resins to create composite materials
  Adding a preservative, finish or coating to timber to increase resistance to decay
  Adding a laminate to improve the properties of the surface
  Which wood composites and finishes have you used before?

## Slide 26
Preservatives
Preservatives can guard against insect and fungal attack, moisture, fire damage and rot as well as enhance aesthetics
  Pigments are added to give different colour options and improve aesthetics – this can make cheap materials look more expensive
  Preservatives are often applied with a rag or brush but pressure treatment of wood requires professional equipment

## Slide 27
How preservatives work
Different products use different methods to improve moisture resistance and impede insect/fungal attack
  Preservatives often contain copper which has anti-microbial properties – this reduces the chance of fungal attack
  Paints and varnishes, such as acrylic and epoxy, create a protective coating to seal wood but can be prone to UV damage
  New methods use bio-polymers or natural acid compounds to impregnate wood cells which guards against decay

## Slide 28
Worksheet task
Complete Task 3 on the Worksheet

## Slide 29
Wood composites
Combining resins with natural wood to create new materials has many advantages
  Engineered floor boards are made with a plywood or MDF base combined with a hardwood or polymer laminate
  This creates a strong and stable product with a wipe-clean, hard and durable surface
  Many engineered boards are formed to ‘click’ together for quick and easy installation
  What are the environmental benefits of using composite laminate flooring?

## Slide 30
Glulam
Glulam combines natural wood planks with glues to create large laminated curved beams for structural and architectural use
  Glulam structures offer a more sustainable alternative to steel or concrete structures with a softer aesthetic
  Finger joints are used to connect small planks into longer lengths before multiple pieces are glued and clamped together
  The joints are staggered to avoid weakness

## Slide 31
Case study: Glulam bridges
Bridges in the Netherlands use glulam to create curved structures
  Read the case study to find out more

## Slide 32
Plenary
In pairs, complete Task 4 or your Worksheet and share your responses with the rest of the class