## Slide 1
AQA
    A Level
      Product Design 7552
Working with woods
Unit 8 Processing and working with woods
1

## Slide 2
Describe the different joining techniques for timber
Explain the suitability of different joining methods for a range of products
Recognise how well different joining methods are suited to different scales of production
Objectives

## Slide 3
Starter
Name some different methods for joining woods
What factors might you consider when choosing a joining method?
  Suggest three reasons why we might need to join woods

## Slide 4
Timber processes
Fabrication processes are grouped into categories
  Addition refers to joining methods
  Forming and wasting processes modify the shape by bending or wearing away material

## Slide 5
Worksheet task
Complete Task 1 to consider the different types of wood joints

## Slide 6
The right joint for the job
Different joints are used for different applications
  A box or carcass may use different joints to some framework – some joints are suitable for both
  The angle and strength required of the joint may affect the joint choice
  The time and skill required to make a joint and the number of times a joint has to be repeated must be considered
    How would the scale of production affect the joints used?

## Slide 7
Traditional methods
There are six traditional joining methods you need to know
  Comb joint
  Dovetail joint
  Housing joint
  Half-lap joint
  Dowel joint
  Mortise and tenon

## Slide 8
Comb joint
Comb joints are used to form boxes and carcasses – they are also known as finger joints
  This simple and effective joint is made from interlocking fingers which fit tightly together and are reinforced by glue
  Accurate work can result in a very strong, aesthetically pleasing joint
  Best created using a router jig on natural or manufactured timbers or using a laser cutter on some materials
    What makes a comb joint stronger than a butt joint?

## Slide 9
Dovetail joint
Prized for their strength and aesthetics, dovetail joints are ideal for cabinets and drawer construction
  Dovetail joints demonstrate a high level of skill but can be cut fairly easily with a router and jig
  Like the comb joint, their strength relies on interlocking fingers and accurate marking and cutting
  The dovetail shapes means that these joints have superior directional strength
  Why are these excellent joints for creating drawers?

## Slide 10
Housing joint
A housing joint is commonly used for shelves and dividers
  A channel is cut through one piece of timber which houses a second perpendicular piece
  It is fairly strong, when supported with glue but can be used without glue to create sliding parts
  Easy to make – only one piece of timber needs to be machined
  How could housing joints be affected by shrinkage?

## Slide 11
Half-lap joint
A versatile joining method that is easy to construct
  Made by two overlapping materials glued together
  Used in picture frames, doors and cabinet making
  Quick and easy to make but not particularly strong
  The shoulder helps resist diagonal distortion
    Which components could be added to reinforce a half-lap joint?
Shoulder
Cheek

## Slide 12
Dowel joint
Dowel joints are a quick, simple and effective method to join a variety of materials
  Used in both frame and carcass construction, flat-pack furniture and to reinforce edge to edge joints
  Holes are machined easily with a drill and jigs can be used to speed up the process further
  Suitable for use in natural timbers and manufactured boards
  Cost effective alternative to mortise and tenon joints

## Slide 13
Mortise and tenon
Working with woods
Unit 8 Processing and working with woods
A heavy duty joint used in load bearing timber frameworks
  With high shear strength, it’s used in traditional building construction and frames for tables and chairs
  The tenon may be glued or pinned in place. Alternatively, wedges can be used to secure it, adding an aesthetic feature
  This joint has been developed to be made easily using CNC machines and is often used in flat-pack furniture
  How could you machine these shapes?
Tenon
Mortise

## Slide 14
Worksheet task
Complete Task 2 of Worksheet 1

## Slide 15
Joint aesthetics
Many joints are prized for their aesthetics
  Dovetail and comb joints create repeated patterns along the joint
  Woods with contrasting colours can be used to accentuate a joint
  Joints can be used to highlight a design feature
  Well-made traditional joints demonstrate great skill
    What are the disadvantages of traditional joining methods?
https://youtu.be/CSpUDEmoiLw

## Slide 16
Joining with components
Joining with bought-in components requires less time and skill – a wide range fittings are available
You will need to know about:
  Wood screws
  Nuts and bolts
  Coach bolts
  Knock down (KD) fittings

## Slide 17
Woods screws
Screws are available in different lengths and widths, with a variety of head shapes and finishes
  Most screws are made from mild steel and are then plated in brass, zinc, chrome or another non-corrosive metal
  Screw heads are often countersunk so the screw hole can be filled or plugged, others have a domed head which can make a feature of the joint
  Screws are quick to install and can join dissimilar materials

## Slide 18
Heads and threads
The most common type of screw is the Pozi-drive
  Philips and slot head screws also are commonly available
  It’s essential to choose a driver bit of the correct size and shape to avoid damaging the screw, driver bit or workpiece
  Self-tapping screws don’t always need a pre-drilled pilot hole and twin drive threads drive into timber in half the time
    How could you damage the wood when using a screw?

## Slide 19
Clearance and pilot holes
Pre-drilled clearance and pilot holes reduce the risk of wood splitting when a screw is inserted
  Pilot holes allow the core of the screw to pass into the material while the thread bites into the sides
  Clearance holes allow components to drop in and out without friction
  Clearance holes are required when using nuts and bolts
Pilot hole
Clearance hole

## Slide 20
Nuts and bolts
These can be used a temporary or permanent fixing
  Bolts have a variety of different head shapes, including countersunk, and can be used to join dissimilar materials
  Nuts and bolts can be used with washers to create moving or folding parts e.g. a deck chair
  Nuts and bolts are used in construction and the manufacture of large furniture frameworks such as beds and chairs

## Slide 21
Coach bolts
Coach bolts are used to build wooden structures such as summer houses, benches and sheds
  Identified by a square section just under the head of the bolt
  Materials must be prepared with a pre-drilled hole and the fixing is tightened with a spanner or socket set
  The square section embeds into the wood and prevents the bolt from spinning during assembly
  Once installed, it’s impossible to remove from the head
  Why might this be a useful feature?

## Slide 22
Speeding up manufacture
Using screws, nuts and bolts and coach bolts requires minimal time and skill
  Pilot and clearance holes can be cut with simple tools for one-offs and production can be scaled up using CNC
  Screws are a quick and easy way of reinforcing butt joints and joining hardware such as hinges and closures
  These components make strong, reliable joints and can be used as decorative features too

## Slide 23
Knock down fittings
Knock down (KD) fittings offer strong but collapsible joints ideal for flat-pack furniture and fitted kitchens
  KD fittings are designed to work with both manufactured and natural timbers and can join dissimilar materials
  Once a product’s parts have been machined, KD fittings are easy to install with simple tools
  Glue-free dowel joints are used to help locate parts and add stability
  How does KD furniture benefit both the consumer and manufacturer?

## Slide 24
Types of KD fittings
KD fittings can be used to join boards edge to edge and build carcasses and frameworks for furniture
Examples include
  Barrel nut and bolt
  Cam fittings
  Modesty blocks

## Slide 25
Modesty blocks
These pre-formed blocks are hidden inside the product once installed
  One of the first modern fittings widely adopted in fitted kitchens and office furniture
  Used for carcass construction, to support edge to edge joints and in modular furniture
  Easy to use but not very strong and the block affects the aesthetics and shape inside the product
  Available in a range of colours and materials

## Slide 26
Cam fittings
Cam fittings require highly accurate pre-drilled holes to function properly
  Jigs or CNC can be used to prepare parts for assembly but once cut, joints can be assembled easily with a screwdriver
  Cam fittings are commonly used in flat-pack furniture made from laminated manufactured board e.g. storage units
  Where does a cam fitting get its name?
https://www.youtube.com/watch?v=qHCmPAKe7Qo

## Slide 27
Barrel nut and bolt
Also known as cross dowels, these are used to assemble furniture with large frameworks such as beds, chairs and tables
  Jigs can be used to ensure accurate positioning of the holes and the joint is easily tightened with an Allen key
  The bolt tightens in a barrel nut which is installed at 90° to the bolt shaft
  These fittings have excellent sheer strength and clamping force ideal for large, load-bearing furniture
  Why is the hole for the bolt drilled longer than necessary?
Cross sectional view

## Slide 28
Making the cut
Product parts must be machined accurately for flat-pack components to function properly
  Handheld jigs can be used for small scale manufacture
  CNC manufacturing ensures accuracy for high-volume production
  Accuracy during manufacture makes component installation and product assembly easy for the customer
https://www.youtube.com/watch?v=SYf1yGOjOvU&t=138s

## Slide 29
Why use KD fittings?
Discuss the advantages of joining furniture with knock down fittings
  How does flat-pack furniture streamline transport?
  How can joints using KD fittings reduce costs?
  How do KD fittings affect end-of-life disposal?
  How might KD fittings facilitate moving house?
  Which scales of production would knock down furniture be best suited to?
  What are the restrictions of using knock down fittings?

## Slide 30
Worksheet Task
Complete Task 3 of your Worksheet

## Slide 31
The restrictions of tradition
Making quality wooden products by hand takes time and skill
  Before the Industrial Revolution, a product’s value was measured by the time it took to create
  The rise of mechanisation and demand for low-cost furniture led to a shift in style
  A cleaner aesthetic was better suited to mass-production
    What scale of production would this chair be best suited to?

## Slide 32
Mass produced furniture
The Swedish firm, IKEA (est. 1940s) make mass-produced, affordable furniture
  IKEA use highly automated production methods and knock down fittings to replace traditional joining methods
  Knock down fittings allow furniture to be flat-packed and easily assembled by the user
  New joining techniques are being developed all the time
https://www.youtube.com/watch?v=TOq3Bgln_K0&t=93s

## Slide 33
Plenary
Consider the working properties and characteristics of the different joining methods
  What properties would you look for in a joining method for each of these scales of production?
One-off
Batch
Mass production