## Slide 1
AQA
    A Level
      Product Design 7552
Forming woods
Unit 8 Processing and working with woods
2

## Slide 2
Recognise the different ways woods can be formed into 3D products
Develop a deeper understanding of a range of forming processes
Justify and explain the suitability of different processes for a range of different applications
Objectives

## Slide 3
Starter activity
What does it mean to form woods?
Why do we form woods?
Name some wood forming methods you have used

## Slide 4
Shapes and forms
Consider the shapes and forms necessary to make this harp
  Products often call for structural strength and integrity along with organic shapes and form
  Some forming techniques are used to produce decorative relief patterns
  Other methods can be used to bend timber into seemingly impossible shapes
    How could the different parts of this harp have been formed?

## Slide 5
Making waves
Lamination and steam bending are two processes used to make wavy wooden structures
  Marcel Breuer’s iconic Short Chair (1937) is crafted through a process of lamination
    How do steam bending and lamination differ?
https://www.youtube.com/watch?v=S8cQz4rSit8

## Slide 6
Laminating
Thin veneers or flexible plywood are glued together to make a permanent curved profile
  A former helps apply uniform pressure to the layers of timber while the adhesive cures

## Slide 7
Preparation is key
The design, manufacture and preparation of a mould is crucial to a successful lamination
  Moulds are often covered in wax or parcel tape to prevent the laminate sticking to the mould
  The mould must allow for the thickness of the laminate
  Even coatings of glue give uniform strength to the laminate
Wax/parcel tape
Outer veneer
Inner veneers / flexiply
Former must allow space for veneers

## Slide 8
The vacuum bag method
Lamination often calls for a two-part former but a vacuum press offers an alternative forming method
  Laminate is placed on a one-part mould and encapsulated in a heavy duty polythene bag
  A pump sucks the air from the sealed bag
  The resulting atmospheric pressure forces the laminate into position
    What are the pros and cons of using a vacuum bag?
https://www.youtube.com/watch?v=vVswXx2m3eI&t=166s

## Slide 9
Steam bending
A steam box heats and softens the wood fibres to make them pliable and easier to bend
  Woods with a straight grain and open pore structure, such as ash, oak or beech, are ideal
  Steamed wood can be bent in all directions to form complex curves and twists
  Used for small, lightweight projects as well as structural, load-bearing forms

## Slide 10
The steam box
Steam boxes take many forms but all are made up of a vented container and a steamer of some kind
  Steam must be able to circulate around the workpiece and excess water and steam must be able to escape
  Steamed wood must be moved quickly to a robust former to cool – this can be hard work!

## Slide 11
Forming steamed timber
There are myriad ways of creating a former for steam bending
  The former design depends on the shape required but also the size and thickness of the timber used
  Thicker material and more complex shapes will require more robust formers
  Thinner material formed into simple or shallow bends can be held with string or straps
https://www.youtube.com/watch?v=ZD5JWP3qDdg

## Slide 12
Worksheet task
Complete Tasks 1 and 2 of your Worksheet

## Slide 13
Hand processes
Chisels, gouges and planes have been used for centuries to manipulate wood by hand
  Nowadays, many wasting processes are carried out by machines
  What are the pros and cons of this technological development?

## Slide 14
Machine processes
Wasting processes are used to shape wood
You will need to know about:
  Turning between centres
  Turning with a chuck and a faceplate
  Milling
  Routing
    Which of these processes have you used before?

## Slide 15
Lathes hold and spin the workpiece while cutting tools are presented to waste away wood bit by bit
  Wood can be wasted, sanded and finished on the lathe
  Before installing a workpiece, a rough ‘stock’ is prepared
    How would this help you get started on the lathe?
Turning on a lathe
Mark centres at both ends
Mark circles at both ends
Plane away sharp edges

## Slide 16
Turning between centres
This technique is used to create long cylindrical forms such as spindles and chair legs
  The prepared stock is secured in a wood lathe at both ends
  Holding the workpiece at both ends gives extra stability to long, thin workpieces
  Rotation speed should be reduced to cope with larger diameter pieces and increased for narrow lengths
  How can you ensure the correct size and shape is machined?

## Slide 17
Chuck and faceplate
Turning with a chuck or faceplate holds larger work more securely
  With both of these methods the material is secured at one end only
  This gives flexibility in terms of the forms that can be created e.g. bowls, vases, domes
  The workpiece is either screwed to the faceplate or clamped in a chuck
  How would the shape of the product affect the turning method used?

## Slide 18
Chuck method
Chucks grip or secure a workpiece at the headstock
  Different chucks are used based on the form of the product
  The three jaw chuck and combination chuck are shown below
Combination chuck
Three jaw chuck

## Slide 19
The workpiece is screwed to the faceplate, then the faceplate is screwed on to the lathe
  This gives a very secure hold, especially for larger pieces
  Alternatively, the faceplate is screwed to a wooden disc which is temporarily glued to the workpiece – a paper separator allows the workpiece to be removed easily
Using a faceplate
https://www.youtube.com/watch?v=wm313cOELdc

## Slide 20
Worksheet task
Complete Task 3 of your Worksheet

## Slide 21
Routing and milling
With lathe work the workpiece spins, but with both routing and milling, the cutting tools spin
  Milling machines are substantial pieces of industrial equipment which require a large capital investment
  Handheld routers are affordable power tools more suited to on-site carpentry and DIY enthusiasts
  CNC routers and milling machines can be programmed to follow CAD designs

## Slide 22
Milling
Milling wood is usually associated with CNC manufacture
  This allows for mass production of flat pack furniture, kitchen units and fitted bedrooms with speed and consistency
  Rotating cutting tools of various shapes and sizes, usually made from tungsten carbide, are also suitable for harder materials
  Milling machines move the tool up and down the work piece laterally

## Slide 23
Advanced milling
The manufacture of 3D wooden forms was once only possible with hand carving techniques
  More advanced milling machines are fitted with a robotic arm or lathe accessory to allow infinitely complex shapes and forms to be made by machines

## Slide 24
Routing
Routers are versatile power tools which can be used with a range of accessories for enhanced machining capabilities
  Used to machine profiles and joints and cut slots and holes of various depths
  Handmade or bought-in jigs increase speed and accuracy
  CNC routers can be used to automate the routing process

## Slide 25
Holes
Handheld routers are spring loaded which allows a steady up and down movement for cutting holes
  Straight plunge bits have blades at the top and sides and are used to cut holes in the workpiece
  A simple up-down motion will make a circular hole, while running the router along a guide will create a square groove
  What joints could be machined using a straight plunge bit?

## Slide 26
Routing a profile
The profiles on mouldings such as architrave and beading are created using a router
  Router bits with sculpted blades are run along the edge of a workpiece to create a decorative or rounded edge
  A bearing called a follower wheel runs along the workpiece to ensure the bit doesn’t go too far into the material
  Using a follower wheel with a straight bit allows templates to be traced exactly

## Slide 27
Slot machines
Specialist router bits can be used to machine slots and channels
  The shape and size of the channel or slot depends on the profile of the router bit
  Bits can be passed through a workpiece from the edge or used to create slots along the edge of a workpiece
  What features, joints or product parts could be machined in this way?

## Slide 28
Routing products
Templates, made by hand or using CAD/CAM can be used to route complex shapes and cavities
  Discuss how this guitar body could have been made using different routing techniques
https://www.youtube.com/watch?v=YHP0STc3Ghg

## Slide 29
Plenary
Name the different processes that could have been used to create the chair below
  Now complete Task 4 of the Worksheet