## Slide 1
AQA
    A Level
      Product Design 7552
Finishing woods
Unit 8 Processing and working with woods
3

## Slide 2
Describe how finishing processes can be used to enhance aesthetics and/or prevent decay
Consider the suitability of specific finishes for different applications
Objectives

## Slide 3
Starter
What would the finish on a product such as this boat need to withstand?

## Slide 4
Performance and aesthetics
Finishes are applied to wood to improve aesthetics and/or performance
  A finish can change the colour, enhance the natural grain or add texture
  Treatments can protect wood by improving moisture resistance and guarding against insect and fungal attack
  Finishes can seal timber to make them easier to clean and protect against airborne pollutants
    Are finishes prone to decay?

## Slide 5
Application and preparation
Good preparation of the substrate is key
  Timber must be sanded smooth along the grain
  Rubbing down the timber with methylated spirit removes surface dust and grease – essential for good adhesion
  Finishes are applied with a brush, cloth, roller, pad or spray
  Pressure treatment finishes are applied professionally

## Slide 6
Worksheet 3
Complete Task 1 of your Worksheet

## Slide 7
User applied finishes
Finishes are either water-based or solvent-based and are usually applied by the user
  Colour wash
  Wax finishes
  Danish oil
  Teak oil
  Polyurethane varnish
  Acrylic varnish
  Water-based paints
  Stains
  How do solvent-based finishes affect clean up?
  Which is better for the environment, water-based or solvent-based finishes?

## Slide 8
Polyurethane varnish
An extremely tough, hardwearing finish that is highly resistant to heat, water and chemicals
  A liquid plastic suspended in a water- or solvent-based carrier and sold as a matt, satin or gloss finish
  May be clear or tinted to highlight, enhance or alter natural wood tones
  Used on boats and wooden flooring
    What properties make this a suitable finish for the floor of a sports hall?

## Slide 9
Polyurethane pros and cons
Many polyurethane varnishes are not resistant to UV and will yellow over time
  It gives a lustrous finish but this can make woods look plastic or fake
  Water-based versions are better for the environment and safer to use
  More durable solvent-based versions have a longer drying time and pose greater health risks
    What PPE equipment should be worn when applying noxious finishes and why?

## Slide 10
Acrylic varnish
Acrylic varnish has a milky-white appearance but dries clear
  Compared to polyurethane, acrylic varnish has a faster drying time and doesn’t yellow with age
  Acrylic varnish is often used on top of paint finishes to add durability
  It’s hardwearing but less resistant to solvents and heat compared to polyurethane varnish
  Non-toxic and virtually odour-free
    How might the aesthetics of a painted surface be enhanced with a coat of varnish?

## Slide 11
Water-based paints
Used for applying opaque colour to wood
  Available in any colour imaginable and can be watered down to give a translucent look
  They have a low odour and low levels of volatile organic compounds (VOCs)
  Used for interior woodwork and furniture
  Hardwearing, quick drying, easy to use and clean up
  Many water-based paints are certified “Toy Safe”
  Use of a primer and an undercoat is usually recommended. What does this mean?

## Slide 12
Stains
These water based stains apply colour to paint while keeping the natural grain of the wood exposed
  They provide an aesthetic finish but offer no protection against decay and degradation
  Stains are available in bright colours as well as natural wood tones so softwoods mimic darker hardwoods

## Slide 13
Colour wash
Colour washes give an artistic, distressed look and accentuate details on a product
  Washes are applied to a painted surface, then roughly wiped away with a rag while still wet
  This removes most of the wash but leaves some of the finish behind to add texture and depth
  Colour washes add a certain aesthetic but do not preserve the wood in any way

## Slide 14
Wax finishes
Wax finishes are easy to apply and give a natural looking finish that nourishes and protects the wood
  Wax offers limited protection against moisture, heat or scratches and should be reapplied regularly
  Several coats are needed for the best results
  Wax is applied with a lint free cloth and left to sink in
  Residual wax is then buffed up to a shine
  Some waxes are food safe and non-toxic

## Slide 15
Oils
Used to replace natural oils lost over time and revive the natural beauty of the wood
  As oils seep into the wood, they offer little protection against scratches, heat or liquid
  In their raw form, oils are non-toxic and food safe finishing methods e.g. coconut oil, sunflower oil
  Oil-based finishes have been developed to enhance the performance of raw oils e.g. Danish and Teak oil
    Raw oils are often used on wooden kitchen utensils. What would you expect to happen to this finish over time?

## Slide 16
Danish oil
Danish oil is categorised as an oil but is actually a mix of oils and varnish
  The oil enhances the wood’s natural beauty and the varnish gives a water resistant, durable and satin finish
  Can be used as a primer on wood before applying paint or varnish
  Danish oil is food safe once it has fully cured
  Why is Danish oil commonly used on wooden toys?

## Slide 17
Teak oil
Teak oil isn’t made from teak but is ideal for use on dense hardwoods like teak
  Like Danish oil, it’s a blend of oils and varnish
  Suitable for indoor or outdoor applications and provides UV protection
  Used on boats and garden furniture
  Teak oil is not ideal if a high-sheen is required or in high-traffic areas
  Wood cannot be glued after teak oil has been applied. Why might this be the case?

## Slide 18
Worksheet 3
Complete Task 2 to consolidate your understanding of wood finishes

## Slide 19
Pressure treated timber
Pressure treated timber is treated prior to being sold using an antimicrobial copper-based preservative
  Used for high level protection where timber is exposed to constant weathering and possible insect/fungal attack
  Common uses include construction, landscaping, fencing and playgrounds
  A common pressure treatment is called tanalising
  Would pressure treated timber still be fully protected once it has been machined?

## Slide 20
Pressure treatment process
This treatment uses a pressurised treatment vessel to force preservative chemicals deep into the wood
  Watch the link video and complete Task 3
https://www.youtube.com/watch?v=8J0JlFpscFM

## Slide 21
Plenary
Complete Task 4 to match the products to an appropriate finish