## Slide 1
AQA
    A Level
      Product Design 7552
Stock forms and types of metals
Unit 4 Performance characteristics of metals
1

## Slide 2
Name the common stock forms of metals
Identify specific ferrous, non-ferrous and alloyed metals
Evaluate the properties and applications of a range of different metals
Objectives

## Slide 3
Starter
Test your existing knowledge of metals with the Starter on Worksheet 1

## Slide 4
Categories of Metals
Metals are classified into three main categories:
  Ferrous – contain iron, are magnetic and can rust
  Non-ferrous – do not contain iron, non magnetic, do not rust
  Alloys – a combination of two or more metals, or two or more elements, one of which must be a metal
  There are both ferrous alloys and non-ferrous alloys
  What are the advantages of combining different metals together?

## Slide 5
Metal is mined from the ground in the form of ore:
  Bauxite is aluminium ore and is extracted by electrolysis
  Iron ore is the second most common ore in the earth’s crust and uses heat and carbon for extraction
From ore to extraction

## Slide 6
Ferrous Metals
Carbon (C) is a common additive used to increase the hardness of iron
All ferrous metals contain iron (Fe)
You need to know about:
  Low carbon steel
  Medium carbon steel
  Cast iron

## Slide 7
Low Carbon Steel (0.05 - 0.25% carbon)
Low carbon steel is malleable, ductile and relatively inexpensive compared to other metals
  It has good tensile strength however this is lower than higher carbon steels
  Applications include nuts, bolts and automotive parts
  It is easy to weld
    Why is low carbon steel used in the manufacture of refrigerator panels?

## Slide 8
Medium Carbon Steel (0.29 - 0.54% carbon)
Medium carbon steel is less ductile than low carbon steel
  It is hard, malleable, tough with good tensile strength
  Applications include springs, gears, rail tracks and machine parts
    Which properties make medium carbon steel a suitable metal for gears?

## Slide 9
Grey cast Iron (2.5 – 4% carbon)
Grey cast iron distributes heat evenly and withstands even compression, resisting deformation
  It is very hard and has good resistance to oxidation
  However it is brittle and has low impact resistance
  Applications include radiators, cookware and stoves
    What might be a disadvantage of using grey cast iron in high quality cookware?

## Slide 10
White cast Iron (1.8 – 3.6% carbon)
White cast iron has excellent resistance to abrasion
  Like grey cast iron, it is also hard and brittle but has a greater tensile strength
  It can be cast with little shrinkage
  Applications include extrusion nozzles, dies, stone crushers and industrial rollers
    Why is white cast iron particularly suited to use in cement mixer drums?

## Slide 11
Non-ferrous metals
Non-ferrous metals do not contain iron
You need to know about:
  Aluminium
  Copper
  Silver
  Gold
  Titanium
  Tin

## Slide 12
Aluminium (Ai)
Aluminium is the most abundant metal in the earth’s crust
  It has an excellent strength to weight ratio
  It is soft, malleable and has a natural oxide layer which helps prevent corrosion
  Applications include window frames, phone casings, aeroplane parts and bicycles

## Slide 13
Copper (Cu)
Copper has been in use for around 10,000 years
  It is malleable and extremely ductile
  It is an excellent conductor of electricity and heat
  Applications include electrical wire, motors, hot water pipes and pans
    What heat treatment would you use when permanently joining copper components?

## Slide 14
Zinc (Zn)
Zinc is very versatile but rarely used on its own to make products – it is often alloyed
  As a metal, it is ductile and easily worked
  A layer of oxide gives it excellent corrosion resistance
  Applications include galvanising, roofing material and batteries
  Zinc is often used as a sacrificial anode on boats and ships to reduce corrosion
    Why is zinc galvanizing a suitable coating for industrial ducting?

## Slide 15
Silver (Ag)
Silver has been used in jewellery and coinage for millennia
  It is the best electric and thermal conductor
  It is extremely ductile
  Applications include electronics, mirrors and jewellery
    Due to its relatively high-cost, most ‘silver’ cutlery is not solid but is made from another metal and then ‘coated’ with silver
    What is this process called?

## Slide 16
Gold (Au)
Gold is one of the least reactive metals
  It is one of the most ductile and malleable metals
  It does not tarnish - it is impervious to air, water, alkalis and most acids
  Applications include jewellery, electronics, ornamentation and dentistry
    Which properties make gold a suitable metal for use in electronic products?

## Slide 17
Titanium (Ti)
Titanium was discovered in 1791 in Cornwall by William Gregor
  Titanium is a low density, durable metal with a high melting point
  It is highly resistant to corrosion and has an excellent strength to weight ratio
  Applications include implants, golf clubs, pacemakers, jewellery and aviation components
    What makes titanium ideal for use in hip and knee replacements?

## Slide 18
Tin (Sn)
Tin has been mined in Cornwall for over 4000 years
  It is soft and malleable
  It has good corrosion resistance
  Applications include ‘tin plate’ coating and solder for electronics

## Slide 19
Worksheet Task
Complete Task 1 of your Worksheet

## Slide 20
Ferrous Alloys
Ferrous alloys contain iron, carbon and one or more other element
You need to know about:
  Stainless steel
  Die steel
  High speed steel

## Slide 21
Stainless Steel
The most common type, stainless steel (SAE 304) contains iron, 0.08% carbon 18-20% chromium and 8-10% nickel
  It is very hard with good impact resistance
  It has very good corrosion resistance
  Applications include medical and catering equipment and construction
    What makes stainless steel an appropriate metal for food preparation equipment?

## Slide 22
Die Steel
Die steel contains iron and carbon alloyed with elements such as silicon, chromium and manganese, tungsten, vanadium or molybdenum
  It has good dimensional stability
  It is hard and has a natural oxide layer which helps prevent corrosion
  Applications include dies for die casting, wire drawing and tooling
    Why is resistance to wear an important property when making dies for casting?

## Slide 23
High Speed Steel (HSS)
High carbon steel is alloyed with one or more elements including molybdenum and cobalt
  A common variety is 18-4-1 HSS which contains 0.5-0.8% carbon, 18% tungsten, 4% chromium and 1% vanadium
  It is extremely hard and tough and holds an edge well
  HSS also withstands much higher temperatures than other carbon steels
  Applications include drill bits, tool blades, milling cutters and kitchen knives

## Slide 24
Non-ferrous alloys
Non-ferrous alloys do not contain iron
You need to know about:
  Bronze
  Brass
  Duralumin
  Pewter

## Slide 25
Brass
Brass contains around 65% copper and 35% zinc
  Brass has a low melting point (approx. 900°C)
  It is a low friction, self lubricating metal
  It is relatively corrosion resistant
  Brass is a good conductor of heat and electricity
  Applications include valves, taps, ornaments and musical instruments
    What makes brass suitable for use in a trumpet?

## Slide 26
Bronze
Bronze was used to make weapons and tools as far back as 3000BC.
  It contains around 90% copper and 10% tin
  Bronze forms an oxide layer and is resistant to corrosion
  Bronze is quite brittle
  Applications include statues, medals and coins
  ‘Bell metal’ is a bronze alloy which is 78% copper and 22% tin and is traditionally used for making bells

## Slide 27
Duralumin
Duralumin consists of 90% aluminium, 4% copper, and small amounts of magnesium and manganese
  It is ductile, malleable, can be hardened and has an excellent strength to weight ratio
  It oxidises to create a protective layer
  Applications include aircraft parts, surgical instruments, telescopic tent and walking poles, automotive and military engineering

## Slide 28
Pewter
Pewter contains around 95% tin and 5% copper and antimony which acts as a hardener
  It has a very low melting point of 170-230° Celsius
  It is soft and malleable
  Applications include flasks and tankards, decorative items and trophies
    Why is pewter often used in school based projects?

## Slide 29
Worksheet Task
Complete Task 2 of your Worksheet

## Slide 30
Stock Forms
Metals are available in a range of stock forms
  Sheet, plate, bar, tube and structural profiles
    Which factors might affect the selection of stock form metals?

## Slide 31
Sheet
Sheet metal is available in large panels up to 3mm thick
  It is ideal for pressing, punching, bending, spinning and riveting
  Applications include tin cans, car body parts, pots, pans, roofing and panels
    Why is sheet metal a suitable stock form for the manufacture of car body panels?

## Slide 32
Plate
Plate metal is available in thicknesses greater than 3mm but is usually narrower than sheet form
  It is ideal for plasma cutting, flame cutting and laser cutting
  Applications include construction and fabrication, architectural features and military machines

## Slide 33
Bar
Bar metal is available in flat, round, square, hexagonal and other forms
  Flat and square bar is more easily milled, drilled or welded or turned using a four jaw chuck
  Round and hexagonal sections can be more easily turned on a lathe
  Applications include tool making, gym equipment and construction
    The Allen keys pictured are made from hexagonal bar – how is the bar manufactured?

## Slide 34
Tube
Metal tube is available in the same stock forms as bar
  Rectangular tube is more commonly called ‘box section’
  Tubular stock forms are structurally strong
  Applications include bike frames, heating and plumbing, musical instruments and some medical applications
  What are the advantages of using tubular metal forms over solid bar?
  What difference will the wall thickness make to a tube?

## Slide 35
Structural beams and joists
Structural metal is available in different profiles including I beam, H beam, L beam, T bar & channel
  I beams spread vertical loading whilst reducing material/weight
  An L beam or ‘angle’ is the ideal shape for easy connections in construction but it is not as strong as tube
  Applications include construction, bridges and skyscrapers
  RSJ is the term given for rolled steel joists used in construction

## Slide 36
Profile and pipe stock forms

## Slide 37
Bar and tube stock forms

## Slide 38
Plenary
Complete Task 3 of the Worksheet