## Slide 1
AQA
    A Level
Performance characteristics of metals
Unit 4 Performance characteristics of metals
2
      Product Design 7552

## Slide 2
Be able to identify different physical and mechanical properties for a range of metals
Describe the different performance characteristics for a range of metals
Explain how the different properties of metals affect their selection for a range of applications
Objectives

## Slide 3
Starter
Identify which metal types and forms may have been used in this children’s playground
State which material properties and characteristics you think would be required in each case

## Slide 4
Atomic structure of metals
Atoms in metals exist in a regular lattice structure
  Metal crystals are made up of positive metal ions surrounded by a sea of ​free-moving negative electrons
  This structure means metals are good ​electrical conductors
  The strong electrostatic attraction between ions and electrons creates a tight bond
    Why do most metals have high melting points?
https://www.youtube.com/watch?v=YsmzuDzOsXg

## Slide 5
Mechanical properties
Mechanical properties are the characteristics a material displays when subject to an external force
You need to know about:
  Hardness
  Toughness
  Malleability
  Elasticity
  Tensile strength

## Slide 6
Hardness
The hardness of metals determines how well they withstand wear and abrasion
  Tightly packed atoms form a strong metallic bond
  Alloys are usually harder than pure metals
  Alloys have different sized atoms which mean they are less able to slide over one another making the metal harder
    Which are the hardest metals?

## Slide 7
Toughness
The toughness of metals determines their ability to absorb energy without cracking
  A tough metal will be both malleable and ductile
  On impact, atoms in tough metals move past each other allowing the metal to deform instead of breaking
  ‘Superalloys’ like C300 Maraging steel have been developed to have above average levels of toughness
    Why is mild steel still used in the manufacture of car bonnets?

## Slide 8
Malleability and Ductility
Both properties refer to a metal’s ability to withstand plastic deformation and retain its new shape
  Malleable metals can be bent, pressed and manipulated without fracturing
  Ductile metals can be drawn or stretched without breaking
  Metal atoms move over each other to allow deformation
    Which metals are most malleable?
    Which metals are most ductile?
    In what applications is ductility vital?

## Slide 9
Elasticity
Elasticity is a material’s resistance to distortion and ability to return to its original shape
  Steel is said to be more elastic than rubber because it requires a greater deforming force
  Nitinol (nickel titanium) is known as a super-elastic alloy
    What makes nitinol a suitable material for use in surgical implants and dental braces?
https://www.youtube.com/watch?v=cArEU2hLSFU

## Slide 10
Material strength
The strength of metals can be measured in different ways
You should know about:
  Compressive strength
  Tensile strength
  Bending strength
  Torsional strength
  Shear strength
    Why does a bridge need good torsional strength?

## Slide 11
Tensile Strength
Tensile strength is the ability of a metal to withstand pulling forces
  Tensile strength is the point at which a material goes from elastic to plastic deformation
  It is the limit of tensile stress before either ductile failure or brittle failure
    What is the difference between ductile and brittle tensile failure?
https://www.youtube.com/watch?v=8ZYUBmmtQlI

## Slide 12
Worksheet Task
Complete Task 1 of Worksheet 1

## Slide 13
Physical properties
Physical properties are the measurable characteristics a material displays
You need to know about:
  Density
  Melting points
  Thermal conductivity
  Electrical conductivity
  Resistance to corrosion
  Ability to take applied coatings and finishes
  Ability to be alloyed and joined with heat processes

## Slide 14
Density
Most metals have a high density as the atomic lattice structure is closely packed together
  Platinum and tungsten have very high densities
  The name ‘tungsten’ is derived from the Swedish for ‘heavy stone’
  What applications might a high density metal be used for?
  Aluminum and titanium have relatively low densities
  Where would this be advantageous?

## Slide 15
Thermal conductivity
Thermal conductivity varies across different types of metals and alloys
  Copper is particularly good at conducting heat
  Comparatively, steel is a poorer conductor of heat making it more suitable for high temperature environments
    List three different applications of copper where thermal conductivity is important

## Slide 16
Melting points
Most metals have high melting points
  Tungsten has the highest melting point of all metals at 3422°C
  Tungsten is used in light bulb filaments and other high temperature applications
  Mercury, tin and lead have much lower melting points
    The melting point of mercury is -38.83°C
    What form will mercury take at room temperature?

## Slide 17
Electrical conductivity
Electrical conductivity varies across different metals
  Silver has the best electrical conductivity of all metals
  Copper also has good conductivity and is far less expensive
  Gold has better corrosion resistance
    Why would these factors be important in electronic applications?

## Slide 18
Metals have variable resistance to damage caused by oxidisation or other chemical reactions
  Some metals are very unreactive and do not corrode easily
  We still find silver, gold and bronze coins that are thousands of years old
  How does this prove these metals have good corrosion resistance?
  What other applications of bronze take advantage of this property?
  Nowadays alloying or applied finishes can protect metals that corrode easily
Resistance to corrosion

## Slide 19
Worksheet Task
Complete Task 2 of your Worksheet

## Slide 20
Ability to be joined with heat
Metals ability to be joined with heat relies on the melting point of the metal and its conductivity
  Soldering, brazing and welding are heat processes used to join metals together
  Copper, brass and silver solder easily
  Mild steel requires greater heat and may be brazed or welded
  Why are stainless steel and aluminium more difficult to join together using heat?

## Slide 21
Ability to take finishes
Some metals require coatings and finishes in order to improve durability and aesthetics
  Steel requires a finish otherwise it will rust
  Anodising is used to increase the aluminium oxide layer to prevent corrosion
  Stainless steel does not require a finish
  The inclusion of which element gives stainless steel its protective surface layer?
  Which other metals do not require a finish to be applied?

## Slide 22
Worksheet Task
Complete Task 3 of your Worksheet

## Slide 23
Defects in metals
Metals can have various defects where there are imperfections in the arrangement of the atoms
These imperfections can result from:
  Deformation, rapid cooling, radiation or impact
  Imperfections could be focused at one point, in a line, across a plane or as a 3D bulk e.g. cluster of impurities or a hole
  Dislocations are line defects where the atoms of the crystal lattice are misaligned

## Slide 24
Plenary
Watch the Link video - then identify and justify the mechanical and physical properties of the different metals parts of Arup’s Millennium Bridge
https://www.youtube.com/watch?v=gQK21572oSU