## Slide 1
AQA
    A Level
      Product Design 7552
Testing and treatment of metals
Unit 4 Performance characteristics of metals
3

## Slide 2
Identify different workshop and industrial tests that are carried out on metals
Describe how tests are set-up, what is tested, measured and compared
Explain how the heat treatment of metals enhances their properties
Objectives

## Slide 3
Starter
Identify the working properties required for the metal components of this fairground ride
How could you test for these properties?

## Slide 4
Testing metals
You need to know how to test the following working properties of metals:
  Tensile strength
  Toughness
  Hardness
  Malleability
  Corrosion
  Conductivity

## Slide 5
Tensile strength tests
Testing for tensile strength can be done in the workshop and on an industrial level
  In the workshop, clamp samples to the end of bench, apply a load and measure the amount of deflection
  In industry tensile strength is tested with a tensometer
  This determines the pulling forces the metal can resist
  Give an example where testing the tensile strength of metals is vital
https://www.youtube.com/watch?v=D8U4G5kcpcM

## Slide 6
Toughness testing
Testing for toughness in metals uses a moving load to hit a metal sample with force
  In industry the Izod impact test is used
  A pivoted arm is raised to a set height and then released
  The arm swings and hits a notched sample, breaking it
  The amount of swing after breaking indicates the amount of energy absorbed
    Would the arm swing lower or higher if a metal with poor toughness was tested?

## Slide 7
Hardness testing
There are three main tests for hardness in industry: Rockwell, Brinell and Vickers
  The Rockwell test uses a diamond indenter to break the surface, additional load is applied then released
  The Brinell test uses a steel ball to indent the surface
  The Vickers pyramid test uses a diamond square based pyramid to indent the surface
  In each case, the depth of the indentation or diameter of the mark made is measured

## Slide 8
Malleability testing
Testing the malleability of metals uses a bend test
  Metal samples are placed into a bend test machine and bent in one continuous bend
  Once the sample is bent, the amount of cracking or fracturing is measured
  The fewer cracks on the inside of the bend, the more malleable the metal
    What other property would the cracks on the outside of the bend indicate?
https://www.youtube.com/watch?v=s5MUL_Q3bkM

## Slide 9
Corrosion testing
Different environments are used in industrial tests for corrosion resistance in metals
  Salt spray testing which accelerates corrosive attack is used to test finishes on metals as well as self-finishing alloys
  Humidity testing is particularly important for metals used in bridges and construction works
    How could you test for corrosion resistance in a workshop?

## Slide 10
Electrical conductivity testing
Understanding the electrical conductivity of metals is extremely useful in the electronics industry
  In the workshop a multimeter can be used to measure resistance
  The lower the resistance the better the conductivity
  In industry, a four-point probe test is used; outer leads measure current and the inner leads measure voltage drop, giving an accurate result

## Slide 11
Thermal conductivity testing
In industry, a heat flow meter enables accurate testing with temperature control and flow sensors
  In the workshop, metal samples can be tested by timing how long it takes heat to move down a metal sample
  The longer it takes, the lower the thermal conductivity
  How could this test be set up to ensure consistent results?
https://www.youtube.com/watch?v=SNG_5lPe2a8

## Slide 12
Non-destructive testing
A range of tests can be carried out on existing metal products without causing damage
  Visual inspections
  X-rays
  Ultrasonic tests
  Liquid penetration tests
    Why are ultrasonic tests carried out on commercial pipe networks?

## Slide 13
Worksheet Task
Complete Task 1 of Worksheet 1

## Slide 14
Changing the structure
Atoms in a metal exist in a regular lattice structure
  However, when the metal is cold worked, faults known as dislocations are formed within the structure causing it to harden and eventually fracture
  If you bend a paperclip back and forth repeatedly, what happens?

## Slide 15
Cold working
Metal is worked by hammering, bending and rolling
  Stresses are introduced into the metal and it becomes work hardened
  Heat treatment can be used to restore the original properties of the work hardened metal
  Two treatments can be used annealing and normalising

## Slide 16
Heat treatment
You need to understand the application of the following heat treatments of metals:
  Annealing
  Hardening
  Tempering
  Case hardening

## Slide 17
Annealing
Annealing is the application of heat to relieve internal stresses making the metal more malleable and easier to work
  Ferrous metals are heated to a cherry red (725°C) and allowed to cool slowly
  Aluminium is heated to 350-400°C and air cooled
  Copper and brass are heated to dull red and allowed to air cool or are quenched

## Slide 18
Hardening
Steel is hardened by heating it to a red heat and quenching (cooling) it in water or oil
  The degree of hardness depends on the carbon content of the steel (min 0.4%)
  A steel that is too brittle is tempered to make it tougher
    Why would a manufacturer harden steel blades like kitchen knives or scissors?

## Slide 19
Tempering
Tempering is used to reduce brittleness and increase toughness after metal has been hardened
  Medium or high carbon steel is heated to a critical temperature depending on its intended application
  The temperature may be judged by the colour of the oxide layer
  Once the desired toughness is reached the piece is air cooled
    How does the colour change as the temperature increases?

## Slide 20
Tempering colours

## Slide 21
Case hardening
Case hardening is used to harden the outer layer of steel while maintaining a ‘soft’ core
  This technique is used for steels with a lower carbon content
  A steel part is ‘carburised’, dipped in carbon powder and heated
  After heating, the part is quenched
    What processing factor would affect the thickness of the carbon layer?
    Why is this an appropriate heat treatment for gears?

## Slide 22
Normalising
Normalising is a form of annealing for ferrous metals which has a faster cooling time
  Normalising removes internal stresses and improves overall strength, hardness and structure, avoiding too much softening
  It involves heating to between 700-900°C and holding or ‘soaking’ it at this temperature before air or gas cooling

## Slide 23
Worksheet Task
Complete Task 2 and 3 of your Worksheet

## Slide 24
Plenary
Discuss in pairs which workshop tests you would use on the metal components for use in a child’s scooter