## Slide 1
AQA
    A Level
      Product Design 7552
Forming metals
Unit 9 Processing and working with metals
1

## Slide 2
Name the different ways metals can be shaped into 3D products
Describe different forming methods
Explain the suitability of different forming methods for a range of specific products and scales of production
Objectives

## Slide 3
Starter
Identify how the main body of the following items has been formed

## Slide 4
Metal forming processes
You need to know about the following metal processes:
  Press forming and spinning
  Cupping and deep drawing
  Forging and drop forging
  Bending and rolling
  Casting, including sand, die, investment and low temperature

## Slide 5
Press forming
Press forming shapes sheet metal into 3D forms
  Metals such as low carbon steel and aluminium are often used
  Common in mass production or large scale batch production due to the cost of producing the dies
  Dies are made from hardened steel, spark eroded and hand burnished to give a high quality surface finish
  What are the advantages of press forming a stainless steel kitchen sink?
https://www.youtube.com/watch?time_continue=1&v=5CuJjSk4U38

## Slide 6
Spinning
Spinning is a way of forming sheet metal giving radial symmetry
  Objects such as kettles and saucepans are made this way
  Spun products can be identified by parallel lines on the surface
  Typically used in mass and batch production and often completed using CNC lathes
  What are the advantages of spinning metals?
https://www.youtube.com/watch?v=43N44ICyuEU

## Slide 7
Cupping and deep drawing
Cupping and deep drawing are used to form tube like shapes from sheet metal
  Objects such as fire extinguishers and aerosol cans are made this way
  Deep drawing is when the depth of pressing exceeds the diameter
  Corners of the punch are rounded so the metal stretches instead of shearing
  High set-up costs of the hydraulic press and dies mean it is best suited to mass or continuous production
https://www.youtube.com/watch?v=r6U6P0Y0bRw

## Slide 8
Worksheet 1
Complete Task 1 of your Worksheet

## Slide 9
Drop forging
Drop forging is used to shape hot metal
  This process is used when the product needs to be tough and hard
  Objects such as spanners, pliers and screwdriver shafts are made this way
  Hot metals is forced into shape under great pressure therefore retaining the original grain structure
  The process is suitable for mass production, however dies can be changed quickly to allow for varied production

## Slide 10
Wrought iron forging
Wrought iron has a very low carbon content making it malleable and easy to shape
  In addition to hydraulic and mechanically powered rams, it can be shaped using hand tools such as hammers and an anvil

## Slide 11
Perfect scrolls
Wrought iron is heated in a forge then shaped
  Scroll formers and twisting bars help make intricate shapes
  Suitable for one off, or limited batch production
  What kind of items might be made this way?

## Slide 12
Bending
A press brake is used for bending sheet or plate metal
  The stock material is clamped between a punch and die
  A brake holds the metal and lowers the punch to bend the metal into shape
  Which products are made using bending methods?
https://www.youtube.com/watch?v=jW9ksLb94vo

## Slide 13
Rolling
Rolling is used to reduce the thickness of metals
  Typically used to make structural steels such as I beams, angle, bar and channel for the construction industry
  Rolling is usually carried out with hot metal that has been heated above recrystallisation temperature
  Hot rolling can result in surface carbon deposits but has no deformation or stresses
  Metal can be cold rolled which gives a fine tolerance
https://www.youtube.com/watch?v=6xnKmt_gsLs

## Slide 14
Die casting
Die casting is used with lower melting point metals such as aluminium, pewter and zinc
  Tool steel is used for the reusable dies
  The complexity and cost of making the dies makes it most suitable for mass production
  Die casting produces a high quality finish
  Die cast items include alloy wheels, metal toys, engine components and ironmongery products
  What are the advantages of die casting?
https://www.youtube.com/watch?v=IZvP6Jj3HvY
https://www.youtube.com/watch?v=iSyBsdJkQu8

## Slide 15
Die casting process
There are two types, gravity die casting and high pressure die casting, shown below
  Molten metal is fed into the die where it cools
  Ejector pins ensure the casting releases from the die

## Slide 16
Sand casting
Sand casting is used to form high melting point metals
  Carried out in foundries, using moulds made using special ‘green’ sand
  It is a slow and labour intensive process and moulds are single use only
  Used for products such as engine blocks, post boxes and train wheels
  Used for one-off or batch produced items
  Why does sand casting not give a very high quality finish?

## Slide 17
Sand casting process
A pattern is used to make the mould – a split, two-part pattern is often used
  Complex solid and hollow parts can be cast but need to be carefully finished after casting
https://www.youtube.com/watch?v=szOwGvYO_Tc

## Slide 18
Worksheet Task
Complete Task 2 of your worksheet

## Slide 19
Investment casting
Investment casting is used to cast items with awkward shapes that would be difficult to mould using any other casting process
  A wide range of metals are suitable including; brass, stainless steel and carbon steels
  It produces high quality products with an excellent finish
  Repeatability is achieved as wax patterns are cast from a master mould

## Slide 20
Pewter casting
Pewter has a low melting point and is often used in school-based casting projects
  It is ideal for making jewellery and decorative components
  It is suitable for one-off production however moulds can be made from many other metals making it good for higher volume production
  What is the melting temperature range for pewter?

## Slide 21
Plenary
Complete Task 3 of your Worksheet