## Slide 1
AQA
    A Level
      Product Design 7552
Joining metals
Unit 9 Processing and working with metals
2

## Slide 2
Name different permanent and temporary joining methods for metals
Be able to describe different joining methods and when to use them
Explain the suitability of joining methods for a range of specific applications and scales of production
Objectives

## Slide 3
Starter
In pairs discuss which joining methods would have been used to create the London Eye

## Slide 4
Metal joining methods
You need to know about the following permanent joining methods:
  Riveting
  Brazing
  Hard and soft soldering
  Oxy-acetylene and spot welding
  MIG (metal inert gas) welding
  TIG (Tungsten inert gas) welding
What health and safety precautions are required when using heat to join metals??

## Slide 5
MIG welding
MIG (Metal Inert Gas) welding is used to weld thin gauge metal such as aluminium and some steels
  Heat is generated by an electric arc in a localised area – if done well it will not burn through or distort the metal
  The workpiece is clamped to the negative connection – the positive connection is called the electrode
  Uses include climbing frames, bike frames and vehicle exhausts
  It can be used for one-off production and is common on production lines

## Slide 6
How MIG welding works
MIG welding uses a filler wire as an electrode
  The wire electrode melts in the arc and fills the gap between the two metals
  The welding torch is gently swirled to form a bead of weld
  The electrode wire is stored on a reel and is fed through the nozzle as the trigger is pressed
  Inert gas shields the area being joined to prevent oxidisation in the weld
https://www.youtube.com/watch?v=twUAa5LWUvk

## Slide 7
TIG welding
TIG (tungsten inert gas) welding is used to weld stainless steel, aluminium and copper alloys
  It is an electric arc welding process, however unlike MIG welding, the electrode made from tungsten does not melt in the process, a filler material is added separately
  It uses a gas shield of argon or helium
  The TIG process gives the operator greater control allowing for more accurate and stronger welds
  Why might TIG welding be used on aluminium ladders?
https://www.youtube.com/watch?v=uO5pVLOAmD4

## Slide 8
Spot welding
Spot welding welds sheet metal together without a filler material
  Heat and pressure are applied to the area to be welded
  Contacting metal surfaces are joined by heat generated from resistance to an electric current
  Workpieces are held together under pressure exerted by electrodes
    Name any advantages and disadvantages of spot welding
https://www.youtube.com/watch?v=Xu1pYrXuJfo

## Slide 9
Oxy-acetylene welding
Oxy-acetylene is used to weld low carbon steel sheet, tube or plate
  It mixes two, high pressure gases (oxygen and acetylene) forming a very hot and intense flame (up to 3,500ºC)
  The flame is adjusted by changing the gas and oxygen mixture enabling flame cutting, welding or brazing
  Why might this method of welding be useful in remote areas?
https://www.youtube.com/watch?v=VfRQxxxLJuo

## Slide 10
Soft soldering
Soft soldering uses low melting point metals (solder) to join other metals together
  Solder is traditionally a tin/lead alloy with a low melting point (320ºC) used to join the parent metals
  New solder variants are lead-free and are RoHS compliant - Restriction of Hazardous Substances Directive
  Soft soldering is used in plumbing and electronics and where damage may be caused by higher temperatures
  Name two different heat sources which could be used for soft soldering

## Slide 11
Hard soldering (apx 590ºC to 870ºC)
Hard soldering uses a higher temperature than soft soldering
  It is used to join precious metals like gold and silver
  It requires the parent metal to be clean and have no gaps between areas being joined
  Flux must be applied to prevent the metal oxidising which enables the solder to flow
  Why might silversmiths use many different melting point solders in one workpiece?

## Slide 12
Brazing
Brazing uses either an oxy-acetylene flame or a gas and compressed air brazing hearth
  It needs a lower temperature than welding as the brazing rod melts at around 850°C, so the joint is not as strong
  It can be used to join many dissimilar metals
  How could it be argued that brazing is a more sustainable method of joining metals than welding?
https://www.youtube.com/watch?v=-oifC7fbQfY

## Slide 13
Riveting
Riveting is semi-permanent joining method used to join sheet or plate metal
  Rivets are metal fasteners that have a head at one end and a shaft or tail the other end
  Best suited to industrial applications as an alternative to threaded fastenings
  Why do high strength bolts often replace rivets in construction?

## Slide 14
Cold-formed rivets
Cold-formed rivets require access to both sides of the sheet material
  They are installed with a ‘set’ and ‘snap’ which domes the ends while pressure is applied
  Why might riveting be used to join metal instead of welding?
  Why are rivets classed as semi-permanent, not permanent?
Snap
Rivet
Set

## Slide 15
Pop riveting
Pop rivets are quicker and easier to use but are not as strong
  They require the use of a pop rivet gun
  They are ideal where the underside of the joint is inaccessible
  A form of pop rivets is used in aircraft production to join sheet aluminium to structural parts
  Which everyday products might use pop rivets?
https://www.youtube.com/watch?v=9aoXmzdSf_I

## Slide 16
Pop rivets
Pop rivets are used to create a semi-permanent fixing between two thin sections of metal
  The pop rivet gun is used to apply pressure to the rivet by pulling the shank until it breaks
  This action splays the inserted end to create the bond

## Slide 17
Worksheet 2
Complete Task 1 of your Worksheet

## Slide 18
Metal joining methods
You need to know about the following temporary joining methods:
  Self tapping screws
  Machine screws
  Nuts & bolts

## Slide 19
Self-tapping screws
Self-tapping screws cut their own thread as they are screwed into sheet metal and some plastics
  They are used in panel products which require maintenance, such as computer panels, washing machines and dryers
  Although some self-tapping can create their own hole, a pilot hole is advised for a precise and accurate result

## Slide 20
Machine screws
Machine screws are a type of bolt with a fine thread
  They are used on motor and gear housings and in many electronic product casings
  Different types of machine screw include cheese head, round head, countersunk, hex head bolt and socket head
  They are identified by their length, diameter, head profile and thread pitch

## Slide 21
Nuts & bolts
Nuts and bolts are similar to machine screws
  Rather than screwing into the material they are passed all the way through, then a nut is tightened at the other end
  Some types of nut, like castle and nyloc nuts are designed not to work loose
  Other types, like wing nuts are designed to be loosened regularly
  Why are washers often used with nuts and bolts?

## Slide 22
Plenary
Complete Tasks 2 and 3 on your Worksheet