## Slide 1
AQA
    A Level
      Product Design 7552
Wasting metals
Unit 9 Processing and working with metals
3

## Slide 2
Know different metal wasting processes
Describe different wasting processes used for different materials
Explain the suitability of different wasting processes for a range of specific components and products
Objectives

## Slide 3
Starter
Pictured below is a constant velocity joint from the drive shaft of a car
  Discuss how its components were made and suggest potential materials used

## Slide 4
Wasting processes
You need to know about these metal wasting processes:
  Milling
  Turning
  Flame cutting
  Plasma cutting
  Laser cutting
  Punching & stamping

## Slide 5
Wasting processes
Wasting processes involve the removal of material by cutting
  They produce waste or unusable material as a by-product of the wasting process
  Are there any metal manufacturing processes that produce no waste?

## Slide 6
Milling machines
Milling machines traditionally cut vertically or horizontally but some advanced mills can now cut on many axes
    What different types of milling cutters are there and what are their uses?
    Name any metal parts of products in the workshop that have been milled
https://www.youtube.com/watch?v=ckzK-LbeZmY

## Slide 7
Complex milling
Milling is used to create highly accurate machine parts
  The workpiece and the rotary cutting tools move through x, y and z axes
  Complex geometry can be created using a 4th and 5th axis
  Milling can be done manually and with CNC machining
  When might companies choose to use milling over casting?

## Slide 8
3D Milling
Some mills use multi-tooled cutters to waste the workpiece
  Mills can be used to create holes, chamfers, slots, joints and large flat surfaces
  Slots can be machined using special cutters with accurate profiles
  Milling is suitable for one-off intricate components as well as being set up to run repeatedly as part of mass or batch production runs

## Slide 9
Turning
A centre lathe or engineer’s lathe is used to turn metal
  The workpiece is held with a three or four jaw chuck in the headstock whilst the cutting tool moves in two axes
  A chuck can also be fitted to the tail stock for centring or drilling
  Longer work pieces are often centred using the tail stock – What benefit does this have?
  For which shaped billets are three and four jaw chucks used?
https://www.youtube.com/watch?v=8EsAxOnzEms

## Slide 10
Lathe components
It is worth knowing the main components of a lathe
  Centre lathes use single point cutting tools usually made from HSS or silicon carbide
  Manual turning can produce bespoke and one off items
  CNC lathes can be used as part of a batch or mass production line
  What factors determine the speed of the lathe?
  What products are commonly produced by turning?

## Slide 11
CNC Turning
CNC lathes use multi-tool heads which change tools automatically for a given task
  CAD programs allow complex and accurate shapes to be repeated quickly and efficiently

## Slide 12
Lathe turning techniques
Many processes are completed on a lathe including:

## Slide 13
Worksheet 3
Complete Task 1 of your Worksheet

## Slide 14
Flame cutting
Flame cutting uses oxyacetylene gas and a flame cutting torch to focus a flame up to 3,500°C
  Oxygen intensifies the flame and forces the molten metal out
  Used to cut low carbon and alloy steel plate
  Why is flame cutting relatively inaccurate?
  What makes it ideal for use in remote areas?
https://www.youtube.com/watch?time_continue=1&v=7EGmrPiumEU

## Slide 15
Plasma cutting
Plasma is an ionised gas which is electrically conductive at very high temperatures
  Plasma cutting generates a faster, cleaner cut than flame cutting
  The heat generated can be as high as 28,000°C
  It is suitable for one off and batch production
  Applications include cutting steel plate for sculptural signs and bespoke gates

## Slide 16
Plasma cutting process
Plasma cutting can be done manually or with CNC machinery
  An electric arc is sent through plasma cutting gas and out a constricted opening
  It can cut steel, aluminium, stainless steel, brass and copper up to 150mm thick
  What are the advantages of using a manual plasma cutter over a CNC plasma cutter?
https://www.youtube.com/watch?v=W46BKlQvHws

## Slide 17
Metal laser cutters
A high powered laser beam is directed through optics at the workpiece on the laser bed
  The beam focus, speed and power are adjusted to create the correct cut for the material
  The laser melts the metal and compressed air or gas blows the molten metal clear
  The fine laser beam allows for a high level of accuracy and a fine finish is possible
https://www.youtube.com/watch?v=5JhA9JyGBBI

## Slide 18
Laser cutting
Laser cutters are used on sheet metal
  They cannot cut metal plate as thick as flame and plasma cutters can
  They are fast, have repetitive accuracy and produce a much higher quality finish than plasma or flame cutting
  It has a very high energy consumption
  Laser cutters are suitable for one off to large batch production runs

## Slide 19
Punching and stamping
Stamping pierces a metal sheet to cut out a shape or slot
  The scrap cut-outs are then recycled
Blanking creates cut out parts for further processing and recycles the original punched sheet

## Slide 20
Punching and stamping parts
CNC machinery can stamp out sections of sheet metal up to 6mm thick
  The upper tool is the punch and lower is the die
  The punched ‘slug’ drops through the hole in the die
  Applications include dishwashers, washing machines and computer casings
https://www.youtube.com/watch?v=HBa1wDv-6bU

## Slide 21
Worksheet Task
Complete Task 2 and 3 of your Worksheet

## Slide 22
Plenary
Design an Olympic torch casing that uses at least two wasting processes