## Slide 1
AQA
    A Level
      Product Design 7552
Finishing metals
Unit 9 Processing and working with metals
4

## Slide 2
Name the different ways metals can be finished to enhance appearance or prevent corrosion
Be able to identify specific applied finishes
Evaluate the properties and applications of a range of different finishes for metals
Objectives

## Slide 3
Starter
Name different ways of protecting a steel ship from corrosion

## Slide 4
Metal finishes
The two main reasons finishes are applied to metals are to enhance appearance and prevent corrosion
  Ferrous metals rust over time
  Some non-ferrous metals and alloys do not form a strong oxide layer to protect them from corrosion
  What would happen to an unfinished low carbon steel bench over time?

## Slide 5
Metal finishes
You need to know about the following metal finishes:
  Cellulose and acrylic paint
  Electroplating and galvanising
  Sealants and preservatives
  Anodising, plating, coating and powder coating
  Cathodic protection

## Slide 6
Cellulose or acrylic
Paints provide both colour and a barrier against corrosion
  The workpiece must be prepared and degreased and a key is provided for the paint to grip to
  Car bodies are often finished with cellulose paint which dries much faster due to the solvent
  Cellulose paints contain VOCs
  Usually more coats are needed with cellulose than acrylic paint to achieve a high quality finish

## Slide 7
Acrylic Paint
Acrylic paints are water-based, durable and hard wearing
  They usually require heat, professional equipment and up to 24 hours to cure
  Applications include bicycles, DIY projects, roofing sheets and window frames
  Paints can be applied with a brush, roller and various spraying methods

## Slide 8
Electroplating
Electroplating uses a desired metal to coat a (usually) cheaper base metal
  This provides a protective layer with increased aesthetic appeal
  The negative electrode is the object to be plated
  The positive electrode is the coating metal
  The electrolyte solution is a solution of the coating metal
  Which everyday items are electroplated?
https://www.youtube.com/watch?v=OxhCU_jBiOA

## Slide 9
Galvanizing
Galvanizing coats iron or steel with zinc to form a protective layer
  Zinc carbonate forms when zinc is exposed to air and water, this layer is extremely resistant to corrosion and very tough
  There are two methods to galvanise: electroplating and hot dipping
  Name some products that are commonly galvanized for protection against corrosion
https://www.youtube.com/watch?v=yQUD2vzfgh8

## Slide 10
Zinc hot dipping method
The workpiece being coated is cleaned using a four stage process to ensure a good bond is made
  The workpiece is dipped into a molten zinc bath at 830-850ºC
  It is then cooled, cleaned up and inspected to ensure even coverage and appropriate thickness of zinc
  This method is better for larger pieces and gives a thicker overall coverage than electroplating

## Slide 11
Worksheet task
Complete Task 1 of Worksheet 4

## Slide 12
Sealants
Sealants blocks the passage of air or fluids through metal joints
  Sealants used on metals are usually polymer based and act as a gasket, often used in machinery
  Sealants help prevent decay, weathering and corrosion
  Where might sealants be used in car manufacturing?

## Slide 13
Preservatives
Preservatives can provide temporary or long term protection for metal surfaces
  They are often used in moulds and dies to prevent atmospheric corrosion or condensation build up
  Mainly oil-based they can be applied through bonding electrostatically, spraying, immersion or simply with a cloth
  Applications include use on machine beds to provide a smooth frictionless surface
  Some other types of preservatives are used to stabilise rust

## Slide 14
Anodising
Anodising is mainly used on aluminium to provide a hard wearing corrosion resistant surface
  The aluminium workpiece is immersed into an acid electrolyte bath and electric current is passed through
  The cathode is inside the tank and the aluminium part (job) acts as the anode
  Magnesium and titanium can also be anodised
https://www.youtube.com/watch?v=UKdm_hJdpQI

## Slide 15
Anodisation process
Anodising is an electrochemical process
  Oxygen ions released from the electrolyte combine with aluminium atoms on the surface increasing the aluminium oxide layer, thickening and protecting the surface
  The benefits include colouration, increased resistance to wear, improved lubrication and increased electrical insulation

## Slide 16
Plating and metal coatings
Plating increase wear resistance and lubricity, it can also offer a thermal barrier or improved conductivity
  Plating can be done using physical vapour deposition (PVD) or through the use of heat and pressure to fuse metals together
  Applications include thin film solar panels, jewellery, surgical implants and titanium nitride coated cutting tools
https://www.youtube.com/watch?v=CH3IsHP7llM

## Slide 17
Worksheet Task
Complete Task 2 of your Worksheet

## Slide 18
Polymer coating
Dip coating provides a thick, wear resistant, water resistant and air tight finish
  Using polymer dip coating, the metal to be covered is heated to 230°C
  It is then dipped into a tank of fluidised polymer powder as warm air blows around it
  The heat from the metal melts and bonds the polymer onto its surface
  It is then cooled to solidify the polymer
  Why is this common on electrical and gardening tools?

## Slide 19
Powder Coating
Powder coating provides an even coating, more hardwearing than paint
  The workpiece is statically charged and powdered paint is sprayed through an air gun
  The charge creates a strong attraction between powder and the workpiece
  The workpiece is then baked in an oven where the powder coating melts and bonds to the metal
https://youtu.be/IFeMX1O6Epk

## Slide 20
Cathodic protection
Sacrificial anodes are used to control the corrosion of a metal surface
  The process makes the metal to be protected the cathode of an electrochemical cell
  An easily corroded sacrificial metal (the anode) is bonded to the surface which corrodes instead of the metal
  Applications include fuel pipelines, boat hulls and oil rig foundations

## Slide 21
Worksheet Task
Complete Task 3 of your Worksheet

## Slide 22
Plenary
Discuss different protective and aesthetic finishes that could be used for the metal body of a torch